ISaGRAF

Version 3.4

Workbench / Kernel

Interface Reference

CJ INTERNATIONAL

| Publisher | CJ International 3, Rue Hector Berlioz 38600 FONTAINE FRANCE Phone: (0033) (0)4 76 26 87 30 Fax: (0033) (0)4 76 26 87 39 http://www.isagraf.com Printed and bound in France. |
| --- | --- |
| Copyright | Copyright © 2000 by CJ International All rights reserved. Specifications subject to change without notice. No part of the contents of this book may be reproduced or transmitted in any form or by any means without the written permission of the publisher. ISaGRAF is a registered trademark of CJ International. All other product and company names mentioned are trademarks or registered trademarks of their respective owners. |

CONTENTS

A.	Introduction	7

B.	ISaGRAF overview	8

B. 1.	ISaGRAF architecture	8

B. 2.	Application Generation	9

C.	Workbench/Kernel Interface	11

C. 1.	Interface description	11

C. 1. 1.	Application Database	11

C. 1. 2.	ISaGRAF Communication protocol	13

C. 1. 3.	C file generation	14

D.	Appendix 1 : Database description	15

D. 1.	Database description	15

D. 1. 1.	Specification of the description	15

D. 1. 2.	Table addresses	16

E.	Appendix 2 : TIC code definition	62

E. 1.	Introduction	62

E. 2.	Notations in the instructions	62

E. 2. 1.	Data type	62

E. 2. 2.	TIC code significance	62

E. 2. 3.	Symbols	63

E. 2. 4.	Intel or Motorola implementation	63

E. 3.	Basic instructions	64

E. 3. 1.	Integer instructions	64

E. 3. 2.	Real instructions	99

E. 3. 3.	Boolean instructions	134

E. 3. 4.	Message instructions	161

E. 3. 5.	Timer instructions	188

E. 4.	Labels and jumps	214

E. 5.	Parameter passing instructions	220

E. 5. 1.	Integer instructions	220

E. 5. 2.	Real instructions	222

E. 5. 3.	Boolean instructions	224

E. 5. 4.	Message instructions	226

E. 5. 5.	Timer instructions	228

E. 5. 6.	SFC instructions	230

E. 6.	Parameter access from a function	234

E. 6. 1.	Integer instructions	234

E. 6. 2.	Real instructions	237

E. 6. 3.	Boolean instructions	240

E. 6. 4.	Message instructions	243

E. 6. 5.	Timer instructions	246

E. 7.	Access to FB output parameters	249

E. 7. 1.	Integer instructions	249

E. 7. 2.	Real instructions	251

E. 7. 3.	Boolean instructions	253

E. 7. 4.	Message instructions	256

E. 7. 5.	Timer instructions	258

E. 8.	Calling function instructions	260

E. 8. 1.	Nil instructions	260

E. 8. 2.	Integer instructions	262

E. 8. 3.	Real instructions	268

E. 8. 4.	Boolean instructions	275

E. 8. 5.	Message instructions	285

E. 8. 6.	Timer instructions	292

E. 9.	SFC control functions instructions	299

E. 10.	Activity control timer instructions	304

E. 11.	Function system instructions	307

E. 11. 1.	Integer Instructions	307

E. 11. 2.	Boolean instructions	314

E. 12.	Conversion function instructions	321

E. 13.	Step activity instructions	324

E. 13. 1.	Boolean instructions	324

E. 13. 2.	Timer instructions	326

E. 14.	Calling function block instructions	328

E. 15.	End of block instruction	331

E. 16.	Reserved TIC code	333

E. 17.	Instruction summary	337

F.	Appendix 3 : Communication Protocol definition	340

F. 1.	Overview	340

F. 2.	Main format	340

F. 2. 1.	Exchange mechanism	340

F. 2. 2.	Frame format	341

F. 2. 3.	Slave number	341

F. 2. 4.	Function codes	341

F. 2. 5.	Frame identification	342

F. 2. 6.	Packet numbering	342

F. 2. 7.	CRC16 checksum	342

F. 3.	Download exchanges	343

F. 3. 1.	Beginning of download	344

F. 3. 2.	Downloading packets	345

F. 3. 3.	End of download	345

F. 4.	Requests used for Upload	346

F. 5.	Control exchanges	348

F. 5. 1.	Initiate communication	348

F. 5. 2.	Control PLC	348

F. 5. 3.	Monitor application state	349

F. 6.	Application level requests	350

F. 6. 1.	R_BKT: set breakpoint	352

F. 6. 2.	R_WBOO: write boolean variable	352

F. 6. 3.	R_WANA: write analog variable	352

F. 6. 4.	R_WTMR: write timer variable	353

F. 6. 5.	R_WMSG: write message variable	353

F. 6. 6.	R_TSTART: start timer	354

F. 6. 7.	R_TSTOP: stop timer	354

F. 6. 8.	R_CC: set cycle by cycle mode	354

F. 6. 9.	R_RT: set real time mode	354

F. 6. 10.	R_EC: execute one cycle	354

F. 6. 11.	R_TUC: transition unconditional clearing	355

F. 6. 12.	R_TCC: transition conditional clearing	355

F. 6. 13.	R_BKDEL: remove breakpoint	355

F. 6. 14.	R_TCW: set cycle timing	355

F. 6. 15.	R_TCR: read cycle timing	356

F. 6. 16.	R_GSTART: start SFC program	356

F. 6. 17.	R_GFREEZE: freeze SFC program	356

F. 6. 18.	R_GKILL: kill SFC program	357

F. 6. 19.	R_GRST: restart SFC program	357

F. 6. 20.	R_GER: get last application error	357

F. 6. 21.	R_UNLOCK: unlock I/O variable	357

F. 6. 22.	R_LOCK: lock I/O variable	358

F. 6. 23.	R_LOCKR: get list of locked I/O variables	358

F. 6. 24.	R_APPL: get application identification	358

F. 6. 25.	R_RANY: read a list of variables (all types)	359

F. 6. 26.	R_UPMDF: realize delayed On-Line modification	360

F. 7.	Summary	361

G.	Appendix 4 : C code definition	364

G. 1.	Introduction	364

G. 2.	General principle of C code generation	364

G. 2. 1.	Principle	364

G. 3.	Architecture	366

G. 3. 1.	Compliance	366

G. 3. 2.	Data representation	366

G. 3. 3.	Code representation	366

G. 3. 4.	Function call of Kernel	368

G. 3. 5.	TIC code representation	369

G. 4.	Description of generated files	380

G. 4. 1.	Appli.h structure	380

G. 4. 2.	Appli.c structure	380

G. 5.	EXAMPLE : RFWASH	415

G. 5. 1.	Appli.h	415

G. 5. 2.	Appli.c	418

# Introduction

This document describes the software interface and data exchange between ISaGRAF Workbench and ISaGRAF Kernel. Most of the information provided here concerns the Workbench.

The first chapter gives an overall view of ISaGRAF, particularly the architecture and how applications are generated. In addition, the components of the Workbench and the Kernel are precisely described.

The second chapter describes the interface between the Workbench and the Kernel.

The remaining chapters display a detailed description of the interface elements (included as appendices).

# ISaGRAF overview

This section gives a general view of the main components of ISaGRAF; their names, positions and structures.

## ISaGRAF architecture

ISaGRAF is made of two parts. The Workbench, which is located on the development system. Programs are developed with the 5 languages of the standard IEC 1131-3. The Kernel, which is located on the target system. Its role is to execute the applications generated by the Workbench in a special format.

| Workbench |
| --- |
| Editor / Configuration | Used to write an application with the 5 standard languages and to connect the variables to the boards. |
| Compiler | Used for translating the applications in a Database which will be directly executed by the Kernel. |
| Communication | Used for communicating with the Kernel. |
| C code generation | Translates the Database in C files. |
| Kernel |
| I/O drivers | Used for communicating with the I/O boards. |
| System | Used for managing the system resources of the target. |
| Communication | Used for communicating with the Workbench. |
| Server | Used in a multi-task environment to communicate with other tasks. |

## Application Generation

Application Generation directly follows the writing of the application. This phase consists of translating the source code into a target code through a compilation process. The result of the compilation is a Database containing the data and the code of the application. From here there are two possible uses of the Database:

- The first choice is the standard solution, which consists of downloading the Database into the target and executing it directly from the Kernel.

- The second choice is to obtain a target system dependent code; this is generally more efficient. The ISaGRAF-Compiler produces C code from the Database. These C files are recompiled with the Kernel source in order to obtain an executable file.

# Workbench/Kernel Interface

This section identifies the software and data elements providing the interface between the Workbench and the Kernel. The role of each  (for the Workbench side only) is defined below.

A detailed description of these interfaces is given in Appendix 3.

## Interface description

The interface between the Workbench and the Kernel is constituted of necessary specific database and communication systems to exchange data.

There are 4 parts in the interface organised in the following way:

### Application Database

The Application Database is a file that contains the data and code of an application after compilation. This section describes briefly the structure and the format of the Database. A detailed description of the Database is given in Appendix 1.

#### Database structure

An application Database is a set of tables producing a hierarchical system including application data and code.

- Data
The data of an application concerns mainly: variables, initial values, I/O connections etc.

- Code
The code of an application is the set of instructions forming the body of functions, function blocks, programs, steps and transitions.

In the Database, the application code is written in a format defined by CJ International. This format is called TIC code (Target Independent Code). The detail of the TIC code is given in Appendix 2.

#### Database format

The Database format depends on a target processor type and a chosen memory model.

- Processor type:

ISaGRAF can generate a Database for INTEL or MOTOROLA processors. For MOTOROLA processors the HIGH and LOW are switched.

- Memory model

Actually, only the memory model is proposed on ISaGRAF V3.x. This model called Medium defines the code and operands (maximum 3) of TIC instructions on 16 bits.

| Instruction | Size (bits) |
| --- | --- |
| code | 16 bits |
| operand 1 | 16 bits |
| operand 2 | 16 bits |
| operand 3 | 16 bits |

### ISaGRAF Communication protocol

The ISaGRAF communication protocol links the Workbench to the Kernel. The communication has several roles in ISaGRAF.

- It is used to transfer files from the Workbench to the target. These files are compiled-codes or symbols of an application.

- The communication allows the Workbench to control and monitor the Kernel state (stop, run etc.).

- The communication allows the Workbench Debugger to monitor the application variables.

ISaGRAF Communication Protocol is a CJ International protocol based on Modbus. The principle of data exchange from the Workbench (master) and the Kernel (slave) is the same as Modbus but the function codes are different.

A detailed presentation of this protocol is described in Appendix 3.

### C file generation

C file generation is a possibility offered by ISaGRAF to generate an application with a shorter execution time than the TIC code.

The principle of C files in an application is to translate the Database in C code. This process is defined in Appendix 4.

# Appendix 1 : Database description

## Database description

This chapter describes all the tables forming the Database. For each table, the structure, name and size (in bytes) is defined.

### Specification of the description

This section defines the notation used to describe the tables.

#### Data definition

Generally the data are values (V), however, certain tables contain references to others tables. In this case there are two types of reference:

- a reference to the beginning of the Database. It is an absolute reference named : AR.

- a reference to the beginning of a table. It is a relative reference named : RR.

| Mnemonic | V | S | RR | AR |
| --- | --- | --- | --- | --- |
| Comment | numeric value | string of characters | relative reference | absolute reference |

#### Processor dependence

The format of the data depends on the processor on which it is executed. There are two formats : INTEL or MOTOROLA. In addition, two mnemonics classify the table contents: PD (processor dependent) and PI (processor independent).

| Size | 1 byte(1 | 2 bytes(12 | 4 bytes(1234 |
| --- | --- | --- | --- |
| Intel format | 1 | 12 | 1234 |
| Motorola format | 1 | 21 | 4321 |

#### Type of data

| data type | corresponding 'C' type | Size (bytes) | comments |
| --- | --- | --- | --- |
| uint16 | unsigned short | 2 |  |
| uint32 | unsigned long | 4 | can contain an address |
| uchar | unsigned char | 1 |  |
| charx | char t[x] | x |  |
| floating point | floating point | 4 |  |

### Table addresses

This is the main table, it is the entry point in the tables' hierarchy.

| Name : __MAIN | Size : 64 bytes |  |  |
| --- | --- | --- | --- |
| Field No. | Format | Type | Comment |
| 1 | uint32 | V, PD | indicator of processor validity |
| 2 | uint32 | AR, PD | address of definition table of the product |
| 3 | uint32 | AR, PD | address of definition table of the application |
| 4 | uint32 | AR, PD | address of definition table of the user functions |
| 5 | uint32 | AR, PD | address of definition table of the function blocks |
| 6 | uint32 | AR, PD | address of definition table of the conversion functions |
| 7 | uint32 | AR, PD | address of definition table of conversion tables |
| 8 | uint32 | AR, PD | address of definition table of variables |
| 9 | uint32 | AR, PD | address of coding variables |
| 10 | uint32 | AR, PD | address of definition table of boards definition |
| 11 | uint32 | AR, PD | address of coding table of OEM |
| 12 | uint32 | AR, PD | address of definition table of hierarchy project |
| 13 | uint32 | AR, PD | address of definition table of programs |
| 14 | uint32 | AR, PD | address of coding table of programs |
| 15 | uint32 | AR, PD | address of structure SFCs table |
| 16 | uint32 | AR, PD | address of resources table |

| Field No. | Notes |
| --- | --- |
|  | It is a integer at 1(value set by the compiler). The kernel must read the same value else the Database and the Kernel are not in accordance. For example, if you compile an application for an INTEL processor and you try to run it on a MOTOROLA target. |
|  | It is an absolute address of the definition table of the product (see chapter D.1.2.0). For example, the table being at address 00 00 00 64 is coded (for INTEL format) : 64 00 00 00 |
|  | It is an absolute address of the definition table of the application (see chapter D.1.2.D. 1. 2. 2. ). For example, the table at address 00 0 00 40 is coded (for INTEL format) : 40 00 00 00 |
|  | It is an absolute address of the definition table of the user functions (see chapter D.1.2.1). For example, the table at address 00 00 02 B4 is coded (for INTEL format) : B4 02 00 00 |
|  | It is an absolute address of the definition table of the function blocks (see chapter D.1.2.D. 1. 2. 4. ). For example, the table at address 00 0 02 B8 is coded (for INTEL format) : B8 02 00 00 |
|  | It is an absolute address of the definition table of the conversion functions (see chapter D.1.2.D. 1. 2. 5. ). For example, the table at address 00 00 00 7C is coded (for INTEL format) : 7C 00 00 00 |
|  | It is an absolute address of the definition table of the conversion tables (see chapter D.1.2.0). For example, the table at address 00 00 00 80 is coded (for INTEL format) : 80 00 00 00 |
|  | It is an absolute address of the definition table of variables (see chapter D.1.2.D. 1. 2. 7. ). For example, the table at address 00 00 03 FC is coded (for INTEL format) : FC 03 00 00 |
|  | It is an absolute address of coding variables (see chapter D.1.2.D. 1. 2. 8. ). For example, the table at address 00 00 01 D4 is coded (for INTEL format) : D4 01 00 00 |
|  | It is an absolute address of the definition table of board definitions (see chapter D.1.2.D. 1. 2. 9. ). For example, the table at address 00 00 00 84 is coded (for INTEL format) : 84 00 00 00 |
|  | It is an absolute address of the coding table of OEM (see chapter D.1.2.0). For example, the table at the address 00 00 00 8C is coded (for INTEL format) : 8C 00 00 00 |
|  | It is an absolute address of the definition table of the project hierarchy (see chapter D.1.2.0). For example, the table at address 00 00 02 98 is coded (for INTEL format) : 98 02 00 00 |
|  | It is an absolute address of the definition table of programs (see chapter D.1.2.D. 1. 2. 12. ). For example, the table at address 00 00 02 A8 is coded (for INTEL format) : A8 02 00 00 |
|  | It is an absolute address of the coding table of programs (see chapter D.1.2.D. 1. 2. 13. ). For example, the table at address 00 00 02 AC is coded (for INTEL format) : AC 02 00 00 |
|  | It is an absolute address of the structure SFC's table (see chapter D.1.2.D. 1. 2. 14. ). For example, the table at address 00 00 02 B0 is coded (for INTEL format) : B0 02 00 00 |
|  | Is an absolute address of the resources table (see chapter D.1.2.D. 1. 2. 15. ). For example, the table at address 00 00 04 30 is coded (for INTEL format) : 30 04 00 00 |

#### Product definition

This table defines the kernel for which the application is generated.

| Name : __DEFPROD | Size : 24 bytes |  |  |
| --- | --- | --- | --- |
| Field No. | Format | Type | Comment |
| 1 | char16 | S, PI | target name |
| 2 | char8 | S, PI | target version |

| Field No. | Notes |
| --- | --- |
|  | Target name : It is a string of a maximum of 15 characters terminated by 0. The Kernel uses this information to verify if the Kernel and the Database are compatible. For example, a target named : (CC86M( is coded : 43 43 38 36 4D 00 00 00 00 00 00 00 00 00 00 00 |
|  | Target version : It is a string of a maximum of 7 characters terminated by 0. This information is not checked by the Kernel. For example, a target version named : (1.00( is coded : 31 2E 30 30 00 00 00 00 |

#### Application definition

This table defines the parameters of the project.

| Name : __DEFAPPLI | Size : 36 bytes |  |  |
| --- | --- | --- | --- |
| Field No. | Format | Type | Comment |
| 1 | char16 | S, PI | project name |
| 2 | uint32 | V, PD | generate date |
| 3 | uint32 | V, PD | check sum |
| 4 | uint16 | V, PD | application version |
| 5 | uint16 | V, PD | number of error in the buffer |
| 6 | uint16 | V, PD | starting mode |
| 7 | uint16 | V, PD | cycle time |
| 8 | uint32 | V, PD | application size |

| Field No. | Notes |
| --- | --- |
|  | Project name : It is a string of a maximum of 15 characters terminated by 0. For example a project named : (rfwash( is coded : 72 66 77 61 73 68 00 00 00 00 00 00 00 00 00 00 |
|  | Date : It is the compilation date and time of the application. This information is not directly used by the kernel but is used by the Debugger of the Workbench. In association with the Check sum it identifies an application. For example a date is coded (for INTEL format) : A0 3A EE 32 The date is calculated using the standard "time" function of the "C" run-time library of MSVC 1.52. |
|  | Check sum : It is a calculation in relation to the symbols of the application. It is not used directly by the Kernel but is used by the Debugger of the Workbench. In association with the Date it identifies an application. Another utilization is to compare this check sum with the check sum of the symbol table which can be download in the target. For example, a Check sum is coded (for INTEL format) : 5C 5F E9 0A |
|  | Version : After each compilation of the application, the version number is increased. For example , after 5 compilations the version number is coded (for INTEL format) : 05 00. |
|  | Error : This value defines the number of errors which can be printed. 0 indicates no printed errors. For example if you want to print 1 error message, this number is coded (for INTEL format) : 01 00 |
|  | Mode : This value indicates how the Kernel starts the application : 0 for real time and 1 for cycle to cycle. For example, the starting mode is coded : 00 00 |
|  | Cycle Time : It is the cycle time (ms) authorized for the application. If this time is exceeded, the kernel store it. A cycle time of 0 indicates that the Kernel does not manage it. For example, a cycle time of 10 ms is coded (for INTEL format) : 0a 00 |
|  | Size : It is the size in bytes of the Database of the application. In fact, it is the size of all the tables describes in this document. For example a size of 2324 bytes is coded (for INTEL format) : 14 09 00 00 |

#### Definition table of the user functions

This table defines the user functions written in ' C ' in the Kernel and called by the application.

| Name : __DEFUSF | Size : 4+ (n*12) bytes |  |  |
| --- | --- | --- | --- |
|  | Field No. | Format | Type | Comment |
| header | 1 | uint16 | V, PD | number of user functions |
|  | 2 | uint16 | V, PD | reserved |
| function | repeated | 3 | uint16 | V, PD | function number |
| description | n | 4 | char9 | S, PI | function name |
|  | times | 5 | char1 | S,PI | terminator |

| Field No. | Notes |
| --- | --- |
|  | This field defined the number n of user functions called by the application. For example if the application calls one user function, this number is coded (for INTEL format) : 01 00 |
|  | This reserved field is coded : 00 00 |
|  | Function number : this number (value is 1 to n) is calculated by the compiler for an application and used by the TIC code. Therefore, if two applications call the same user function, it may have a different number. This number allows the user function to be found. For example, a user function numbered 1 is coded (for INTEL format) : 01 00 |
|  | Function name : It is a string of a maximum of 8 characters terminated by 0. This name is independent of the application (not the function number). Also it is used by the Kernel to find the code corresponding to the function. For example, the user function named (cfsample( is coded : 43 46 53 41 4D 50 4C 45 00 |
|  | Terminator : this character is used to align the table fields numbered 3 and 4 to 12 characters. This field is coded : 00 |

The fields 3,4 and 5 are repeated 'number of user functions (field 1)' times.

#### Definition table of function blocks

This table defines the standard function blocks written in ' C ' in the Kernel (predefined list dependent on ISaGRAF) and the user function blocks written in ' C ' in the Kernel which the instance are declared in the application (list dependent on the application). The difference between standard and user function blocks is the name; prefixed for the standard blocks.

| Name : __DEFFBL | Size : 4+ (n*16) bytes |  |  |
| --- | --- | --- | --- |
|  |  | Field No. | Format | Type | Comment |
|  | header | 1 | uint16 | V, PD | number of functions block |
|  |  | 2 | uint16 | V, PD | reserved |
| function | repeated | 3 | uint16 | V, PD | function block number |
| blocks | n | 4 | uint16 | V, PD | number of instance |
| description | times | 5 | char10 | S,PI | function block name |
|  |  | 6 | uint16 | V,PD | terminator |

| Field No. | Notes |
| --- | --- |
|  | This field defines the number n of standard function blocks defined in ISaGRAF and user function blocks call by the application. For example, if the Database defines 20 function blocks, this number is coded (for INTEL format) : 14 00 |
|  | This reserved field is coded : 00 00 |
|  | Function number : this number (value 1 to n) is calculated by the compiler for an application and used by the TIC code. The standard blocks are always the same numbers because they are stored first in the table, however, it is different for the user blocks. In fact, if two applications call the same user block it may have different numbers. This number allows the name of the function block to be found. For example, a function block numbered 1 is coded (for INTEL format) : 01 00 |
|  | Number of instances. It is the number of instanciations of the function block numbered by the field 3. This information is used by the Kernel to manage the memory necessary for the data of the instances. For example, if the application instanciated a function block three times the number is (for INTEL format) : 03 00 |
|  | Function name : It is a string of a maximum of 9 characters terminated by 0. This name is independent of the application (not the function number). Also it is used by the Kernel to find the code corresponding to the function block. The name of standard blocks are prefixed by the character ' # '.For example, the standard block named (#sig_gen( is coded : 23 53 49 47 5F 47 45 4E 00 00 and the user block named : (cbsample( is coded : 43 42 53 41 4D 50 4C 45 00 00 |
|  | Terminator : this field is used to align the table fields numbered 3, 4 and 5 to 16 characters. This field is coded : 00 00 |

Fields 3 to 6 are repeated for each function block ('field 1' times).

#### Conversion functions

This table contains the conversion functions declared in the application.

| Name : __DEFFCNV | Size : 4+ (n*16) bytes |  |  |
| --- | --- | --- | --- |
|  |  | Field No. | Format | Type | Comment |
|  | header | 1 | uint16 | V, PD | number of conv. functions |
|  |  | 2 | uint16 | V, PD | reserved |
| conversion | repeated | 3 | uint16 | V, PD | conversion function number |
| function | n | 4 | uint16 | V, PD | reserved |
| description | times | 5 | char10 | S,PI | conversion function name |
|  |  | 6 | uint16 | V,PD | terminator |

| Field No. | Notes |
| --- | --- |
|  | Number n of conversion functions. It is the number of conversion functions declared in the application. For example, if one conversion function is declared this number is coded (for INTEL format) : 01 00 |
|  | reserved |
|  | Conversion function number. This number (between 128 and 255) is calculated by the linker. For example, a conversion function with the number 128 is coded (for INTEL format) : 81 00 |
|  | reserved |
|  | Conversion function name. It is a string of a maximum of 9 characters terminated by 0. This name is independent of the application (not the function number). Also, it is used by the Kernel to find the code corresponding to the function. For example, a conversion function named (bcd( is coded : 42 43 44 00 00 00 00 00 00 00 |
|  | Terminator : this field is used to align the table fields numbered 3, 4 and 5 to 16 characters. This field is coded : 00 00 |

Fields 3 to 6 are repeated (field 1) times.

#### Conversion tables

This table contains the conversion tables declared in the application.

| Name : __DEFTCNV | Size : 4+ n*(4+p*8) bytes |
| --- | --- |
|  |  |  | Field No. | Format | Type | Comment |
|  | header | 1 | uint16 | V, PD | number of conversion tables (n) |
|  |  | 2 | uint16 | V, PD | reserved |
| conversion | repeated |  | 3 | uint16 | V, PD | conversion table number |
| table | n |  | 4 | uint16 | V, PD | number of points (p) |
| description | times | repeated | 5 | floating point | V, PD | value from the device (x) |
|  |  | p times | 6 | floating point | V,PD | value for the application (y) |

| Field No. | Notes |
| --- | --- |
|  | Number of conversion tables. It is the number of conversion tables declared in the application. For example, if one conversion table is declared, this number is coded (for INTEL format) : 01 00 |
|  | The field 2 is reserved. |
|  | Conversion table number. This number (between 1 and 127) is calculated by the linker. For example, a conversion table with the number 1 is coded (for INTEL format) : 01 00 |
|  | Number of points. It is the number of points (x,y) defining the conversion between value reads from device (x) to value uses by the application(y). For example, a conversion table with 3 points is coded (for INTEL format) : 03 00 |
|  | Value from device. It is an ' electric value ' read from the device. For example, the 10.0 volts is coded (for INTEL format) : 00 00 20 41 |
|  | Value for application. It is a ' physical value ' used by the application. For example, the measure of 100.0 units is coded (for INTEL format) : 00 00 C8 42 |

Fields 5 and 6 are repeated (field 4) times. Fields 3 to 6 are repeated for each conversion table; (field 1) times.

#### Definition table of variables

This table defines the number of variables for each type (Boolean, Analog, Timer and Message) declared in the application.

| Name : __DEFVAR | Size : 32 bytes |  |  |
| --- | --- | --- | --- |
| Field No. | Format | Type | Comment |
| 1 | uint16 | V, PD | number of internal Boolean |
| 2 | unit16 | V, PD | number of input Boolean |
| 3 | unit16 | V, PD | number of output Boolean |
| 4 | unit16 | V, PD | reserved |
| 5 | unit16 | V, PD | number of internal analog |
| 6 | unit16 | V, PD | number of input analog |
| 7 | unit16 | V, PD | number of output analog |
| 8 | unit16 | V, PD | reserved |
| 9 | unit16 | V, PD | number of timer |
| 10 | unit16 | V, PD | reserved |
| 11 | unit16 | V, PD | reserved |
| 12 | unit16 | V, PD | reserved |
| 13 | unit16 | V, PD | number of internal message |
| 14 | unit16 | V, PD | number of input message |
| 15 | unit16 | V, PD | number of output message |
| 16 | unit16 | V, PD | reserved |

| Field No. | Notes |
| --- | --- |
|  | Number of internal Boolean variables. For example, one internal Boolean declared in the application is coded (for INTEL format) : 01 00 |
|  | Number of input Boolean variables connected to a board. For example, one input Boolean declared in the application and connected to a board with 8 inputs is coded (for INTEL format) : 08 00 |
|  | Number of output Boolean variables connected to a board. For example, one output Boolean declared in the application and connected to a board with 8 outputs is coded (for INTEL format) : 08 00 |
|  | reserved |
|  | Number of internal analogs. For example, two internal analogs declared in the application is coded (for INTEL format) : 02 00 |
|  | Number of input analog connected to a board. For example, two input analogs declared in the application and connected to a board with 8 inputs is coded (for INTEL format) : 08 00 |
|  | Number of output analog connected to a board. For example, two output analog declared in the application and connected to a board with 8 outputs is coded (for INTEL format) : 08 00 |
|  | reserved |
|  | Number of internal timer. For example, ten internal timers declared in the application is coded (for INTEL format) : 0A 00 |
|  | reserved |
|  | reserved |
|  | reserved |
|  | Number of internal messages. For example, one internal message declared in the application is coded (for INTEL format) : 01 00 |
|  | Number of input messages connected to a board. For example, one input message declared in the application and connected to a board with 8 inputs is coded (for INTEL format) : 08 00 |
|  | Number of output messages connected to a board. For example, one output message declared in the application and connected to a board with 8 outputs is coded (for INTEL format) : 08 00 |
|  | reserved |

#### Variables coding

This table defines the location of the initialization tables for each type and the number of variables to be initialized.

| Name : __CODEVAR | Size : 36 bytes |  |  |
| --- | --- | --- | --- |
| Field No. | Format | Type | Comment |
| 1 | uint32 | AR, PD | address of initialization Boolean table |
| 2 | uint32 | AR, PD | address of initialization analog |
| 3 | uint32 | AR, PD | address of initialization timer table |
| 4 | uint32 | AR, PD | address of initialization message table of initialization timer table |
| 5 | uint32 | AR, PD | address of length message table |
| 6 | uint32 | AR, PD | address of definition MODBUS table |
| 7 | uint32 | AR, PD | address of backup table |
| 8 | uint16 | V, PD | number of Boolean variable to be initialized |
| 9 | uint16 | V, PD | number of analog variable to be initialized |
| 10 | uint16 | V, PD | number of timer variable to be initialized |
| 11 | uint16 | V, PD | number of message variable to be initialized |

| Field No. | Notes |
| --- | --- |
|  | It is an absolute address of initialization Boolean table(see chapter D.1.2.8.D. 1. 2. 8. 1. ). For example, the table at address 00 00 08 42 is coded (for INTEL format) : 42 08 00 00 |
|  | It is an absolute address of initialization analog (see chapter D.1.2.8.D. 1. 2. 8. 2. ). For example, the table at address 00 00 02 4C is coded (for INTEL format) : 4C 02 00 00 |
|  | It is an absolute address of initialization timer table (see chapter D.1.2.8.0). For example, the table at address 00 00 02 50 is coded (for INTEL format) : 50 02 00 00 |
|  | It is an absolute address of initialization message table (see chapter D.1.2.8.0). For example, the table at address 00 00 02 54 is coded (for INTEL format) :54 02 00 00 |
|  | It is an absolute address of length message table (see chapter D.1.2.8.D. 1. 2. 8. 5. ). For example, the table at address 00 00 04 1C is coded (for INTEL format) : 1C 04 00 00 |
|  | It is an absolute address of definition MODBUS table (see chapter D.1.2.8.D. 1. 2. 8. 6. ) For example, the table at address 00 00 02 58 is coded (for INTEL format) : 58 02 00 00 |
|  | It is an absolute address of definition table of conversion tables (see chapter D.1.2.8.0) For example, the table at address 00 00 01 F8 is coded (for INTEL format) : F8 01 00 00 |
|  | Number of Boolean variable to be initialized |
|  | Number of analog variable to be initialized |
|  | Number of timer variable to be initialized |
|  | Number of message variable to be initialized |

##### Boolean initialization table

This table is the list of Boolean variables to be set to TRUE. The number (n) of elements is defined in field 8 of the table __CODEVAR.

| Name : __INITBOO | Size : (n*2) + 4 - (n*2 % 4) bytes |  |  |
| --- | --- | --- | --- |
|  |  | Field No. | Format | Type | Comment |
| Boolean description | repeated n times | 1 | uint16 | V, PD | variable number |
|  |  | n+1 | charx | S,PI | terminator |

| Field No. | Notes |
| --- | --- |
|  | Variable number. It is the variable number to be set at TRUE. For example, the Boolean numbered 9 is coded (for INTEL format) : 09 00 |
| n+1. | Terminator. It is a string of x null value. x is : 4 - (n*2 % 4). For example, if there are three Boolean variables to be initialized, the length of the terminator is : 4 - (3*2 % 4 ) = 2 and it is coded : 00 00 |

NOTE : % gives the integer remainder of a division. For example, 1%2=1

##### Analog initialization table

This table is the list of analog variables to be initialized with a value. The number (n) of elements is defined in field 9 of the table __CODEVAR.

| Name : __INITANA | Size : (n*6) + 4 - (n*6 % 4) bytes |  |  |
| --- | --- | --- | --- |
|  |  | Field No. | Format | Type | Comment |
| analog | repeated n | 1 | uint16 | V, PD | variable number |
| description | times | 2 | uint32 / floating point | V, PD | value |
|  |  | n*2+1 | charx | S,PI | terminator |

| Field No. | Notes |
| --- | --- |
|  | Variable number. It is the variable number to be set initialized with the value contented in the field 2. For example, the Analog numbered 5 is coded (for INTEL format) : 05 00 |
|  | value. It is the value (integer or floating pointing point) assigned to the variable defined by the field 1. For example, an integer value 10 is coded (for INTEL format) : 0A 00 and a real value 10.0 is coded (for INTEL format) : 00 00 20 41. |
| n*2+1. | Terminator. It is a string of x null value. x is : 4 - (n*6 % 4). For example, if there are three analogs to be initialized, the length of terminator is : 4 - (3*6 % 4 ) = 2 and it is coded : 00 00 |

NOTE : % gives the integer remainder of a division. For example, 1%2=1

##### Timer initialization table

This table is the list of timer variables to be initialized with a value. The number (n) of elements is defined in field 10 of the table __CODEVAR.

| Name : __INITTMR | Size : (n*6) + 4 - (n*6 % 4) bytes |  |  |
| --- | --- | --- | --- |
|  |  | Field No. | Format | Type | Comment |
| timer | repeated n | 1 | uint16 | V, PD | variable number |
| description | times | 2 | uint32 | V, PD | value |
|  |  | n*2+1 | charx | S,PI | terminator |

| Field No. | Notes |
| --- | --- |
|  | Variable number. It is the variable number to be set initialized with the value contented in the field 2. For example, the timer numbered 4 is coded (for INTEL format) : 04 00 |
|  | value. It is a integer value (millisecond) affected to the variable defined by the field 1. For example a value 10 ms is coded (for INTEL format) : 0A 00. |
| n*2+1. | Terminator. It is a string of x null characters. x is : 4 - (n*6 % 4). For example, if there are three timers to be initialized, the length of terminator is : 4 - (3*6 % 4 ) = 2 and it is coded : 00 00 |

NOTE : % gives the integer remainder of a division. For example, 1%2=1

##### Message initialization table

This table is the list of message variables to be initialized with a string of characters. The number (n) of elements is defined in field 11 of the table __CODEVAR.

| Name : __INITMSG | Size : (i=1,n)(3+li+2-((1+li)%2) +(4-(((5+li-(1+li)%2))%4) bytes |  |  |
| --- | --- | --- | --- |
|  |  | Field No. | Format | Type | Comment |
|  | repeated | 1 | uint16 | V, PD | variable number |
| message | n | 2 | uchar | V, PI | length |
| description | times | 3 | charx | S, PI | string |
|  |  | 4 | uchary | S, PI | extension |
|  |  | n*4+1 | charx | S,PI | terminator |

| Field No. | Notes |
| --- | --- |
|  | Variable number. It is the variable number to be set initialized with the value contented in the field 2. For example, the message numbered 4 is coded (for INTEL format) : 04 00 |
|  | Length. It is the length l (0-255) of the message defined in the field 3. For example the length of the message (aaa( is 3 and is coded : 03 |
|  | String. It is a string of x characters. For example the message (aaa( is coded : 61 61 61. |
|  | Extension. It is a string of x null characters. It is an extension at an even length of the fields 2 and 3 because MOTOROLA uses even addresses. Also x = 2-((1+l)%2). For example, the message (aaa( has an extension of x=2-((1+3)%2)=2 characters, but the message (aaaa( has an extension of x=2-((1+4)%2)=1 character coded : 00 |
| n*4+1. | Terminator. It is a string of x null characters. x is : 4 - (( (5+li-(1+li)%2))%4 with 1(i(n. For example, if there are two messages (aa( and (bbb( to be initialized, the length of terminator is 2 and it is coded : 00 00 |

NOTE : % gives the integer remainder of a division. For example, 1%2=1

##### Message length table

This table contains the maximum length of the declared message variable. Notably, this information allows the Kernel to reserve the necessary memory used to store the messages.

| Name : __LNGMSG | Size : n+(4-n%4) bytes |  |  |
| --- | --- | --- | --- |
|  |  | Field No. | Format | Type | Comment |
| length description | repeated n times | 1 | uchar | V, PI | message length |
|  |  | n+1. | charx | S, PI | terminator |

| Field No. | Notes |
| --- | --- |
|  | Message length. It is the maximum length of the message variable. The message number corresponds to the order in the table (the second message length is the number variable two). For example, a message declared with a maximum length of 20 characters is coded: 14 |
| n+1. | Terminator. It is a string of x null value. x is : 4 - (n%4). For example, if there are three messages the length of terminator is : 4 - (3%4 ) = 1 and it is coded : 00 |

NOTE : % gives the integer remainder of a division. For example, 1%2=1

##### MODBUS definition table

This table contains the reference to the MODBUS tables for each type.

| Name : __DEFMODBUS | Size : 16 bytes |  |  |
| --- | --- | --- | --- |
| Field No. | Format | Type | Comment |
| 1 | uint32 | AR, PD | address of Boolean MODBUS definition table |
| 2 | uint32 | AR, PD | address of analog MODBUS definition table |
| 3 | uint32 | AR, PD | address of timer MODBUS definition table |
| 4 | uint32 | AR, PD | address of message MODBUS definition table |

| Field No. | Notes |
| --- | --- |
|  | It is an absolute address of the Boolean MODBUS definition table (see chapter D.1.2.8.6.D. 1. 2. 8. 7. ). For example, the table at address 00 00 02 68 is coded (for INTEL format) : 68 02 00 00 |
|  | It is an absolute address of the analog MODBUS definition table (see chapter D.1.2.8.6.D. 1. 2. 8. 8. ). For example, the table at address 00 00 02 74 is coded (for INTEL format) : 74 02 00 00 |
|  | It is an absolute address of the timer MODBUS definition table (see chapter D.1.2.8.6.0). For example, the table at address 00 00 02 80 is coded (for INTEL format) : 80 02 00 00 |
|  | It is an absolute address of the message MODBUS definition table (see chapter D.1.2.8.6.0). For example, the table at address 00 00 02 8C is coded (for INTEL format) : 8C 02 00 00 |

##### Boolean MODBUS table definition

This table defines all the Boolean variables which have a MODBUS address.

| Name : __DEFMDBBOO | Size : 12+n*4 bytes |  |  |
| --- | --- | --- | --- |
|  |  | Field No. | Format | Type | Comment |
|  |  | 1 | uint16 | V, PD | number |
| header |  | 2 | uint16 | V, PI | lowest address |
|  |  | 3 | uint16 | V, PD | highest address |
|  |  | 4 | uint16 | V, PD | reserved |
| message | repeated n | 5 | uint16 | V, PD | address |
| description | times | 6 | uint16 | V, PD | variable number |
|  |  | n*2+5 | uint32 | V, PI | terminator |

| Field No. | Notes |
| --- | --- |
|  | Number. It is the number of Boolean variables which have a MODBUS address. For example, two Boolean variables with an MODBUS address are coded (for INTEL Format) :02 00 |
|  | Lowest address. This information indicates which has the lowest address of all Boolean variables which are a MODBUS address. For example, the address 1000 (hexa) is coded (for INTEL format) : 00 10 |
|  | Highest address. This information indicates which is the highest address of all Boolean which are a MODBUS address. For example, the address 2000 (hexa) is coded (for INTEL format) : 00 20 |
|  | Reserved |
|  | Address. It is the MODBUS address of the Boolean variable numbered in the field 6. For example, the address 1000 (hexa) is coded (for INTEL format) : 00 10 |
|  | Variable number. It is the Boolean number. For example, the Boolean numbered 4 is coded (for INTEL format) : 04 00 |
| n*2+5. | Terminator. Is a null value coded : 00 00 00 00 |

##### Analog MODBUS table definition

This table defines all the analog variables which have a MODBUS address.

| Name : __DEFMDBANA | Size : 12+n*4 bytes |  |  |
| --- | --- | --- | --- |
|  |  | Field No. | Format | Type | Comment |
|  |  | 1 | uint16 | V, PD | number |
| header |  | 2 | uint16 | V, PI | lowest address |
|  |  | 3 | uint16 | V, PD | highest address |
|  |  | 4 | uint16 | V, PD | reserved |
| message | repeated n | 5 | uint16 | V, PD | address |
| description | times | 6 | uint16 | V, PD | variable number |
|  |  | n*2+5 | uint32 | V, PI | terminator |

| Field No. | Notes |
| --- | --- |
|  | Number. It is the number of Boolean variables which have a MODBUS address. For example, two analogs with a MODBUS address are coded (for INTEL Format) :02 00 |
|  | Lowest address. This information indicates which is the lowest address of all analogs which are a MODBUS address. For example, the address 1000 (hexa) is coded (for INTEL format) : 00 10 |
|  | Highest address. This information indicates which is the highest address of all analogs which are a MODBUS address. For example, the address 2000 (hexa) is coded (for INTEL format) : 00 20 |
|  | Reserved |
|  | Address. It is the MODBUS address of the analog variable numbered in the field 6. For example, the address 1000 (hexa) is coded (for INTEL format) : 00 10 |
|  | Variable number. It is the analog number. For example, the analog numbered 4 is coded (for INTEL format) : 04 00 |
| n*2+5. | Terminator. Is a null value coded : 00 00 00 00 |

##### Timer MODBUS table definition

This table defines all the timer variables which have an MODBUS address.

| Name : __DEFMDBTMR | Size : 12+n*4 bytes |  |  |
| --- | --- | --- | --- |
|  |  | Field No. | Format | Type | Comment |
|  |  | 1 | uint16 | V, PD | number |
| header |  | 2 | uint16 | V, PI | lowest address |
|  |  | 3 | uint16 | V, PD | highest address |
|  |  | 4 | uint16 | V, PD | reserved |
| message | repeated n | 5 | uint16 | V, PD | address |
| description | times | 6 | uint16 | V, PD | variable number |
|  |  | n*2+5 | uint32 | V, PI | terminator |

| Field No. | Notes |
| --- | --- |
|  | Number. It is the number of timer variable which have a MODBUS address. For example, two timers with an MODBUS address are coded (for INTEL Format) :02 00 |
|  | Lowest address. This information indicates which is the lowest address of all timers which are a MODBUS address. For example, the address 1000 (hexa) is coded (for INTEL format) : 00 10 |
|  | Highest address. This information indicates which is the highest address of all timers which are a MODBUS address. For example, the address 2000 (hexa) is coded (for INTEL format) : 00 20 |
|  | Reserved |
|  | Address. It is the MODBUS address of the timer variable numbered in the field 6. For example, the address 1000 (hexa) is coded (for INTEL format) : 00 10 |
|  | Variable number. It is the timer number. For example, the timer numbered 4 is coded (for INTEL format) : 04 00 |
| n*2+5. | Terminator. Is a null value coded : 00 00 00 00 |

##### Message MODBUS table definition

This table defines all the message variables which have a MODBUS address.

| Name : __DEFMDBMSG | Size : 12+n*4 bytes |  |  |
| --- | --- | --- | --- |
|  |  | Field No. | Format | Type | Comment |
|  |  | 1 | uint16 | V, PD | number |
| header |  | 2 | uint16 | V, PI | lowest address |
|  |  | 3 | uint16 | V, PD | highest address |
|  |  | 4 | uint16 | V, PD | reserved |
| message | repeated n | 5 | uint16 | V, PD | address |
| description | times | 6 | uint16 | V, PD | variable number |
|  |  | n*2+5 | uint32 | V, PI | terminator |

| Field No. | Notes |
| --- | --- |
|  | Number. It is the number of message variable which have a MODBUS address. For example, two messages with an MODBUS address are coded (for INTEL Format) :02 00 |
|  | Lowest address. This information indicates which is the lowest address of all messages which are a MODBUS address. For example, the address 1000 (hexa) is coded (for INTEL format) : 00 10 |
|  | Highest address. This information indicates which is the highest address of all messages which are a MODBUS address. For example, the address 2000 (hexa) is coded (for INTEL format) : 00 20 |
|  | Reserved |
|  | Address. It is the MODBUS address of the message variable numbered in the field 6. For example, the address 1000 (hex) is coded (for INTEL format) : 00 10 |
|  | Variable number. It is the message number. For example, the message numbered 4 is coded (for INTEL format) : 04 00 |
| n*2+5. | Terminator. Is a null value coded : 00 00 00 00 |

##### Backup table

This table contains all the information to be saved by the Kernel.

| Name : __BACKUP | Size : 80 bytes |  |  |
| --- | --- | --- | --- |
| Field No. | Format | Type | Comment |
| 1 | char64 | S, PI | memory area |
| 2 | uint16 | V, PD | number of Boolean |
| 3 | uint16 | V, PD | first Boolean |
| 4 | uint16 | V, PD | number of Analog |
| 5 | uint16 | V, PD | first Analog |
| 6 | uint16 | V, PD | number of Timers |
| 7 | uint16 | V, PD | first Timer |
| 8 | uint16 | V, PD | number of Message |
| 9 | uint16 | V, PD | first Message |

| Field No. | Notes |
| --- | --- |
|  | Memory area. It contents the backup’s parameters in Ascii mode : address and size for each type. For example, you want to save the Boolean at the address 1000 and reserved an area of 16 bytes for it. It is coded : 31 30 30 30 2C 31 36 00 - 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 - 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 - 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 - 00 00 00 00 00 00 00 00 |
|  | Number of Boolean variables. This is the number of Boolean variables to be saved. One Boolean to be saved is coded (for INTEL format) : 01 00 |
|  | First Boolean. This is the number of the first Boolean variables to be saved. The Boolean numbered 9 to be saved is coded (for INTEL format) : 09 00 |
|  | Number of analog. This is the number of analog variables to be saved. Two analogs to be saved is coded (for INTEL format) : 02 00 |
|  | First analog. This is the number of the first analog variables to be saved. The analog numbered 10 to be saved is coded (for INTEL format) : 0A 00 |
|  | Number of timer. This is the number of timer variables to be saved. Five timers to be saved is coded (for INTEL format) : 05 00 |
|  | First timer. This is the number of the first timer variables to be saved. The timer numbered 16 to be saved is coded (for INTEL format) : 10 00 |
|  | Number of message. This is the number of message variables to be saved. One message to be saved is coded (for INTEL format) : 01 00 |
|  | First message. This is the number of the first message variables to be saved. The Boolean numbered 8 to be saved is coded (for INTEL format) : 08 00 |

NOTE : The linker arranges all the variables to be saved from the first variable number.

#### Boards definition

This table contains the information concerning the number of input/output boards or the number of real variables.

| Name : __DEFOEM | Size : 8 bytes |  |  |
| --- | --- | --- | --- |
| Field No. | Format | Type | Comment |
| 1 | uint16 | V, PD | Number of inputs board |
| 2 | uint16 | V, PD | Number of outputs board |
| 3 | uint16 | V, PD | Number of analog variables (floating point, convert) |
| 4 | uint16 | V, PD | Reserved |

| Field No. | Notes |
| --- | --- |
|  | Number of inputs board. It is the total number of inputs board (Boolean, analog and message). For example 3 inputs board are coded (for INTEL format) : 03 00 |
|  | Number of outputs board. It is the total number of outputs board (Boolean, analog and message). For example 2 outputs board are coded (for INTEL format) : 02 00 |
|  | Number of variable to convert. It is the number of input/output analog variables to convert in real. For example, 1 variable to convert is coded (for INTEL format) : 01 00 |
|  | Reserved. |

#### OEM table coding

This table contains the references to the table OEM.

| Name : __CODEOEM | Size : 16 bytes |  |  |
| --- | --- | --- | --- |
| Field No. | Format | Type | Comment |
| 1 | uint32 | AR, PD | Address of Boolean table OEM |
| 2 | uint32 | AR, PD | Address of Analog table OEM |
| 3 | uint32 | AR, PD | Address of Message table OEM |
| 4 | uint32 | AR, PD | Address of I/O boards definition |

| Field No. | Notes |
| --- | --- |
|  | Address of Boolean table OEM (see the chapter D.1.2.10.D. 1. 2. 10. 1. ). For example, the table at address 00 00 00 D0 is coded (for INTEL format) : D0 00 00 00 |
|  | Address of analog table OEM (see the chapter D.1.2.10.D. 1. 2. 10. 2. ). For example, the table at address 00 00 01 10 is coded (for INTEL format) : 10 01 00 00 |
|  | Address of message table OEM (see the chapter D.1.2.10.D. 1. 2. 10. 3. ). For example, the table at address 00 00 01 D0 is coded (for INTEL format) : D0 01 00 00 |
|  | Address of I/O boards definition (see the chapter D.1.2.10.D. 1. 2. 10. 4. ). For example, the table at address 00 00 00 9C is coded (for INTEL format) : D0 00 00 00 |

##### Boolean table (OEM)

This table contains the information necessary to connect the Boolean to the input or output Boolean board.

| Name : __DEFBOO | Size : n*8 bytes |  |  |
| --- | --- | --- | --- |
|  |  | Field No. | Format | Type | Comment |
|  |  | 1 | uint16 | V, PD | number |
|  |  | 2 | uchar | V, PI | rack |
| Boolean | repeated n | 3 | uchar | V, PI | slot |
| description | times | 4 | uchar | V, PI | channel |
|  |  | 5 | uchar | V, PI | I/O |
|  |  | 6 | uchar | V, PI | conversion/length |
|  |  | 7 | uchar | V, PI | real |

| Field No. | Notes |
| --- | --- |
|  | Number. It is the Boolean variable number connected. For example, the variable numbered 1is coded (for INTEL Format) :01 00 |
|  | Rack number. It is the rack number (0-255) where a set of boards are plugged. A PLC can have several racks. For example, a rack numbered 2 is coded : 02 |
|  | Slot number. It is the slot number (0 to 255) where the board is plugged. For example, a slot numbered 1 is coded : 01 |
|  | Channel number. It is the channel number (0 to 255) where the variable is connected. For example, a channel numbered 1 is coded : 01 |
|  | I/O. It is an indicator of input board (value equal 0) or output board (value different 0). For example an output board is coded : 01 |
|  | Conversion/length. It is a null value coded : 00 |
|  | Real. It is a null value coded : 00 |

NOTE : n is defined in the table __DEFEOM

##### Analog table (OEM)

This table contains the information necessary to connect the analog variables to the input or output analog board.

| Name : __DEFANA | Size : n*8 bytes |  |  |
| --- | --- | --- | --- |
|  |  | Field No. | Format | Type | Comment |
|  |  | 1 | uint16 | V, PD | number |
|  |  | 2 | uchar | V, PI | rack |
| analog | repeated n | 3 | uchar | V, PI | slot |
| description | times | 4 | uchar | V, PI | channel |
|  |  | 5 | uchar | V, PI | I/O |
|  |  | 6 | uchar | V, PI | conversion/length |
|  |  | 7 | uchar | V, PI | real |

| Field No. | Notes |
| --- | --- |
|  | Number. It is the analog variable number connected. For example, the variable numbered 1is coded (for INTEL Format) :01 00 |
|  | Rack number. It is the rack number (0-255) where a set of boards are plugged. A PLC can have several racks. For example, a rack numbered 2 is coded : 02 |
|  | Slot number. It is the slot number (0 to 255) where the board is plugged. For example, a slot numbered 1 is coded : 01 |
|  | Channel number. It is the channel number (0 to 255) where the variable is connected. For example, a channel numbered 1 is coded : 01 |
|  | I/O. It is an indicator of input board (value equal 0) or output board (value different 0). For example an output board is coded : 01 |
|  | Conversion/length. It is the function or table conversion number used to convert the analog (see table __DEFFCNV and __DEFTCNV). For example a conversion function numbered 81 (hexa) is coded: 81 |
|  | Real. It is a null value if the variable is an analog or a none null value if the variable is a real. For example, a real is coded : 01 |

NOTE : n is defined in the table __DEFEOM

##### Message table (OEM)

This table contains the information necessary to connect the message to the input or output analog board.

| Name : __DEFMSG | Size : n*8 bytes |  |  |
| --- | --- | --- | --- |
|  |  | Field No. | Format | Type | Comment |
|  |  | 1 | uint16 | V, PD | number |
|  |  | 2 | uchar | V, PI | rack |
| message | repeated n | 3 | uchar | V, PI | slot |
| description | times | 4 | uchar | V, PI | channel |
|  |  | 5 | uchar | V, PI | I/O |
|  |  | 6 | uchar | V, PI | conversion/length |
|  |  | 7 | uchar | V, PI | real |

| Field No. | Notes |
| --- | --- |
|  | Number. It is the message variable number connected. For example, the variable numbered 1is coded (for INTEL Format) :01 00 |
|  | Rack number. It is the rack number (0-255) where a set of boards are plugged. A PLC can have several racks. For example, a rack numbered 2 is coded : 02 |
|  | Slot number. It is the slot number (0 to 255) where the board is plugged. For example, a slot numbered 1 is coded : 01 |
|  | Channel number. It is the channel number (0 to 255) where the variable is connected. For example, a channel numbered 1 is coded : 01 |
|  | I/O. It is an indicator of input board (value equal 0) or output board (value different 0). For example an output board is coded : 01 |
|  | Conversion/length. It is a the length of the message (see the table __LNGMSG). For example a input message declares with a maximum 100 (decimal) is coded : 64 |
|  | Real. It is a null value coded : 00 |

NOTE : n is defined in the table __DEFEOM

##### I/O boards definition

This table defines all the I/O boards numbered from 1 to n.

| Name : __DEFBRD | Size : 12*n + (4 - (((12+xi))%4) bytes 1(i(n |  |  |
| --- | --- | --- | --- |
|  |  | Field No. | Format | Type | Comment |
|  |  | 1 | uint16 | V, PD | size |
|  |  | 2 | uint16 | V, PD | OEM key |
|  |  | 3 | uint16 | V, PD | first variable |
|  |  | 4 | uchar | V, PI | rack |
| board | repeated n | 5 | uchar | V, PI | slot |
| description | times | 6 | uchar | V, PI | mode |
|  |  | 7 | uchar | V, PI | type |
|  |  | 8 | uchar | V, PI | I/O |
|  |  | 9 | uchar | V, PI | number of connected variable |
|  |  | 10 | charx | S, PI | OEM board parameters |
|  |  | 11 | chary | S, PI | terminator |

| Field No. | Notes |
| --- | --- |
|  | Size. It is the size in bytess of the OEM board description (field 1 to 10). For example, a description size of 12 is coded (for INTEL format) : 0C 00 |
|  | OEM key. It is the hardware supplier number (different for each supplier). For example, hardware supplier with the number 1000 (hexa) is coded (for INTEL format) : 00 10 |
|  | First variable. It is the number of the first variable connected. For example, the variable numbered 9 connected to the board is coded (for INTEL format) : 09 00. |
|  | Rack number. It is the rack number (0-255) where a set of boards are plugged. A PLC can have several racks. For example, a rack numbered 2 is coded : 02 |
|  | Slot number. It is the slot number (0 to 255) where the board is plugged. For example, a slot numbered 1 is coded : 01 |
|  | Mode. It indicates if the board is in real mode (value equal to 1) or in simulation mode (null value). For example, a board in real mode is coded : 01 |
|  | Type. It is the type of the variables connected to the board. The type value is 1 for Boolean, 2 for analog and 3 for message. For example, a message board is coded : 03 |
|  | I/O. The value of this field indicated if the board is an input board (value equal to 0) or an output board (value equal to 1). For example, an output board is coded : 01 |
|  | Number of connected variable. It is the number of possible connection on the board (0 to 255). For example, a board of 8 inputs is coded : 08 |
|  | OEM board parameters. The contents depends of the configuration made by the OEM supplier. The size x of this field is : x=size-12. |
|  | Terminator. It is a string of y null characters. y is : 4 - (((12+xi))%4 with 1(i(n. For example, if a length of terminator of 2 is coded : 00 00 |

NOTE : The rack and slot number (field 4 and 5) allow to link the I/O variables define in the tables : __DEFBOO, __DEFANA, __DEFMSG.

#### Hierarchy project definition table

This table contains all the programs, functions and function blocks and defines the SFC hierarchy.

| Name : __DEFHIE | Size : 16+n*4 bytes |  |  |
| --- | --- | --- | --- |
|  |  | Field No. | Format | Type | Comment |
|  |  | 1 | uint16 | V, PD | number of BEGIN programs |
|  |  | 2 | uint16 | V, PD | number of END programs |
| header |  | 3 | uint16 | V, PD | number of SFC main |
|  |  | 4 | uint16 | V, PD | number of SFC child |
|  |  | 5 | uint16 | V, PD | number of functions or blocks |
|  |  | 6 | uint16 | V, PD | reserved |
| SFC | repeated | 7 | uint16 | V, PD | SFC number |
| description | n times | 8 | uint16 | V, PD | level |
|  |  | n*2+7 | char4 | V, PI | terminator |

| Field No. | Notes |
| --- | --- |
|  | Number of BEGIN program. For example, an application with two begin programs is coded (for INTEL format) : 02 00 |
|  | Number of END program. For example, an application with three end programs is coded (for INTEL format) : 03 00 |
|  | Number of SFC main. SFC main is the SFC having the highest level in the hierarchy. For example, an application with three SFC main is coded (for INTEL format) : 03 00 |
|  | Number of SFC child. A SFC child depends of a SFC main. For example, an application with five SFC child is coded (for INTEL format) : 05 00 |
|  | Number of function or IEC function blocks. For example, an application with three functions is coded (for INTEL format) : 03 00 |
|  | Reserved |
|  | SFC number. For example a SFC numbered 10 is coded (for INTEL format) : 0A 00 |
|  | Level. It is the hierarchy level number of a SFC. Level 0 identifies a main SFC and the other value (1..) are decreasing level for SFC child. For a SFC child with the level number 2 is coded (for INTEL format) : 02 00. Also, it indicates which there are two SFC above in the SFC hierarchy. |
| n*2+7. | Terminator. It is string of 4 null value coded : 00 00 00 00 |

#### Programs definition table

This table defines each program of an application. The programs are numbered from 1 to n.

| Name : __DEFPROG | Size : n*4 bytes |  |  |
| --- | --- | --- | --- |
|  |  | Field No. | Format | Type | Comment |
| program | repeated | 1 | uint16 | V, PD | program type |
| description | n time | 2 | uint16 | V, PD | level |

| Field No. | Notes |
| --- | --- |
|  | Program type. The programs type are identified by a number : 1 for BEGIN, 2 for END, 3 for SFC main, 4 for SFC child and 5 for function or IEC function block. For example a SFC main is coded (for INTEL format) : 03 00 |
|  | Level. It is the level of the SFC hierarchy. Also, the programs with the type 1,2,3 and 5 have a level numbered 0. A SFC child (type value : 1 to n) numbered 2 for example is coded (for INTEL format) : 02 00 |

NOTE : The number of programs is calculated with the table __DEFHIE (it is the total of the fields of 1 to 5).

#### Coding programs table

This table contains the address of all the program sequences (code of programs, SFC, function, IEC function blocks).

| Name : __CODEPROG | Size : n*4 bytes |  |  |
| --- | --- | --- | --- |
|  | Field No. | Format | Type | Comment |
| repeated n time | 1 | uint32 | AR, PD | Address of program sequence |

| Field No. | Notes |
| --- | --- |
|  | Address of program sequence. It is the absolute address of the programs code. For example, the table at address 00 00 00 D0 is coded (for INTEL format) : D0 00 00 00 |

NOTE : The number of programs is calculated with the table __DEFHIE (it is the total of the fields of 1 to 5).

##### Program sequence

This table contains some information in relation to the code of the application.

| Name : __ProgName_CODE | Size : 12*m+((s1k+s2k+s3k) +4*n ((s1l) +x bytes 1(k(m, 1(l(n |  |  |
| --- | --- | --- | --- |
|  | Field | Fmt | Type | Comment |
|  |  | BEGIN action or non | 1 | uint16 | RR, PD | address block |
| Step |  | SFC program | 2 | uint16 | V, PD | size block (s1) |
| SFC or | Rept'd | COMPLEX action | 3 | uint16 | RR, PD | address block |
| non SFC | m times |  | 4 | uint16 | V, PD | size block (s2) |
| desc. |  | END action | 5 | uint16 | RR, PD | address block |
|  |  |  | 6 | uint16 | V, PD | size block (s3) |
| transition SFC |  | repeated | 7 | uint16 | RR, PD | address block |
| description |  | n times | 8 | uint16 | V, PD | size block (t1) |
| block | rept'd | TIC code |  | 9 | uint16 | V, PD | TIC code |
| desc. | i times | desc. | rept'd p time | 10 | uint16 | V, PD | parameter |
|  |  |  |  | 11 | charx | S, PI | terminator |

| Field No. | Notes |
| --- | --- |
|  | Address block. It is an offset from the begin the table __ProgName_CODE. This address correspond to the block if code of the BEGIN action or a non SFC program. For example, the table being at the relative address 01 AC is coded (for INTEL format) : AC 01 |
|  | Size block. It is the size in bytess of the block of code of the BEGIN action or a non SFC program. For example a block of code of 28 bytes is coded (for INTEL format) : 1C 00 |
|  | Address block. It is an offset from the begin the table __ProgName_CODE. This address correspond to the block of code of the COMPLEX action. For example, the table being at the relative address 01 AC is coded (for INTEL format) : AC 01 |
|  | Size block. It is the size in bytess of the block of code of the COMPLEX action. For example a block of code of 28 bytes is coded (for INTEL format) : 1C 00 |
|  | Address block. It is an offset from the begin the table __ProgName_CODE. This address correspond to the block of code of the END action. For example, the table being at the relative address 01 AC is coded (for INTEL format) : AC 01 |
|  | Size block. It is the size in bytess of the block of code of the END action. For example a block of code of 28 bytes is coded (for INTEL format) : 1C 00 |
|  | Address block. It is an offset from the begin the table __ProgName_CODE. This address correspond to the block of code of a SFC transition. For example, the table being at the relative address 01 AC is coded (for INTEL format) : AC 01 |
|  | Size block. It is the size in bytess of the block of code of a SFC transition. For example a block of code of 28 bytes is coded (for INTEL format) : 1C 00 |
|  | TIC code. It is the TIC code number. For more information see the TIC code document. For example, the TIC code number 03 (hexa) is coded (for INTEL format) : 03 00 |
|  | Parameter. It a parameter of TIC code. For more information see the TIC code document. For example, a variable numbered 7 is coded (for INTEL format) : 07 00 |
|  | Terminator. It is a string of x null characters. x is : (2*p*i (((1+pu,v))%4 with 1(u(i and 1(v(p. For example, a terminator length of 2 is coded : 00 00 |

#### Table of the SFC’s structure

This table contains the address of all the program structure (structure of SFC programs).

| Name : __LINKSFC | Size : n*4 bytes |  |  |
| --- | --- | --- | --- |
|  | Field No. | Format | Type | Comment |
| repeated n time | 1 | uint32 | AR, PD | Address of program structure |

| Field No. | Notes |
| --- | --- |
|  | Address of program sequence. It is the absolute address for SFC programs and null address for none SFC programs. For example; the table at address 00 00 00 D0 is coded (for INTEL format) : D0 00 00 00 |

NOTE : The number of programs is calculated with the table __DEFHIE (it is the total of the fields of 1 to 5).

##### Address of the SFCs structure

This table defines all the steps and transitions and their links of a SFC programs. Be careful, because a SFC program can content several SFC.

| Name : __ProgName_LINK | Size : 8+2*m*((iu+iu+2) + 2*m*((jv+jv+2) + (8+2*m*((iu+iu+2) + 2*m*((jv+jv+2) )%4 with 1(u(i and 1(v(j bytes |  |  |
| --- | --- | --- | --- |
|  | Field No. | Format | Type | Comment |
|  | 1 | uint16 | V, PD | first transition |
| header | 2 | uint16 | V, PD | number of transition |
|  | 3 | uint16 | V, PD | first step |
|  | 4 | uint16 | V, PD | number of step |
| step link | repeated | 5 | uint16 | RR, PD | address predecessors |
| description | m times | 6 | uint16 | RR, PD | addr successors |
| transition link | repeated | 7 | uint16 | RR, PD | addr predecessors |
| description | n time | 8 | uint16 | RR, PD | address successors |
| predecessor | repeated i times | 9 | uint16 | V, PD | transition number |
| of step |  | 10 | uint16 | V, PD | terminator |
| successor | repeated j times | 11 | uint16 | V, PD | transition number |
| of step |  | 12 | uint16 | V, PD | terminator |
| predecessor | repeated k times | 13 | uint16 | V, PD | step number |
| of transition |  | 14 | uint16 | V, PD | terminator |
| successor | repeated l times | 15 | uint16 | V, PD | step number |
| of transition |  | 16 | uint16 | V, PD | terminator |
|  |  | 17 | charx | V, PD | terminator |

| Field No. | Notes |
| --- | --- |
|  | First transition. It is the first transition number of a SFC program. For example, the first transition numbered 1 is coded (for INTEL format) : 01 00 |
|  | Number of transition. It is the total number of transition of the SFC program. For example, a SFC with 10 transitions is coded (for INTEL format) : 0A 00 |
|  | First step. It is the first step number of a SFC program. For example, the first step numbered 100 is coded (for INTEL format) : 64 00 |
|  | Number of step. It is the total number of step of the SFC program. For example, a SFC with 20 steps is coded (for INTEL format) : 14 00 |
|  | Address predecessors. It is an address of the list of the predecessors of a step. It is an offset in bytes from the beginning of the table. For example, an offset of 30 bytes is coded (for INTEL format) : 1E 00 |
|  | Address successors. It is an address of the list of the successors of a step. It is an offset in bytes from the beginning of the table. For example, an offset of 20 bytes is coded (for INTEL format) : 14 00 |
|  | Address predecessors. It is an address of the list of the predecessors of a transition. It is an offset in bytes from the beginning of the table. For example, an offset of 30 bytes is coded (for INTEL format) : 1E 00 |
|  | Address successors. It is an address of the list of the successors of a transition. It is an offset in bytes from the beginning of the table. For example, an offset of 20 bytes is coded (for INTEL format) : 14 00 |
|  | Transition number. It is the transition number preceding the step. For example, the transition numbered 2 is coded (for INTEL format) : 02 00 |
|  | Terminator. It is a null value terminating the list of transitions preceding the step. This value is coded : 00 00 |
|  | Transition number. It is the transition number succeeding the step. For example, the transition numbered 4 is coded (for INTEL format) : 04 00 |
|  | Terminator. It is a null value terminating the list of transitions succeeding the step. This value is coded : 00 00 |
|  | Step number. It is the step number preceding the transition. For example, the step numbered 2 is coded (for INTEL format) : 02 00 |
|  | Terminator. It is a null value terminating the list of steps preceding the step. This value is coded : 00 00 |
|  | Step number. It is the step number succeeding the transition. For example, the step numbered 4 is coded (for INTEL format) : 04 00 |
|  | Terminator. It is a null value terminating the list of steps succeeding the step. This value is coded : 00 00 |
|  | Terminator. It is a string of x null value. x = (8+2*m*((iu+iu+2) + 2*m*((jv+jv+2) )%4 with 1(u(i and 1(v(j . A value of x of 1 is coded : 00 |

#### Resources table

This table contains all the information in relation to the resources.

| Name : __RESOURCE | Size : 4+32*i + ((xu+yu) + (4 + 32*I + ((xu+yu) )%4, 1(u(j bytes |  |  |
| --- | --- | --- | --- |
|  | Field No. | Format | Type | Comment |
| header | 1 | uint32 | V, PD | number of resources |
|  |  | 2 | char16 | S, PI | name |
|  | repeated | 3 | uint32 | V, PD | type |
| resource | i | 4 | uint32 | V, PD | data size |
|  | time | 5 | uint32 | V, PD | address of data |
|  |  | 6 | uint32 | V, PD | address of path |
| data | repeated | 7 | charx | S, PI | data |
|  | j time | 8 | chary | S, PI | path |
|  |  | 9 | charz | S, PI | terminator |

| Field No. | Notes |
| --- | --- |
|  | Number of resources. It is the number of resource of the application. For example, It five resources to be transfer are coded (for INTEL format) : 05 00 00 00 |
|  | Name. It the name of the resource. It is a string of 16 maximum characters terminated by 0. For example, a resource named (ANA( is coded : 41 4E 41 00 00 00 00 00 00 00 00 00 00 00 00 00 |
|  | Type. It is the type of resource. 1 for binary file, 2 for text file, 3 for ulongdata and 4 for varlist. For example, the type of a text file to be transfer is coded (for INTEL format) : 02 00 00 00 |
|  | Data size. It is the size in bytess of the data of the resource. For example, the size of a text file of 20 bytes to be transfer is coded (for INTEL format) : 14 00 00 00 |
|  | Address of data. It is an offset in bytes from the beginning of the current resource (field 1) which located the data. For example, an offset of 30 bytes id coded (for INTEL format) : 1E 00 00 00 |
|  | Address of path. It is an offset in bytes from the beginning of the current resource (field 1) which located the path for a file to be transfers. For example, an offset of 20 bytes id coded (for INTEL format) : 14 00 00 00 |
|  | Data. It is a string of x characters. X is defined by the field 4. For example the data (AAA( is coded : 41 41 41 |
|  | Path. It is a string of y characters terminated by 0. The path indicated the location in the target of a file to be transfer. For example the path (/PRJ( is coded : 2F 50 52 4A |
|  | Terminator. It is a string of x null value. x = (4 + 32*i + ((xu+yu) )%4 with 1(u(j.This value is coded : 00 |

# Appendix 2 : TIC code definition

## Introduction

This section is a whole description of the TIC code V2.00.

## Notations in the instructions

### Data type

The 'Type' field describes the data type of an object, and can take one of the following values:

| Type Name | Description | Format |
| --- | --- | --- |
| NIL | no type is associated to the object |  |
| INTEGER | integer analog | 16 bits |
| REAL | real analog |  |
| BOOLEAN | Boolean |  |
| MESSAGE | message string | 0-255 chars |
| TIMER | time of day in MS |  |
| SFC | SFC program |  |

### TIC code significance

The name of the TIC code contents certain mnemonic which indicate the type of the instruction.

| Attributes Name | Description | Example |
| --- | --- | --- |
| _OUT_ | instructions used to assign an output variable | TIC_OUT_A3I |
| _SYS_ | instructions used kernel functions | TIC_SYS_TAC |
| _USF_ | instructions represent a call to a user written C function | TIC_USF_A4B |
| _TRS_ | instructions used to assign a SFC transition receptivity | TIC_TRS_A3B |
| _STD_ | instructions represent a call to a standard C function | TIC_STD_FBL |
| _A1 | unary operation | TIC_A1B |
| _A2 | binary operation | TIC_A2I |
| _A3 | simple copy operation | TIC_A3M |
| _A4 | call function of function block | TIC_A4I |
| _A5 | copy operation from a array to a simple variable | TIC_A5B |
| _A6 | copy operation from a simple variable to an array | TIC_A6R |
| _C1 | conditional jump | TIC_C1B |
| _C2 | conditional jump | TIC_C2B |
| _I1 | unconditional jump | TIC_I1 |
| _I2 | unconditional jump | TIC_I2 |
| _L1 | label | TIC_L1 |
| _P1 | parameter passing | TIC_P1 |
| B | Boolean instruction | TIC_A3B |
| I | integer instruction | TIC_A3I |
| R | real instruction | TIC_A3R |
| T | timer instruction | TIC_A3T |
| M | message instruction | TIC_A3M |

### Symbols

The following notation is used to describe the operation and TIC syntax

| Symbol | Comments |
| --- | --- |
| d | displacement or constant value |
| <a> | effective address of the variable a |
| #<a> | immediate data |
| label | assemble program label |

### Intel or Motorola implementation

| Size | Intel format | Motorola format |
| --- | --- | --- |
| 1 byte(1 | 1 | 1 |
| 2 bytes(12 | 12 | 21 |
| 4 bytes(1234 | 1234 | 4321 |

## Basic instructions

The basic instructions performing single operations between variables are detailed below.

### Integer instructions

| TIC_A1SI | Integer Negation | TIC_A1SI |
| --- | --- | --- |

Operation : 	0 - <a2> ( <a1>

TIC syntax :	<a1> = - <a2>

Type :

| a1 | integer |
| --- | --- |
| a2 | integer |

Description :	Subtracts the operand <a2> from zero and stores the result in the destination location <a1>.

Format :

- Medium

| 47 | 31 | 15 |
| --- | --- | --- |
| 0x01 | a1 | a2 |
| code | destination | operand |

| TIC_A2MI | Integer Multiply | TIC_A2MI |
| --- | --- | --- |

Operation : 	<a2> * <a3> ( <a1>

TIC syntax :	<a1> = <a2> * <a3>

Type :

| a1 | integer |
| --- | --- |
| a2 | integer |
| a3 | integer |

Description :	Multiplies the two operands <a2> and <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x04 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_A2DI | Integer Divide | TIC_A2DI |
| --- | --- | --- |

Operation : 	<a2> / <a3> ( <a1>

TIC syntax :	<a1> = <a2> / <a3>

Type :

| a1 | integer |
| --- | --- |
| a2 | integer |
| a3 | integer |

Description :	Divides the operand <a2> by the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x06 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_A2AI | Integer Add | TIC_A2AI |
| --- | --- | --- |

Operation : 	<a2> + <a3> ( <a1>

TIC syntax :	<a1> = <a2> + <a3>

Type :

| a1 | integer |
| --- | --- |
| a2 | integer |
| a3 | integer |

Description :	Adds the two operands <a2> and <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x08 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_A2SI | Integer Subtract | TIC_A2SI |
| --- | --- | --- |

Operation : 	<a2> - <a3> ( <a1>

TIC syntax :	<a1> = <a2> - <a3>

Type :

| a1 | integer |
| --- | --- |
| a2 | integer |
| a3 | integer |

Description :	Subtracts the operand <a3> from the operand <a2> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x0c | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_A2LTI | Integer Test | TIC_A2LTI |
| --- | --- | --- |

Operation : 	<a2> < <a3> ( <a1>

TIC syntax :	<a1> = <a2> < <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | integer |
| a3 | integer |

Description :	Checks if the operand <a2> is less than the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x0f | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_A2GTI | Integer Test | TIC_A2GTI |
| --- | --- | --- |

Operation : 	<a2> > <a3> ( <a1>

TIC syntax :	<a1> = <a2> > <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | integer |
| a3 | integer |

Description :	Checks if the operand <a2> is greater than the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x13 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_A2LEI | Integer Test | TIC_A2LEI |
| --- | --- | --- |

Operation : 	<a2> ( <a3> ( <a1>

TIC syntax :	<a1> = <a2> <= <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | integer |
| a3 | integer |

Description :	Checks if the operand <a2> is less than or equal to the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x17 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_A2GEI | Integer Test | TIC_A2GEI |
| --- | --- | --- |

Operation : 	<a2> ( <a3> ( <a1>

TIC syntax :	<a1> = <a2> >= <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | integer |
| a3 | integer |

Description :	Checks if the operand <a2> is greater or equal than the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x1b | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_A2EQI | Integer Test | TIC_A2EQI |
| --- | --- | --- |

Operation : 	<a2> = <a3> ( <a1>

TIC syntax :	<a1> = <a2> == <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | integer |
| a3 | integer |

Description :	Checks if the operand <a2> is equal to the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x1f | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_A2NEI | Integer Test | TIC_A2NEI |
| --- | --- | --- |

Operation : 	<a2> <> <a3> ( <a1>

TIC syntax :	<a1> = <a2> != <a3>

Type :

| a1 | boolean |
| --- | --- |
| a2 | integer |
| a3 | integer |

Description :	Checks if the operand <a2> is not equal to the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x24 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_A3I | Integer Assignment | TIC_A3I |
| --- | --- | --- |

Operation : 	<a2> ( <a1>

TIC syntax :	<a1> = <a2>

Type :

| a1 | integer |
| --- | --- |
| a2 | integer |

Description :	Stores the operand <a2> in the destination location <a1>.

Format :

- Medium

| 47 | 32 | 15 |
| --- | --- | --- |
| 0x2d | a1 | a2 |
| code | destination | operand |

| TIC_A5I | Integer Assignment of array element | TIC_A5I |
| --- | --- | --- |

Operation : 	<a2> [ <a3> ] ( <a1>

TIC syntax :	<a1> = <a2> [ <a3> ]

Type :

| a1 | integer |
| --- | --- |
| a2 | integer |
| a3 | integer |

Description :	Reads an element of the index <a2> from the array <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x38 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_A6I | Integer Assignment array | TIC_A6I |
| --- | --- | --- |

Operation : 	<a3> (<a1> [ <a2> ]

TIC syntax :	<a1> [ <a2> ] = <a3>

Type :

| a1 | integer |
| --- | --- |
| a2 | integer |
| a3 | integer |

Description :	Stores <a3> in array <a1> at the index <a2>

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x3d | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_TRS_A2LTI | Integer Test | TIC_TRS_A2LTI |
| --- | --- | --- |

Operation : 	<a2> < <a3> ( <a1>

TIC syntax :	<a1> = <a2> < <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | integer |
| a3 | integer |

Description :	Checks if the operand <a2> is less than the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x4e | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_TRS_A2GTI | Integer Test | TIC_TRS_A2GTI |
| --- | --- | --- |

Operation : 	<a2> > <a3> ( <a1>

TIC syntax :	<a1> = <a2> > <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | integer |
| a3 | integer |

Description :	Checks if the operand <a2> is greater than the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x52 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_TRS_A2LEI | Integer Test | TIC_TRS_A2LEI |
| --- | --- | --- |

Operation : 	<a2> ( <a3> ( <a1>

TIC syntax :	<a1> = <a2> <= <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | integer |
| a3 | integer |

Description :	Checks if the operand <a2> is less or equal than the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x56 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_TRS_A2GEI | Integer Test | TIC_TRS_A2GEI |
| --- | --- | --- |

Operation : 	<a2> ( <a3> ( <a1>

TIC syntax :	<a1> = <a2> >= <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | integer |
| a3 | integer |

Description :	Checks if the operand <a2> is greater than or equal to the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x5a | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_TRS_A2EQI | Integer Test | TIC_TRS_A2EQI |
| --- | --- | --- |

Operation : 	<a2> = <a3> ( <a1>

TIC syntax :	<a1> = <a2> == <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | integer |
| a3 | integer |

Description :	Checks if the operand <a2> is equal to the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x5e | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_TRS_A2NEI | Integer Test | TIC_TRS_A2NEI |
| --- | --- | --- |

Operation : 	<a2> <> <a3> ( <a1>

TIC syntax :	<a1> = <a2> != <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | integer |
| a3 | integer |

Description :	Checks if the operand <a2> is not equal to the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x63 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_OUT_A1SI | Integer Negation | TIC_OUT_A1SI |
| --- | --- | --- |

Operation : 	0 - <a2> ( <a1>

TIC syntax :	<a1> = - <a2>

Type :

| a1 | integer |
| --- | --- |
| a2 | integer |

Description :	Subtracts the operand <a2> from zero and stores the result in the destination location <a1>.

Format :

- Medium

| 47 | 31 | 15 |
| --- | --- | --- |
| 0x6e | a1 | a2 |
| code | destination | operand |

| TIC_OUT_A2MI | Integer Multiply | TIC_OUT_A2MI |
| --- | --- | --- |

Operation : 	<a2> * <a3> ( <a1>

TIC syntax :	<a1> = <a2> * <a3>

Type :

| a1 | integer |
| --- | --- |
| a2 | integer |
| a3 | integer |

Description :	Multiplies the two operands <a2> and <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x71 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_OUT_A2DI | Integer Divide | TIC_OUT_A2DI |
| --- | --- | --- |

Operation : 	<a2> / <a3> ( <a1>

TIC syntax :	<a1> = <a2> / <a3>

Type :

| a1 | integer |
| --- | --- |
| a2 | integer |
| a3 | integer |

Description :	Divides the operand <a2> by the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x73 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_OUT_A2AI | Integer Add | TIC_OUT_A2AI |
| --- | --- | --- |

Operation : 	<a2> + <a3> ( <a1>

TIC syntax :	<a1> = <a2> + <a3>

Type :

| a1 | integer |
| --- | --- |
| a2 | integer |
| a3 | integer |

Description :	Adds the two operands <a2> and <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x75 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_OUT_A2SI | Integer Subtract | TIC_OUT_A2SI |
| --- | --- | --- |

Operation : 	<a2> - <a3> ( <a1>

TIC syntax :	<a1> = <a2> - <a3>

Type :

| a1 | integer |
| --- | --- |
| a2 | integer |
| a3 | integer |

Description :	Subtracts the operand <a3> from the operand <a2> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x78 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_OUT_A2LTI | Integer Test | TIC_OUT_A2LTI |
| --- | --- | --- |

Operation : 	<a2> < <a3> ( <a1>

TIC syntax :	<a1> = <a2> < <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | integer |
| a3 | integer |

Description :	Checks if the operand <a2> is less than the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x7a | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_OUT_A2GTI | Integer Test | TIC_OUT_A2GTI |
| --- | --- | --- |

Operation : 	<a2> > <a3> ( <a1>

TIC syntax :	<a1> = <a2> > <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | integer |
| a3 | integer |

Description :	Checks if the operand <a2> is greater than the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x7e | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_OUT_A2LEI | Integer Test | TIC_OUT_A2LEI |
| --- | --- | --- |

Operation : 	<a2> ( <a3> ( <a1>

TIC syntax :	<a1> = <a2> <= <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | integer |
| a3 | integer |

Description :	Checks if the operand <a2> is less or equal than the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x82 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_OUT_A2GEI | Integer Test | TIC_OUT_A2GEI |
| --- | --- | --- |

Operation : 	<a2> ( <a3> ( <a1>

TIC syntax :	<a1> = <a2> >= <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | integer |
| a3 | integer |

Description :	Checks if the operand <a2> is greater than or equal to the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x86 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_OUT_A2EQI | Integer Test | TIC_OUT_A2EQI |
| --- | --- | --- |

Operation : 	<a2> = <a3> ( <a1>

TIC syntax :	<a1> = <a2> == <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | integer |
| a3 | integer |

Description :	Checks if the operand <a2> is equal to the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x8a | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_OUT_A2NEI | Integer Test | TIC_OUT_A2NEI |
| --- | --- | --- |

Operation : 	<a2> <> <a3> ( <a1>

TIC syntax :	<a1> = <a2> != <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | integer |
| a3 | integer |

Description :	Checks if the operand <a2> is not equal to the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x8f | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_OUT_A3I | Integer Assignment | TIC_OUT_A3I |
| --- | --- | --- |

Operation : 	<a2> ( <a1>

TIC syntax :	<a1> = <a2>

Type :

| a1 | integer |
| --- | --- |
| a2 | integer |

Description : Stores the operand <a2> in the destination location <a1>.

Format :

- Medium

| 47 | 32 | 15 |
| --- | --- | --- |
| 0x98 | a1 | a2 |
| code | destination | operand |

| TIC_OUT_A5I | Integer Assignment of array element | TIC_OUT_A5I |
| --- | --- | --- |

Operation : 	<a2> [ <a3> ] ( <a1>

TIC syntax :	<a1> = <a2> [ <a3> ]

Type :

| a1 | integer |
| --- | --- |
| a2 | integer |
| a3 | integer |

Description :	Reads an element of the index <a2> from the array <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0xa2 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_OUT_A6I | Integer Assignment array | TIC_OUT_A6I |
| --- | --- | --- |

Operation : 	<a3> (<a1> [ <a2> ]

TIC syntax :	<a1> [ <a2> ] = <a3>

Type :

| a1 | integer |
| --- | --- |
| a2 | integer |
| a3 | integer |

Description :	Stores <a3> in array <a1> at the index <a2>

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0xa7 | a1 | a2 | a3 |
| code | destination | operand | operand |

### Real instructions

| TIC_A1SR | Real Negation | TIC_A1SR |
| --- | --- | --- |

Operation : 	0 - <a2> ( <a1>

TIC syntax :	<a1> = - <a2>

Type :

| a1 | Real |
| --- | --- |
| a2 | Real |

Description :	Subtracts the operand <a2> from zero and stores the result in the destination location <a1>.

Format :

- Medium

| 47 | 31 | 15 |
| --- | --- | --- |
| 0x02 | a1 | a2 |
| code | destination | operand |

| TIC_A2MR | Real Multiply | TIC_A2MR |
| --- | --- | --- |

Operation : 	<a2> * <a3> ( <a1>

TIC syntax :	<a1> = <a2> * <a3>

Type :

| a1 | Real |
| --- | --- |
| a2 | Real |
| a3 | Real |

Description :	Multiplies the two operands <a2> and <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x05 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_A2DR | Real Divide | TIC_A2DR |
| --- | --- | --- |

Operation : 	<a2> / <a3> ( <a1>

TIC syntax :	<a1> = <a2> / <a3>

Type :

| a1 | Real |
| --- | --- |
| a2 | Real |
| a3 | Real |

Description :	Divides the operand <a2> by the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x07 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_A2AR | Real Add | TIC_A2AR |
| --- | --- | --- |

Operation : 	<a2> + <a3> ( <a1>

TIC syntax :	<a1> = <a2> + <a3>

Type :

| a1 | Real |
| --- | --- |
| a2 | Real |
| a3 | Real |

Description :	Adds the two operands <a2> and <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x09 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_A2SR | Real Subtract | TIC_A2SR |
| --- | --- | --- |

Operation : 	<a2> - <a3> ( <a1>

TIC syntax :	<a1> = <a2> - <a3>

Type :

| a1 | Real |
| --- | --- |
| a2 | Real |
| a3 | Real |

Description :	Subtracts the operand <a3> from the operand <a2> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x0d | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_A2LTR | Real Test | TIC_A2LTR |
| --- | --- | --- |

Operation : 	<a2> < <a3> ( <a1>

TIC syntax :	<a1> = <a2> < <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | Real |
| a3 | Real |

Description :	Checks if the operand <a2> is less than the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x10 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_A2GTR | Real Test | TIC_A2GTR |
| --- | --- | --- |

Operation : 	<a2> > <a3> ( <a1>

TIC syntax :	<a1> = <a2> > <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | Real |
| a3 | Real |

Description :	Checks if the operand <a2> is greater than the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x14 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_A2LER | Real Test | TIC_A2LER |
| --- | --- | --- |

Operation : 	<a2> ( <a3> ( <a1>

TIC syntax :	<a1> = <a2> <= <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | Real |
| a3 | Real |

Description :	Checks if the operand <a2> is less than or equal to the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x18 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_A2GER | Real Test | TIC_A2GER |
| --- | --- | --- |

Operation : 	<a2> ( <a3> ( <a1>

TIC syntax :	<a1> = <a2> >= <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | Real |
| a3 | Real |

Description :	Checks if the operand <a2> is greater than or equal to the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x1c | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_A2EQR | Real Test | TIC_A2EQR |
| --- | --- | --- |

Operation : 	<a2> = <a3> ( <a1>

TIC syntax :	<a1> = <a2> == <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | Real |
| a3 | Real |

Description :	Checks if the operand <a2> is equal to the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x20 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_A2NER | Real Test | TIC_A2NER |
| --- | --- | --- |

Operation : 	<a2> <> <a3> ( <a1>

TIC syntax :	<a1> = <a2> != <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | Real |
| a3 | Real |

Description :	Checks if the operand <a2> is not equal to the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x25 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_A3R | Real Assignment | TIC_A3R |
| --- | --- | --- |

Operation : 	<a2> ( <a1>

TIC syntax :	<a1> = <a2>

Type :

| a1 | Real |
| --- | --- |
| a2 | Real |

Description :	Stores the operand <a2> in the destination location <a1>.

Format :

- Medium

| 47 | 32 | 15 |
| --- | --- | --- |
| 0x2e | a1 | a2 |
| code | destination | operand |

| TIC_A5R | Real Assignment of array element | TIC_A5R |
| --- | --- | --- |

Operation : 	<a2> [ <a3> ] ( <a1>

TIC syntax :	<a1> = <a2> [ <a3> ]

Type :

| a1 | Real |
| --- | --- |
| a2 | integer |
| a3 | integer |

Description :	Reads an element of the index <a2> from the array <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x39 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_A6R | Real Assignment array | TIC_A6R |
| --- | --- | --- |

Operation : 	<a3> (<a1> [ <a2> ]

TIC syntax :	<a1> [ <a2> ] = <a3>

Type :

| a1 | integer |
| --- | --- |
| a2 | integer |
| a3 | Real |

Description :	Stores <a3> in array <a1> at the index <a2>

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x3e | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_TRS_A2LTR | Real Test | TIC_TRS_A2LTR |
| --- | --- | --- |

Operation : 	<a2> < <a3> ( <a1>

TIC syntax :	<a1> = <a2> < <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | Real |
| a3 | Real |

Description :	Checks if the operand <a2> is less than the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x4f | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_TRS_A2GTR | Real Test | TIC_TRS_A2GTR |
| --- | --- | --- |

Operation : 	<a2> > <a3> ( <a1>

TIC syntax :	<a1> = <a2> > <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | Real |
| a3 | Real |

Description :	Checks if the operand <a2> is greater than the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x53 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_TRS_A2LER | Real Test | TIC_TRS_A2LER |
| --- | --- | --- |

Operation : 	<a2> ( <a3> ( <a1>

TIC syntax :	<a1> = <a2> <= <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | Real |
| a3 | Real |

Description :	Checks if the operand <a2> is less than or equal to the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x57 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_TRS_A2GER | Real Test | TIC_TRS_A2GER |
| --- | --- | --- |

Operation : 	<a2> ( <a3> ( <a1>

TIC syntax :	<a1> = <a2> >= <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | Real |
| a3 | Real |

Description :	Checks if the operand <a2> is greater than or equal to the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x5b | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_TRS_A2EQR | Real Test | TIC_TRS_A2EQR |
| --- | --- | --- |

Operation : 	<a2> = <a3> ( <a1>

TIC syntax :	<a1> = <a2> == <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | Real |
| a3 | Real |

Description :	Checks if the operand <a2> is equal to the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x5f | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_TRS_A2NER | Real Test | TIC_TRS_A2NER |
| --- | --- | --- |

Operation : 	<a2> <> <a3> ( <a1>

TIC syntax :	<a1> = <a2> != <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | Real |
| a3 | Real |

Description :	Checks if the operand <a2> is not equal to the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x64 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_OUT_A1SR | Real Negation | TIC_OUT_A1SR |
| --- | --- | --- |

Operation : 	0 - <a2> ( <a1>

TIC syntax :	<a1> = - <a2>

Type :

| a1 | Real |
| --- | --- |
| a2 | Real |

Description :	Subtracts the operand <a2> from zero and stores the result in the destination location <a1>.

Format :

- Medium

| 47 | 31 | 15 |
| --- | --- | --- |
| 0x6f | a1 | a2 |
| code | destination | operand |

| TIC_OUT_A2MR | Real Multiply | TIC_OUT_A2MR |
| --- | --- | --- |

Operation : 	<a2> * <a3> ( <a1>

TIC syntax :	<a1> = <a2> * <a3>

Type :

| a1 | Real |
| --- | --- |
| a2 | Real |
| a3 | Real |

Description :	Multiplies the two operands <a2> and <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x72 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_OUT_A2DR | Real Divide | TIC_OUT_A2DR |
| --- | --- | --- |

Operation : 	<a2> / <a3> ( <a1>

TIC syntax :	<a1> = <a2> / <a3>

Type :

| a1 | Real |
| --- | --- |
| a2 | Real |
| a3 | Real |

Description :	Divides the operand <a2> by the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x74 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_OUT_A2AR | Real Add | TIC_OUT_A2AR |
| --- | --- | --- |

Operation : 	<a2> + <a3> ( <a1>

TIC syntax :	<a1> = <a2> + <a3>

Type :

| a1 | Real |
| --- | --- |
| a2 | Real |
| a3 | Real |

Description :	Adds the two operands <a2> and <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x76 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_OUT_A2SR | Real Subtract | TIC_OUT_A2SR |
| --- | --- | --- |

Operation : 	<a2> - <a3> ( <a1>

TIC syntax :	<a1> = <a2> - <a3>

Type :

| a1 | Real |
| --- | --- |
| a2 | Real |
| a3 | Real |

Description :	Subtracts the operand <a3> from the operand <a2> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x79 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_OUT_A2LTR | Real Test | TIC_OUT_A2LTR |
| --- | --- | --- |

Operation : 	<a2> < <a3> ( <a1>

TIC syntax :	<a1> = <a2> < <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | Real |
| a3 | Real |

Description :	Checks if the operand <a2> is less than the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x7b | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_OUT_A2GTR | Real Test | TIC_OUT_A2GTR |
| --- | --- | --- |

Operation : 	<a2> > <a3> ( <a1>

TIC syntax :	<a1> = <a2> > <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | Real |
| a3 | Real |

Description :	Checks if the operand <a2> is greater than the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x7f | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_OUT_A2LER | Real Test | TIC_OUT_A2LER |
| --- | --- | --- |

Operation : 	<a2> ( <a3> ( <a1>

TIC syntax :	<a1> = <a2> <= <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | Real |
| a3 | Real |

Description :	Checks if the operand <a2> is less than or equal to the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x83 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_OUT_A2GER | Real Test | TIC_OUT_A2GER |
| --- | --- | --- |

Operation : 	<a2> ( <a3> ( <a1>

TIC syntax :	<a1> = <a2> >= <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | Real |
| a3 | Real |

Description :	Checks if the operand <a2> is greater than or equal to the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x87 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_OUT_A2EQR | Real Test | TIC_OUT_A2EQR |
| --- | --- | --- |

Operation : 	<a2> = <a3> ( <a1>

TIC syntax :	<a1> = <a2> == <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | Real |
| a3 | Real |

Description :	Checks if the operand <a2> is equal to the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x8b | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_OUT_A2NER | Real Test | TIC_OUT_A2NER |
| --- | --- | --- |

Operation : 	<a2> <> <a3> ( <a1>

TIC syntax :	<a1> = <a2> != <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | Real |
| a3 | Real |

Description :	Checks if the operand <a2> is not equal to the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x90 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_OUT_A3R | Real Assignment | TIC_OUT_A3R |
| --- | --- | --- |

Operation : 	<a2> ( <a1>

TIC syntax :	<a1> = <a2>

Type :

| a1 | Real |
| --- | --- |
| a2 | Real |

Description :	Stores the operand <a2> in the destination location <a1>.

Format :

- Medium

| 47 | 32 | 15 |
| --- | --- | --- |
| 0x99 | a1 | a2 |
| code | destination | operand |

| TIC_OUT_A5R | Real Assignment of array element | TIC_OUT_A5R |
| --- | --- | --- |

Operation : 	<a2> [ <a3> ] ( <a1>

TIC syntax :	<a1> = <a2> [ <a3> ]

Type :

| a1 | Real |
| --- | --- |
| a2 | integer |
| a3 | integer |

Description :	Reads an element of the index <a2> from the array <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0xa3 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_OUT_A6R | Real Assignment array | TIC_OUT_A6R |
| --- | --- | --- |

Operation : 	<a3> (<a1> [ <a2> ]

TIC syntax :	<a1> [ <a2> ] = <a3>

Type :

| a1 | integer |
| --- | --- |
| a2 | integer |
| a3 | Real |

Description :	Stores <a3> in array <a1> at the index <a2>

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0xa8 | a1 | a2 | a3 |
| code | destination | operand | operand |

### Boolean instructions

| TIC_A1NO. | Boolean Negation | TIC_A1NO. |
| --- | --- | --- |

Operation : 	~ <a2> ( <a1>

TIC syntax :	<a1> = ! <a2>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | Boolean |

Description :	Calculates the logical-negation of the operand <a2> and stores the result in the destination location <a1>.

Format :

- Medium

| 47 | 31 | 15 |
| --- | --- | --- |
| 0x03 | a1 | a2 |
| code | destination | operand |

| TIC_A2EQB | Boolean Test | TIC_A2EQB |
| --- | --- | --- |

Operation : 	<a2> = <a3> ( <a1>

TIC syntax :	<a1> = <a2> == <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | Boolean |
| a3 | Boolean |

Description :	Checks if the operand <a2> is equal to the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x23 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_A2NEB | Boolean Test | TIC_A2NEB |
| --- | --- | --- |

Operation : 	<a2> <> <a3> ( <a1>

TIC syntax :	<a1> = <a2> != <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | Boolean |
| a3 | Boolean |

Description :	Checks if the operand <a2> is not equal to the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x28 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_A2ORB | OR Logical | TIC_A2ORB |
| --- | --- | --- |

Operation : 	<a2> OR <a3> ( <a1>

TIC syntax :	<a1> = <a2> || <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | Boolean |
| a3 | Boolean |

Description :	Performs an inclusive OR on the operand <a2> and the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x29 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_A2ANO. | AND Logical | TIC_A2ANO. |
| --- | --- | --- |

Operation : 	<a2> AND <a3> ( <a1>

TIC syntax :	<a1> = <a2> && <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | Boolean |
| a3 | Boolean |

Description :	Performs an AND operation of the operand <a2> and the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x2a | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_A2XOB | Logical XOR | TIC_A2XOB |
| --- | --- | --- |

Operation : 	<a2> XOR <a3> ( <a1>

TIC syntax :	<a1> = <a2> ^^ <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | Boolean |
| a3 | Boolean |

Description :	Performs an exclusive OR on the operand <a2> and the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x2b | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_A3B | Boolean Assignment | TIC_A3B |
| --- | --- | --- |

Operation : 	<a2> ( <a1>

TIC syntax :	<a1> = <a2>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | Boolean |

Description :	Stores the operand <a2> in the destination location <a1>.

Format :

- Medium

| 47 | 32 | 15 |
| --- | --- | --- |
| 0x2c | a1 | a2 |
| code | destination | operand |

| TIC_A5B | Boolean Assignment of array element | TIC_A5B |
| --- | --- | --- |

Operation : 	<a2> [ <a3> ] ( <a1>

TIC syntax :	<a1> = <a2> [ <a3> ]

Type :

| a1 | Boolean |
| --- | --- |
| a2 | integer |
| a3 | integer |

Description :	Reads an element of the index <a2> from the array <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x37 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_A6B | Boolean Assignment array | TIC_A6B |
| --- | --- | --- |

Operation : 	<a3> (<a1> [ <a2> ]

TIC syntax :	<a1> [ <a2> ] = <a3>

Type :

| a1 | integer |
| --- | --- |
| a2 | integer |
| a3 | Boolean |

Description :	Stores <a3> in array <a1> at the index <a2>

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x3c | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_TRS_A1NO. | Boolean Negation | TIC_TRS_A1NO. |
| --- | --- | --- |

Operation : 	~ <a2> ( <a1>

TIC syntax :	<a1> = ! <a2>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | Boolean |

Description :	Calculates the logical-negation of the operand <a2> and stores the result in the destination location <a1>.

Format :

- Medium

| 47 | 31 | 15 |
| --- | --- | --- |
| 0x4d | a1 | a2 |
| code | destination | operand |

| TIC_TRS_A2EQB | Boolean Test | TIC_TRS_A2EQB |
| --- | --- | --- |

Operation : 	<a2> = <a3> ( <a1>

TIC syntax :	<a1> = <a2> == <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | Boolean |
| a3 | Boolean |

Description :	Checks if the operand <a2> is equal to the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x62 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_TRS_A2NEB | Boolean Test | TIC_TRS_A2NEB |
| --- | --- | --- |

Operation : 	<a2> <> <a3> ( <a1>

TIC syntax :	<a1> = <a2> != <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | Boolean |
| a3 | Boolean |

Description :	Checks if the operand <a2> is not equal to the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x67 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_TRS_A2ORB | OR Logical | TIC_TRS_A2ORB |
| --- | --- | --- |

Operation : 	<a2> OR <a3> ( <a1>

TIC syntax :	<a1> = <a2> || <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | Boolean |
| a3 | Boolean |

Description :	Performs an inclusive OR on the operand <a2> and the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x68 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_TRS_A2ANO. | AND Logical | TIC_TRS_A2ANO. |
| --- | --- | --- |

Operation : 	<a2> AND <a3> ( <a1>

TIC syntax :	<a1> = <a2> && <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | Boolean |
| a3 | Boolean |

Description :	Performs an AND operation on the operand <a2> and the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x69 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_TRS_A2XOB | Logical XOR | TIC_TRS_A2XOB |
| --- | --- | --- |

Operation : 	<a2> XOR <a3> ( <a1>

TIC syntax :	<a1> = <a2> ^^ <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | Boolean |
| a3 | Boolean |

Description :	Performs an exclusive OR on the operand <a2> and the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x6a | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_TRS_A3B | Boolean Assignment | TIC_TRS_A3B |
| --- | --- | --- |

Operation : 	<a2> ( <a1>

TIC syntax :	<a1> = <a2>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | Boolean |

Description :	Stores the operand <a2> in the destination location <a1>.

Format :

- Medium

| 47 | 32 | 15 |
| --- | --- | --- |
| 0x6b | a1 | a2 |
| code | destination | operand |

| TIC_TRS_A5B | Boolean Assignment of array element | TIC_TRS_A5B |
| --- | --- | --- |

Operation : 	<a2> [ <a3> ] ( <a1>

TIC syntax :	<a1> = <a2> [ <a3> ]

Type :

| a1 | Boolean |
| --- | --- |
| a2 | integer |
| a3 | integer |

Description :	Reads an element of the index <a2> from the array <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x6d | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_OUT_A1NO. | Boolean Negation | TIC_OUT_A1NO. |
| --- | --- | --- |

Operation : 	~ <a2> ( <a1>

TIC syntax :	<a1> = ! <a2>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | Boolean |

Description :	Calculates the logical-negation of the operand <a2> and stores the result in the destination location <a1>.

Format :

- Medium

| 47 | 31 | 15 |
| --- | --- | --- |
| 0x70 | a1 | a2 |
| code | destination | operand |

| TIC_OUT_A2EQB | Boolean Test | TIC_OUT_A2EQB |
| --- | --- | --- |

Operation : 	<a2> = <a3> ( <a1>

TIC syntax :	<a1> = <a2> == <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | Boolean |
| a3 | Boolean |

Description :	Checks if the operand <a2> is equal to the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x8d | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_OUT_A2NEB | Boolean Test | TIC_OUT_A2NEB |
| --- | --- | --- |

Operation : 	<a2> <> <a3> ( <a1>

TIC syntax :	<a1> = <a2> != <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | Boolean |
| a3 | Boolean |

Description :	Checks if the operand <a2> is not equal to the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x92 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_OUT_A2ORB | OR Logical | TIC_OUT_A2ORB |
| --- | --- | --- |

Operation : 	<a2> OR <a3> ( <a1>

TIC syntax :	<a1> = <a2> || <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | Boolean |
| a3 | Boolean |

Description :	Performs an inclusive OR on the operand <a2> and the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x94 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_OUT_A2ANO. | AND Logical | TIC_OUT_A2ANO. |
| --- | --- | --- |

Operation : 	<a2> AND <a3> ( <a1>

TIC syntax :	<a1> = <a2> && <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | Boolean |
| a3 | Boolean |

Description :	Performs an AND operation on the operand <a2> and the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x95 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_OUT_A2XOB | Logical XOR | TIC_OUT_A2XOB |
| --- | --- | --- |

Operation : 	<a2> XOR <a3> ( <a1>

TIC syntax :	<a1> = <a2> ^^ <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | Boolean |
| a3 | Boolean |

Description :	Performs an exclusive OR on the operand <a2> and the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x96 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_OUT_A3B | Boolean Assignment | TIC_OUT_A3B |
| --- | --- | --- |

Operation : 	<a2> ( <a1>

TIC syntax :	<a1> = <a2>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | Boolean |

Description :	Stores the operand <a2> in the destination location <a1>.

Format :

- Medium

| 47 | 32 | 15 |
| --- | --- | --- |
| 0x97 | a1 | a2 |
| code | destination | operand |

| TIC_OUT_A5B | Boolean Assignment of array element | TIC_OUT_A5B |
| --- | --- | --- |

Operation : 	<a2> [ <a3> ] ( <a1>

TIC syntax :	<a1> = <a2> [ <a3> ]

Type :

| a1 | Boolean |
| --- | --- |
| a2 | integer |
| a3 | integer |

Description :	Reads an element of the index <a2> from the array <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0xa1 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_OUT_A6B | Boolean Assignment array | TIC_OUT_A6B |
| --- | --- | --- |

Operation : 	<a3> (<a1> [ <a2> ]

TIC syntax :	<a1> [ <a2> ] = <a3>

Type :

| a1 | integer |
| --- | --- |
| a2 | integer |
| a3 | Boolean |

Description :	Stores <a3> in array <a1> at the index <a2>

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0xa6 | a1 | a2 | a3 |
| code | destination | operand | operand |

### Message instructions

For further information on the operations on the messages variables refers to ISaGRAF Guide.

| TIC_A2AM | Message Add | TIC_A2AM |
| --- | --- | --- |

Operation : 	<a2> + <a3> ( <a1>

TIC syntax :	<a1> = <a2> + <a3>

Type :

| a1 | message |
| --- | --- |
| a2 | message |
| a3 | message |

Description :	Adds the two operands <a2> and <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x0b | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_A2LTM | Message Test | TIC_A2LTM |
| --- | --- | --- |

Operation : 	<a2> < <a3> ( <a1>

TIC syntax :	<a1> = <a2> < <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | message |
| a3 | message |

Description :	Checks if the operand <a2> is less than the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x12 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_A2GTM | Message Test | TIC_A2GTM |
| --- | --- | --- |

Operation : 	<a2> > <a3> ( <a1>

TIC syntax :	<a1> = <a2> > <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | message |
| a3 | message |

Description :	Checks if the operand <a2> is greater than the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x16 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_A2LEM | Message Test | TIC_A2LEM |
| --- | --- | --- |

Operation : 	<a2> ( <a3> ( <a1>

TIC syntax :	<a1> = <a2> <= <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | message |
| a3 | message |

Description :	Checks if the operand <a2> is less than or equal to the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x1a | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_A2GEM | Message Test | TIC_A2GEM |
| --- | --- | --- |

Operation : 	<a2> ( <a3> ( <a1>

TIC syntax :	<a1> = <a2> >= <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | message |
| a3 | message |

Description :	Checks if the operand <a2> is greater than or equal to the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x1e | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_A2EQM | Message Test | TIC_A2EQM |
| --- | --- | --- |

Operation : 	<a2> = <a3> ( <a1>

TIC syntax :	<a1> = <a2> == <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | message |
| a3 | message |

Description :	Checks if the operand <a2> is equal to the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x22 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_A2NEM | Message Test | TIC_A2NEM |
| --- | --- | --- |

Operation : 	<a2> <> <a3> ( <a1>

TIC syntax :	<a1> = <a2> != <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | message |
| a3 | message |

Description :	Checks if the operand <a2> is not equal to the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x27 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_A3M | Message Assignment | TIC_A3M |
| --- | --- | --- |

Operation : 	<a2> ( <a1>

TIC syntax :	<a1> = <a2>

Type :

| a1 | message |
| --- | --- |
| a2 | message |

Description :	Stores the operand <a2> in the destination location <a1>.

Format :

- Medium

| 47 | 32 | 15 |
| --- | --- | --- |
| 0x30 | a1 | a2 |
| code | destination | operand |

| TIC_A5M | Message Assignment of array element | TIC_A5M |
| --- | --- | --- |

Operation : 	<a2> [ <a3> ] ( <a1>

TIC syntax :	<a1> = <a2> [ <a3> ]

Type :

| a1 | Message |
| --- | --- |
| a2 | integer |
| a3 | integer |

Description :	Reads an element at index <a2> of the array <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x3b | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_A6M | Message Assignment array | TIC_A6M |
| --- | --- | --- |

Operation : 	<a3> (<a1> [ <a2> ]

TIC syntax :	<a1> [ <a2> ] = <a3>

Type :

| a1 | integer |
| --- | --- |
| a2 | integer |
| a3 | Message |

Description :	Stores <a3> in array <a1> at the index <a2>

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x40 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_TRS_A2LTM | Message Test | TIC_TRS_A2LTM |
| --- | --- | --- |

Operation : 	<a2> < <a3> ( <a1>

TIC syntax :	<a1> = <a2> < <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | message |
| a3 | message |

Description :	Checks if the operand <a2> is less than the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x51 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_TRS_A2GTM | Message Test | TIC_TRS_A2GTM |
| --- | --- | --- |

Operation : 	<a2> > <a3> ( <a1>

TIC syntax :	<a1> = <a2> > <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | message |
| a3 | message |

Description :	Checks if the operand <a2> is greater than the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x55 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_TRS_A2LEM | Message Test | TIC_TRS_A2LEI |
| --- | --- | --- |

Operation : 	<a2> ( <a3> ( <a1>

TIC syntax :	<a1> = <a2> <= <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | message |
| a3 | message |

Description :	Checks if the operand <a2> is less than or equal to the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x59 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_TRS_A2GEM | Message Test | TIC_TRS_A2GEM |
| --- | --- | --- |

Operation : 	<a2> ( <a3> ( <a1>

TIC syntax :	<a1> = <a2> >= <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | message |
| a3 | message |

Description :	Checks if the operand <a2> is greater than or equal to the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x5d | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_TRS_A2EQM | Message Test | TIC_TRS_A2EQM |
| --- | --- | --- |

Operation : 	<a2> = <a3> ( <a1>

TIC syntax :	<a1> = <a2> == <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | message |
| a3 | message |

Description :	Checks if the operand <a2> is equal to the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x61 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_TRS_A2NEM | Message Test | TIC_TRS_A2NEM |
| --- | --- | --- |

Operation : 	<a2> <> <a3> ( <a1>

TIC syntax :	<a1> = <a2> != <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | message |
| a3 | message |

Description :	Checks if the operand <a2> is not equal to the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x66 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_OUT_A2AM | Message Add | TIC_OUT_A2AM |
| --- | --- | --- |

Operation : 	<a2> + <a3> ( <a1>

TIC syntax :	<a1> = <a2> + <a3>

Type :

| a1 | message |
| --- | --- |
| a2 | message |
| a3 | message |

Description :	Adds the two operands <a2> and <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x77 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_OUT_A2LTM | Message Test | TIC_OUT_A2LTM |
| --- | --- | --- |

Operation : 	<a2> < <a3> ( <a1>

TIC syntax :	<a1> = <a2> < <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | message |
| a3 | message |

Description :	Checks if the operand <a2> is less than the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x7c | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_OUT_A2GTM | Message Test | TIC_OUT_A2GTM |
| --- | --- | --- |

Operation : 	<a2> > <a3> ( <a1>

TIC syntax :	<a1> = <a2> > <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | message |
| a3 | message |

Description :	Checks if the operand <a2> is greater than the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x80 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_OUT_A2LEM | Message Test | TIC_OUT_A2LEM |
| --- | --- | --- |

Operation : 	<a2> ( <a3> ( <a1>

TIC syntax :	<a1> = <a2> <= <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | message |
| a3 | message |

Description :	Checks if the operand <a2> is less than or equal to the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x84 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_OUT_A2GEM | Message Test | TIC_OUT_A2GEM |
| --- | --- | --- |

Operation : 	<a2> ( <a3> ( <a1>

TIC syntax :	<a1> = <a2> >= <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | message |
| a3 | message |

Description :	Checks if the operand <a2> is greater than or equal to the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x88 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_OUT_A2EQM | Message Test | TIC_OUT_A2EQM |
| --- | --- | --- |

Operation : 	<a2> = <a3> ( <a1>

TIC syntax :	<a1> = <a2> == <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | message |
| a3 | message |

Description :	Checks if the operand <a2> is equal to the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x8c | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_OUT_A2NEM | Message Test | TIC_OUT_A2NEM |
| --- | --- | --- |

Operation : 	<a2> <> <a3> ( <a1>

TIC syntax :	<a1> = <a2> != <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | message |
| a3 | message |

Description :	Checks if the operand <a2> is not equal to the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x91 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_OUT_A3M | Message Assignment | TIC_OUT_A3M |
| --- | --- | --- |

Operation : 	<a2> ( <a1>

TIC syntax :	<a1> = <a2>

Type :

| a1 | message |
| --- | --- |
| a2 | message |

Description : Stores the operand <a2> in the destination location <a1>.

Format :

- Medium

| 47 | 32 | 15 |
| --- | --- | --- |
| 0x9a | a1 | a2 |
| code | destination | operand |

| TIC_OUT_A5M | Message Assignment of array element | TIC_OUT_A5M |
| --- | --- | --- |

Operation : 	<a2> [ <a3> ] ( <a1>

TIC syntax :	<a1> = <a2> [ <a3> ]

Type :

| a1 | Message |
| --- | --- |
| a2 | integer |
| a3 | integer |

Description :	Reads an element of the index <a2> from the array <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0xa4 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_OUT_A6M | Message Assignment array | TIC_OUT_A6M |
| --- | --- | --- |

Operation : 	<a3> (<a1> [ <a2> ]

TIC syntax :	<a1> [ <a2> ] = <a3>

Type :

| a1 | integer |
| --- | --- |
| a2 | integer |
| a3 | Message |

Description :	Stores <a3> in array <a1> at the index <a2>

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0xa9 | a1 | a2 | a3 |
| code | destination | operand | operand |

### Timer instructions

| TIC_A2AT | Timer Add | TIC_A2AT |
| --- | --- | --- |

Operation : 	<a2> + <a3> ( <a1>

TIC syntax :	<a1> = <a2> + <a3>

Type :

| a1 | timer |
| --- | --- |
| a2 | timer |
| a3 | timer |

Description :	Adds the two operands <a2> and <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x0a | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_A2ST | Timer Subtract | TIC_A2ST |
| --- | --- | --- |

Operation : 	<a2> - <a3> ( <a1>

TIC syntax :	<a1> = <a2> - <a3>

Type :

| a1 | timer |
| --- | --- |
| a2 | timer |
| a3 | timer |

Description :	Subtracts the operand <a3> from the operand <a2> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x0e | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_A2LTT | Timer Test | TIC_A2LTT |
| --- | --- | --- |

Operation : 	<a2> < <a3> ( <a1>

TIC syntax :	<a1> = <a2> < <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | timer |
| a3 | timer |

Description :	Checks if the operand <a2> is less than the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x11 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_A2GTT | Timer Test | TIC_A2GTT |
| --- | --- | --- |

Operation : 	<a2> > <a3> ( <a1>

TIC syntax :	<a1> = <a2> > <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | timer |
| a3 | timer |

Description :	Checks if the operand <a2> is greater than the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x15 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_A2LET | Timer Test | TIC_A2LET |
| --- | --- | --- |

Operation : 	<a2> ( <a3> ( <a1>

TIC syntax :	<a1> = <a2> <= <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | timer |
| a3 | timer |

Description :	Checks if the operand <a2> is less than or equal to the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x19 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_A2GET | Timer Test | TIC_A2GET |
| --- | --- | --- |

Operation : 	<a2> ( <a3> ( <a1>

TIC syntax :	<a1> = <a2> >= <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | timer |
| a3 | timer |

Description :	Checks if the operand <a2> is greater than or equal to the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x1d | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_A2EQT | Timer Test | TIC_A2EQT |
| --- | --- | --- |

Operation : 	<a2> = <a3> ( <a1>

TIC syntax :	<a1> = <a2> == <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | timer |
| a3 | timer |

Description :	Checks if the operand <a2> is equal to the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x21 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_A2NET | Timer Test | TIC_A2NET |
| --- | --- | --- |

Operation : 	<a2> <> <a3> ( <a1>

TIC syntax :	<a1> = <a2> != <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | timer |
| a3 | timer |

Description :	Checks if the operand <a2> is not equal to the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x26 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_A3T | Timer Assignment | TIC_A3T |
| --- | --- | --- |

Operation : 	<a2> ( <a1>

TIC syntax :	<a1> = <a2>

Type :

| a1 | timer |
| --- | --- |
| a2 | timer |

Description : Stores the operand <a2> in the destination location <a1>.

Format :

- Medium

| 47 | 32 | 15 |
| --- | --- | --- |
| 0x2f | a1 | a2 |
| code | destination | operand |

| TIC_A5T | Timer Assignment of array element | TIC_A5T |
| --- | --- | --- |

Operation : 	<a2> [ <a3> ] ( <a1>

TIC syntax :	<a1> = <a2> [ <a3> ]

Type :

| a1 | Timer |
| --- | --- |
| a2 | integer |
| a3 | integer |

Description :	Reads an element of the index <a2> from the array <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x3a | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_A6T | Timer Assignment array | TIC_A6T |
| --- | --- | --- |

Operation : 	<a3> (<a1> [ <a2> ]

TIC syntax :	<a1> [ <a2> ] = <a3>

Type :

| a1 | integer |
| --- | --- |
| a2 | integer |
| a3 | Timer |

Description :	Stores <a3> in array <a1> at the index <a2>

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x3f | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_TRS_A2LTT | Timer Test | TIC_TRS_A2LTT |
| --- | --- | --- |

Operation : 	<a2> < <a3> ( <a1>

TIC syntax :	<a1> = <a2> < <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | timer |
| a3 | timer |

Description :	Checks if the operand <a2> is less than the operand <a3> and stores the result in the destination location <a1>

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x50 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_TRS_A2GTT | Timer Test | TIC_TRS_A2GTT |
| --- | --- | --- |

Operation : 	<a2> > <a3> ( <a1>

TIC syntax :	<a1> = <a2> > <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | timer |
| a3 | timer |

Description :	Checks if the operand <a2> is greater than the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x54 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_TRS_A2LET | Timer Test | TIC_TRS_A2LET |
| --- | --- | --- |

Operation : 	<a2> ( <a3> ( <a1>

TIC syntax :	<a1> = <a2> <= <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | timer |
| a3 | timer |

Description :	Checks if the operand <a2> is less than or equal to the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x58 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_TRS_A2GET | Timer Test | TIC_TRS_A2GEI |
| --- | --- | --- |

Operation : 	<a2> ( <a3> ( <a1>

TIC syntax :	<a1> = <a2> >= <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | timer |
| a3 | timer |

Description :	Checks if the operand <a2> is greater than or equal to the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x5c | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_TRS_A2EQT | Timer Test | TIC_TRS_A2EQT |
| --- | --- | --- |

Operation : 	<a2> = <a3> ( <a1>

TIC syntax :	<a1> = <a2> == <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | timer |
| a3 | timer |

Description :	Checks if the operand <a2> is equal to the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x60 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_TRS_A2NET | Timer Test | TIC_TRS_A2NET |
| --- | --- | --- |

Operation : 	<a2> <> <a3> ( <a1>

TIC syntax :	<a1> = <a2> != <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | timer |
| a3 | timer |

Description :	Checks if the operand <a2> is not equal to the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x65 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_OUT_A2LTT | Timer Test | TIC_OUT_A2LTT |
| --- | --- | --- |

Operation : 	<a2> < <a3> ( <a1>

TIC syntax :	<a1> = <a2> < <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | timer |
| a3 | timer |

Description :	Checks if the operand <a2> is less than the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x7d | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_OUT_A2GTT | Timer Test | TIC_OUT_A2GTT |
| --- | --- | --- |

Operation : 	<a2> > <a3> ( <a1>

TIC syntax :	<a1> = <a2> > <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | timer |
| a3 | timer |

Description :	Checks if the operand <a2> is greater than the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x81 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_OUT_A2LET | Timer Test | TIC_OUT_A2LET |
| --- | --- | --- |

Operation : 	<a2> ( <a3> ( <a1>

TIC syntax :	<a1> = <a2> <= <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | timer |
| a3 | timer |

Description :	Checks if the operand <a2> is less than or equal to the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x85 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_OUT_A2GET | Timer Test | TIC_OUT_A2GEI |
| --- | --- | --- |

Operation : 	<a2> ( <a3> ( <a1>

TIC syntax :	<a1> = <a2> >= <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | timer |
| a3 | timer |

Description :	Checks if the operand <a2> is greater than or equal to the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x89 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_OUT_A2EQT | Timer Test | TIC_OUT_A2EQT |
| --- | --- | --- |

Operation : 	<a2> = <a3> ( <a1>

TIC syntax :	<a1> = <a2> == <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | timer |
| a3 | timer |

Description :	Checks if the operand <a2> is equal to the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x8e | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_OUT_A2NET | Timer Test | TIC_OUT_A2NET |
| --- | --- | --- |

Operation : 	<a2> <> <a3> ( <a1>

TIC syntax :	<a1> = <a2> != <a3>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | timer |
| a3 | timer |

Description :	Checks if the operand <a2> is not equal to the operand <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0x93 | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_OUT_A3T | Timer Assignment | TIC_OUT_A3T |
| --- | --- | --- |

Operation : 	<a2> ( <a1>

TIC syntax :	<a1> = <a2>

Type :

| a1 | timer |
| --- | --- |
| a2 | timer |

Description : Stores the operand <a2> in the destination location <a1>.

Format :

- Medium

| 47 | 32 | 15 |
| --- | --- | --- |
| 0x9b | a1 | a2 |
| code | destination | operand |

| TIC_OUT_A5T | Timer Assignment of array element | TIC_OUT_A5T |
| --- | --- | --- |

Operation : 	<a2> [ <a3> ] ( <a1>

TIC syntax :	<a1> = <a2> [ <a3> ]

Type :

| a1 | Timer |
| --- | --- |
| a2 | integer |
| a3 | integer |

Description :	Reads an element of the index <a2> from the array <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0xa5 | a1 | a2 | a3 |
| code | destination | operand | operand |

## Labels and jumps

The following instructions perform operations on labels. The arguments of a 'goto' instruction are signed offsets from the current code position. The argument of the instruction TIC_L1 (label marker) is not used by the target, and is reserved for future extensions.

| TIC_C1B | Conditional Jump | TIC_C1B |
| --- | --- | --- |

Operation : 	if <a1> == TRUE then goto <a2>

TIC syntax :	if <a1> goto <a2>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | integer |

Description : Compares the Boolean value <a1> with the Boolean constant TRUE. If the result is true jumps of <a2> bytes from the current position.

Format :

- Medium

| 47 | 31 | 15 |
| --- | --- | --- |
| 0x41 | a2 | a3 |
| code | operand | operand |

| TIC_C2B | Conditional Jump | TIC_C2B |
| --- | --- | --- |

Operation : 	if <a1> == FALSE then goto <a2>

TIC syntax :	if !<a1> goto <a2>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | integer |

Description : Compares the Boolean value <a1> with the Boolean constant FALSE. If the result is true the program continues at <a2> bytes from the current position.

Format :

- Medium

| 47 | 31 | 15 |
| --- | --- | --- |
| 0x42 | a2 | a3 |
| code | operand | operand |

| TIC_I1 | Unconditional Jump | TIC_I1 |
| --- | --- | --- |

Operation : 	goto <a1>

TIC syntax :	goto <a1>

Type :

| a1 | Integer |
| --- | --- |

Description : The program continues at <a1> bytes from the current position.

Format :

- Medium

| 31 | 15 |
| --- | --- |
| 0x43 | a1 |
| code | operand |

| TIC_I2 | Return | TIC_I2 |
| --- | --- | --- |

Operation : 	Restore the context of the caller

TIC syntax :	ret

Type :

| a1 | Integer |
| --- | --- |

Description : The program leaves the function and restores the context of the caller

Format :

- Medium

15

0x44

code

| TIC_L1 | Label | TIC_L1 |
| --- | --- | --- |

Operation : 	null effect

TIC syntax :	label :

Type :

Description : This instruction has no effect. It’s just a mark. The operand <a1> is  reserved for a future extension.

Format :

- Medium

| 31 | 15 |
| --- | --- |
| 0x4c | a1 |
| code | operand |

## Parameter passing instructions

The following instructions aer used in a calling program, to push parameters before calling a function or a function block.

### Integer instructions

| TIC_P1I | Integer Parameter | TIC_P1I |
| --- | --- | --- |

Operation : 	pushes <a1> in the stack

TIC syntax :	param <a1>

Type :

| a1 | integer |
| --- | --- |

Description :	Pushes the parameter <a1> in a stack or memory block.

Format :

- Medium

| 31 | 15 |
| --- | --- |
| 0x48 | a1 |
| code | operand |

### Real instructions

| TIC_P1R | Real Parameter | TIC_P1R |
| --- | --- | --- |

Operation : 	pushes <a1> in the stack

TIC syntax :	param <a1>

Type :

| a1 | Real |
| --- | --- |

Description :	Pushes the parameter <a1> in a stack or memory block.

Format :

- Medium

| 31 | 15 |
| --- | --- |
| 0x49 | a1 |
| code | operand |

### Boolean instructions

| TIC_P1B | Boolean Parameter | TIC_P1B |
| --- | --- | --- |

Operation : 	pushes <a1> in the stack

TIC syntax :	param <a1>

Type :

| a1 | Boolean |
| --- | --- |

Description :	Pushes the parameter <a1> in a stack or memory block.

Format :

- Medium

| 31 | 15 |
| --- | --- |
| 0x47 | a1 |
| code | operand |

### Message instructions

| TIC_P1M | Message Parameter | TIC_P1M |
| --- | --- | --- |

Operation : 	pushes <a1> in the stack

TIC syntax :	param <a1>

Type :

| a1 | Message |
| --- | --- |

Description :	Pushes the parameter <a1> in a stack or memory block.

Format :

- Medium

| 31 | 15 |
| --- | --- |
| 0x4b | a1 |
| code | operand |

### Timer instructions

| TIC_P1T | Timer Parameter | TIC_P1T |
| --- | --- | --- |

Operation : 	pushes <a1> in the stack

TIC syntax :	param <a1>

Type :

| a1 | Timer |
| --- | --- |

Description :	Pushes the parameter <a1> in a stack or memory block.

Format :

- Medium

| 31 | 15 |
| --- | --- |
| 0x4a | a1 |
| code | operand |

### SFC instructions

| TIC_P1C | SFC Parameter | TIC_P1C |
| --- | --- | --- |

Operation : 	pushes <a1> in the stack

TIC syntax :	param <a1>

Type :

| a1 | SFC |
| --- | --- |

Description :	Pushes the parameter <a1> which is a SFC-child in a stack or memory block.

Format :

- Medium

| 31 | 15 |
| --- | --- |
| 0x45 | a1 |
| code | operand |

| TIC_P1F | SFC Parameter | TIC_P1F |
| --- | --- | --- |

Operation : 	pushes <a1> in the stack

TIC syntax :	param <a1>

Type :

| a1 | SFC |
| --- | --- |

Description :	Pushes the parameter <a1> which is a SFC-parent in a stack or memory block.

Format :

- Medium

| 31 | 15 |
| --- | --- |
| 0x46 | a1 |
| code | operand |

| TIC_P1S | SFC Parameter | TIC_P1S |
| --- | --- | --- |

Operation : 	pushes <a1> in the stack

TIC syntax :	param <a1>

Type :

| a1 | SFC |
| --- | --- |

Description :	Pushes the parameter <a1> which is an SFC-parent in a stack or memory block.

Format :

- Medium

| 31 | 15 |
| --- | --- |
| 0xf3 | a1 |
| code | operand |

## Parameter access from a function

The following instructions occur in the body of a function written in IEC language (ST/IL/LD/FBD) to assign its return parameter. The second argument (#b) is an absolute value which indicates the order number, and is always equal to 0 for a function.

### Integer instructions

| TIC_SYS_GPARI | Integer Parameter | TIC_SYS_GPARI |
| --- | --- | --- |

Operation : 	GetPar (#<a2>) ( <a1>

TIC syntax :	<a1> = GetPar ( #<a2>)

Type :

| a1 | integer |
| --- | --- |
| a2 | integer |

Description :	Reads the parameter number <a2> in a stack or memory block and stores the result in the destination location <a1>.

Format :

- Medium

| 47 | 31 | 15 |
| --- | --- | --- |
| 0xab | a1 | a2 |
| code | destination | operand |

| TIC_SYS_PPARI | Integer Parameter | TIC_SYS_PPARI |
| --- | --- | --- |

Operation : 	PutPar (#<a2>) ( <a1>

TIC syntax :	PutPar ( <a1>,#<a2>)

Type :

| a1 | integer |
| --- | --- |
| a2 | integer |

Description :	Reads the parameter number <a2> in a stack or memory block and stores the result in the destination location <a1>.

Format :

- Medium

| 47 | 31 | 15 |
| --- | --- | --- |
| 0xb0 | a1 | a2 |
| code | destination | operand |

Notes :

In this case, #<a2> is equal to 0.

### Real instructions

| TIC_SYS_GPARR | Real Parameter | TIC_SYS_GPARR |
| --- | --- | --- |

Operation : 	GetPar (#<a2>) ( <a1>

TIC syntax :	<a1> = GetPar ( #<a2>)

Type :

| a1 | Real |
| --- | --- |
| a2 | integer |

Description :	Reads the parameter number <a2> in a stack or memory block and stores the result in the destination location <a1>.

Format :

- Medium

| 47 | 31 | 15 |
| --- | --- | --- |
| 0x | a1 | a2 |
| code | destination | operand |

| TIC_SYS_PPARR | Real Parameter | TIC_SYS_PPARR |
| --- | --- | --- |

Operation : 	PutPar (#<a2>) ( <a1>

TIC syntax :	PutPar ( <a1>,#<a2>)

Type :

| a1 | Real |
| --- | --- |
| a2 | integer |

Description :	Reads the parameter number <a2> in a stack or memory block and stores the result in the destination location <a1>.

Format :

- Medium

| 47 | 31 | 15 |
| --- | --- | --- |
| 0xb1 | a1 | a2 |
| code | destination | operand |

Notes :

In this case, #<a2> is equal to 0.

### Boolean instructions

| TIC_SYS_GPARB | Boolean Parameter | TIC_SYS_GPARB |
| --- | --- | --- |

Operation : 	GetPar (#<a2>) ( <a1>

TIC syntax :	<a1> = GetPar ( #<a2>)

Type :

| a1 | Boolean |
| --- | --- |
| a2 | integer |

Description :	Reads the parameter number <a2> in a stack or memory block and stores the result in the destination location <a1>.

Format :

- Medium

| 47 | 31 | 15 |
| --- | --- | --- |
| 0xaa | a1 | a2 |
| code | destination | operand |

| TIC_SYS_PPARB | Boolean Parameter | TIC_SYS_PPARB |
| --- | --- | --- |

Operation : 	PutPar (#<a2>) ( <a1>

TIC syntax :	PutPar ( <a1>,#<a2>)

Type :

| a1 | Boolean |
| --- | --- |
| a2 | integer |

Description :	Reads the parameter number <a2> in a stack or memory block and stores the result in the destination location <a1>.

Format :

- Medium

| 47 | 31 | 15 |
| --- | --- | --- |
| 0xaf | a1 | a2 |
| code | destination | operand |

Notes :

In this case, #<a2> is equal to 0.

### Message instructions

| TIC_SYS_GPARM | Message Parameter | TIC_SYS_GPARM |
| --- | --- | --- |

Operation : 	GetPar (#<a2>) ( <a1>

TIC syntax :	<a1> = GetPar ( #<a2>)

Type :

| a1 | message |
| --- | --- |
| a2 | integer |

Description :	Reads the parameter number <a2> in a stack or memory block and stores the result in the destination location <a1>.

Format :

- Medium

| 47 | 31 | 15 |
| --- | --- | --- |
| 0xae | a1 | a2 |
| code | destination | operand |

| TIC_SYS_PPARM | Message Parameter | TIC_SYS_PPARM |
| --- | --- | --- |

Operation : 	PutPar (#<a2>) ( <a1>

TIC syntax :	PutPar ( <a1>,#<a2>)

Type :

| a1 | Message |
| --- | --- |
| a2 | integer |

Description :	Reads the parameter number <a2> in a stack or memory block and stores the result in the destination location <a1>.

Format :

- Medium

| 47 | 31 | 15 |
| --- | --- | --- |
| 0xb3 | a1 | a2 |
| code | destination | operand |

Notes :

In this case, #<a2> is equal to 0.

### Timer instructions

| TIC_SYS_GPART | Timer Parameter | TIC_SYS_GPART |
| --- | --- | --- |

Operation : 	GetPar (#<a2>) ( <a1>

TIC syntax :	<a1> = GetPar ( #<a2>)

Type :

| a1 | timer |
| --- | --- |
| a2 | integer |

Description :	Reads the parameter number <a2> in a stack or memory block and stores the result in the destination location <a1>.

Format :

- Medium

| 47 | 31 | 15 |
| --- | --- | --- |
| 0xad | a1 | a2 |
| code | destination | operand |

| TIC_SYS_PPART | Timer Parameter | TIC_SYS_PPART |
| --- | --- | --- |

Operation : 	PutPar (#<a2>) ( <a1>

TIC syntax :	PutPar ( <a1>,#<a2>)

Type :

| a1 | Timer |
| --- | --- |
| a2 | integer |

Description :	Reads the parameter number <a2> in a stack or memory block and stores the result in the destination location <a1>.

Format :

- Medium

| 47 | 31 | 15 |
| --- | --- | --- |
| 0xb2 | a1 | a2 |
| code | destination | operand |

Notes :

In this case, #<a2> is equal to 0.

## Access to FB output parameters

The following instructions are used to access an output parameter of a called function block. A different code is used if the parameter value is used to assign an SFC transition. The second argument (#b) is an absolute value which indicates the order number of the accessed parameter. The last arguments (c and d) are the address and the instance number of a function block.

### Integer instructions

| TIC_SYS_GPARBLKI | Integer Output Parameter | TIC_SYS_GPARBLKI |
| --- | --- | --- |

Operation : 	GetFBout (#<a2>, <a3>, <a4>) ( <a1>

TIC syntax :	<a1> = GetFBout ( #<a2>,<a3>,<a4>)

Type :

| a1 | integer |
| --- | --- |
| a2 | integer |
| a3 | integer |
| a4 | integer |

Description :	Reads the output parameter number <a2> in a stack or memory block associated to the instance <a4> of the function block <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 78 | 63 | 47 | 31 | 15 |
| --- | --- | --- | --- | --- |
| 0xb6 | a1 | a2 | a3 | a4 |
| code | destination | operand | operand | operand |

### Real instructions

| TIC_SYS_GPARBLKR | Real Output Parameter | TIC_SYS_GPARBLKR |
| --- | --- | --- |

Operation : 	GetFBout (#<a2>, <a3>, #<a4>) ( <a1>

TIC syntax :	<a1> = GetFBout ( #<a2>,<a3>,#<a4>)

Type :

| a1 | Real |
| --- | --- |
| a2 | integer |
| a3 | integer |
| a4 | integer |

Description :	Reads the output parameter number <a2> in a stack or memory block associated to the instance number <a4> of the function block <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 78 | 63 | 47 | 31 | 15 |
| --- | --- | --- | --- | --- |
| 0xb7 | a1 | a2 | a3 | a4 |
| code | destination | operand | operand | operand |

### Boolean instructions

| TIC_SYS_GPARBLKB | Boolean Output Parameter | TIC_SYS_GPARBLKB |
| --- | --- | --- |

Operation : 	GetFBout (#<a2>, <a3>, #<a4>) ( <a1>

TIC syntax :	<a1> = GetFBout ( #<a2>,<a3>,#<a4>)

Type :

| a1 | Boolean |
| --- | --- |
| a2 | integer |
| a3 | integer |
| a4 | integer |

Description :	Reads the output parameter number <a2> in a stack or memory block associated to the instance number <a4> of the function block <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 78 | 63 | 47 | 31 | 15 |
| --- | --- | --- | --- | --- |
| 0xb5 | a1 | a2 | a3 | a4 |
| code | destination | operand | operand | operand |

| TIC_TRS_GPARBLKB | Boolean Output Parameter | TIC_TRS_GPARBLKB |
| --- | --- | --- |

Operation : 	GetFBout (#<a2>, <a3>, #<a4>) ( <a1>

TIC syntax :	<a1> = GetFBout ( #<a2>,<a3>,#<a4>)

Type :

| a1 | Boolean |
| --- | --- |
| a2 | integer |
| a3 | integer |
| a4 | integer |

Description :	Reads the output parameter number <a2> in a stack or memory block associated to the instance number <a4> of the function block <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 78 | 63 | 47 | 31 | 15 |
| --- | --- | --- | --- | --- |
| 0xba | a1 | a2 | a3 | a4 |
| code | destination | operand | operand | operand |

### Message instructions

| TIC_SYS_GPARBLKM | Message Output Parameter | TIC_SYS_GPARBLKM |
| --- | --- | --- |

Operation : 	GetFBout (#<a2>, <a3>, #<a4>) ( <a1>

TIC syntax :	<a1> = GetFBout ( #<a2>,<a3>,#<a4>)

Type :

| a1 | message |
| --- | --- |
| a2 | integer |
| a3 | integer |
| a4 | Integer |

Description :	Reads the output parameter number <a2> in a stack or memory block associated to the instance number <a4> of the function block <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 78 | 63 | 47 | 31 | 15 |
| --- | --- | --- | --- | --- |
| 0xb9 | a1 | a2 | a3 | a4 |
| Code | destination | operand | operand | operand |

### Timer instructions

| TIC_SYS_GPARBLKT | Timer Output Parameter | TIC_SYS_GPARBLKT |
| --- | --- | --- |

Operation : 	GetFBout (#<a2>, <a3>, #<a4>) ( <a1>

TIC syntax :	<a1> = GetFBout ( #<a2>,<a3>,#<a4>)

Type :

| a1 | integer |
| --- | --- |
| a2 | integer |
| a3 | integer |
| a4 | integer |

Description :	Reads the output parameter number <a2> in a stack or memory block associated to the instance number <a4> of the function block <a3> and stores the result in the destination location <a1>.

Format :

- Medium

| 78 | 63 | 47 | 31 | 15 |
| --- | --- | --- | --- | --- |
| 0xb8 | a1 | a2 | a3 | a4 |
| code | destination | operand | operand | operand |

## Calling function instructions

The following instructions represent a call to a user function written in an IEC language (ST, IL, LD or FBD). The calling parameters of the function have been pushed by 'param' instructions. The second argument (b) is the address of the function.

### Nil instructions

| TIC_A4N | Nil Function | TIC_A4N |
| --- | --- | --- |

Operation : 	call <a2> ( <a1>

TIC syntax :	<a1> = call <a2>

Type :

| a1 | Nil |
| --- | --- |
| a2 | Integer |

Description :	 Calls the function <a2> and stores the result in the destination location <a1>.

Format :

- Medium

| 47 | 31 | 15 |
| --- | --- | --- |
| 0x31 | a1 | a2 |
| code | destination | operand |

### Integer instructions

| TIC_A4I | Integer Function | TIC_A4I |
| --- | --- | --- |

Operation : 	call <a2> ( <a1>

TIC syntax :	<a1> = call <a2>

Type :

| a1 | integer |
| --- | --- |
| a2 | integer |

Description :	 Calls the function <a2> and stores the result in the destination location <a1>.

Format :

- Medium

| 47 | 31 | 15 |
| --- | --- | --- |
| 0x32 | a1 | a2 |
| code | destination | operand |

| TIC_OUT_A4I | Integer Function | TIC_OUT_A4I |
| --- | --- | --- |

Operation : 	call <a2> ( <a1>

TIC syntax :	<a1> = call <a2>

Type :

| a1 | integer |
| --- | --- |
| a2 | integer |

Description :	 Calls the function <a2> and stores the result in the destination location <a1>.

Format :

- Medium

| 47 | 31 | 15 |
| --- | --- | --- |
| 0x9d | a1 | a2 |
| code | destination | operand |

| TIC_USF_A4I | Integer Function | TIC_USF_A4I |
| --- | --- | --- |

Operation : 	call <a2> ( <a1>

TIC syntax :	<a1> = call <a2>

Type :

| a1 | integer |
| --- | --- |
| a2 | integer |

Description :	 Calls the function <a2> and stores the result in the destination location <a1>.

Format :

- Medium

| 47 | 31 | 15 |
| --- | --- | --- |
| 0xd3 | a1 | a2 |
| code | destination | operand |

| TIC_STD_A4I | Integer Function | TIC_STD_A4I |
| --- | --- | --- |

Operation : 	call <a2> ( <a1>

TIC syntax :	<a1> = call <a2>

Type :

| a1 | integer |
| --- | --- |
| a2 | integer |

Description :	 Calls the function <a2> and stores the result in the destination location <a1>.

Format :

- Medium

| 47 | 31 | 15 |
| --- | --- | --- |
| 0xde | a1 | a2 |
| code | destination | operand |

| TIC_USF_OUT_A4I | Integer Function | TIC_USF_OUT_A4I |
| --- | --- | --- |

Operation : 	call <a2> ( <a1>

TIC syntax :	<a1> = call <a2>

Type :

| a1 | integer |
| --- | --- |
| a2 | integer |

Description :	 Calls the function <a2> and stores the result in the destination location <a1>.

Format :

- Medium

| 47 | 31 | 15 |
| --- | --- | --- |
| 0xe4 | a1 | a2 |
| code | destination | operand |

### Real instructions

| TIC_A4R | Real Function | TIC_A4R |
| --- | --- | --- |

Operation : 	call <a2> ( <a1>

TIC syntax :	<a1> = call <a2>

Type :

| a1 | Real |
| --- | --- |
| a2 | integer |

Description :	 Calls the function <a2> and stores the result in the destination location <a1>.

Format :

- Medium

| 47 | 31 | 15 |
| --- | --- | --- |
| 0x34 | a1 | a2 |
| code | destination | operand |

| TIC_OUT_A4R | Real Function | TIC_OUT_A4R |
| --- | --- | --- |

Operation : 	call <a2> ( <a1>

TIC syntax :	<a1> = call <a2>

Type :

| a1 | Real |
| --- | --- |
| a2 | integer |

Description :	 Calls the function <a2> and stores the result in the destination location <a1>.

Format :

- Medium

| 47 | 31 | 15 |
| --- | --- | --- |
| 0x9e | a1 | a2 |
| code | destination | operand |

| TIC_USF_A4R | Real Function | TIC_USF_A4R |
| --- | --- | --- |

Operation : 	call <a2> ( <a1>

TIC syntax :	<a1> = call <a2>

Type :

| a1 | Real |
| --- | --- |
| a2 | integer |

Description :	 Calls the function <a2> and stores the result in the destination location <a1>.

Format :

- Medium

| 47 | 31 | 15 |
| --- | --- | --- |
| 0xd4 | a1 | a2 |
| code | destination | operand |

| TIC_USF_OUT_A4R | Real Function | TIC_USF_OUT_A4R |
| --- | --- | --- |

Operation : 	call <a2> ( <a1>

TIC syntax :	<a1> = call <a2>

Type :

| a1 | Real |
| --- | --- |
| a2 | integer |

Description :	 Calls the function <a2> and stores the result in the destination location <a1>.

Format :

- Medium

| 47 | 31 | 15 |
| --- | --- | --- |
| 0xda | a1 | a2 |
| code | destination | operand |

| TIC_STD_A4R | Real Function | TIC_STD_A4R |
| --- | --- | --- |

Operation : 	call <a2> ( <a1>

TIC syntax :	<a1> = call <a2>

Type :

| a1 | Real |
| --- | --- |
| a2 | integer |

Description :	 Calls the function <a2> and stores the result in the destination location <a1>.

Format :

- Medium

| 47 | 31 | 15 |
| --- | --- | --- |
| 0xdf | a1 | a2 |
| code | destination | operand |

| TIC_STD_OUT_A4R | Real Function | TIC_STD_OUT_A4R |
| --- | --- | --- |

Operation : 	call <a2> ( <a1>

TIC syntax :	<a1> = call <a2>

Type :

| a1 | Real |
| --- | --- |
| a2 | integer |

Description :	 Calls the function <a2> and stores the result in the destination location <a1>.

Format :

- Medium

| 47 | 31 | 15 |
| --- | --- | --- |
| 0xe5 | a1 | a2 |
| code | destination | operand |

### Boolean instructions

| TIC_A4B | Boolean Function | TIC_A4B |
| --- | --- | --- |

Operation : 	call <a2> ( <a1>

TIC syntax :	<a1> = call <a2>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | integer |

Description : Calls the function <a2> and stores the result in the destination location <a1>.

Format :

- Medium

| 47 | 31 | 15 |
| --- | --- | --- |
| 0x32 | a1 | a2 |
| code | destination | operand |

| TIC_TRS_A4B | Boolean Function | TIC_TRS_A4B |
| --- | --- | --- |

Operation : 	call <a2> ( <a1>

TIC syntax :	<a1> = call <a2>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | integer |

Description : Calls the function <a2> and stores the result in the destination location <a1>.

Format :

- Medium

| 47 | 31 | 15 |
| --- | --- | --- |
| 0x6c | a1 | a2 |
| code | destination | operand |

| TIC_OUT_A4B | Boolean Function | TIC_OUT_A4B |
| --- | --- | --- |

Operation : 	call <a2> ( <a1>

TIC syntax :	<a1> = call <a2>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | integer |

Description : Calls the function <a2> and stores the result in the destination location <a1>.

Format :

- Medium

| 47 | 31 | 15 |
| --- | --- | --- |
| 0x9c | a1 | a2 |
| code | destination | operand |

| TIC_USF_A4B | Boolean Function | TIC_USF_A4B |
| --- | --- | --- |

Operation : 	call <a2> ( <a1>

TIC syntax :	<a1> = call <a2>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | integer |

Description : Calls the function <a2> and stores the result in the destination location <a1>.

Format :

- Medium

| 47 | 31 | 15 |
| --- | --- | --- |
| 0xd2 | a1 | a2 |
| code | destination | operand |

| TIC_USF_TRS_A4B | Boolean Function | TIC_USF_TRS_A4B |
| --- | --- | --- |

Operation : 	call <a2> ( <a1>

TIC syntax :	<a1> = call <a2>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | integer |

Description : Calls the function <a2> and stores the result in the destination location <a1>.

Format :

- Medium

| 47 | 31 | 15 |
| --- | --- | --- |
| 0xd7 | a1 | a2 |
| code | destination | operand |

| TIC_USF_OUT_A4B | Boolean Function | TIC_USF_OUT_A4B |
| --- | --- | --- |

Operation : 	call <a2> ( <a1>

TIC syntax :	<a1> = call <a2>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | integer |

Description : Calls the function <a2> and stores the result in the destination location <a1>.

Format :

- Medium

| 47 | 31 | 15 |
| --- | --- | --- |
| 0xd8 | a1 | a2 |
| code | destination | operand |

| TIC_STD_A4B | Boolean Function | TIC_STD_A4B |
| --- | --- | --- |

Operation : 	call <a2> ( <a1>

TIC syntax :	<a1> = call <a2>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | integer |

Description : Calls the function <a2> and stores the result in the destination location <a1>.

Format :

- Medium

| 47 | 31 | 15 |
| --- | --- | --- |
| 0xdd | a1 | a2 |
| code | destination | operand |

| TIC_STD_TRS_A4B | Boolean Function | TIC_STD_TRS_A4B |
| --- | --- | --- |

Operation : 	call <a2> ( <a1>

TIC syntax :	<a1> = call <a2>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | integer |

Description : Calls the function <a2> and stores the result in the destination location <a1>.

Format :

- Medium

| 47 | 31 | 15 |
| --- | --- | --- |
| 0xe2 | a1 | a2 |
| code | destination | operand |

| TIC_STD_OUT_A4B | Boolean Function | TIC_STD_OUT_A4B |
| --- | --- | --- |

Operation : 	call <a2> ( <a1>

TIC syntax :	<a1> = call <a2>

Type :

| a1 | Boolean |
| --- | --- |
| a2 | integer |

Description : Calls the function <a2> and stores the result in the destination location <a1>.

Format :

- Medium

| 47 | 31 | 15 |
| --- | --- | --- |
| 0xe3 | a1 | a2 |
| code | destination | operand |

### Message instructions

| TIC_A4M | Message Function | TIC_A4M |
| --- | --- | --- |

Operation : 	call <a2> ( <a1>

TIC syntax :	<a1> = call <a2>

Type :

| a1 | message |
| --- | --- |
| a2 | integer |

Description :	 Calls the function <a2> and stores the result in the destination location <a1>.

Format :

- Medium

| 47 | 31 | 15 |
| --- | --- | --- |
| 0x36 | a1 | a2 |
| code | destination | operand |

| TIC_OUT_A4M | Message Function | TIC_OUT_A4M |
| --- | --- | --- |

Operation : 	call <a2> ( <a1>

TIC syntax :	<a1> = call <a2>

Type :

| a1 | message |
| --- | --- |
| a2 | integer |

Description :	 Calls the function <a2> and stores the result in the destination location <a1>.

Format :

- Medium

| 47 | 31 | 15 |
| --- | --- | --- |
| 0x36 | a1 | a2 |
| code | destination | operand |

| TIC_USF_A4M | Message Function | TIC_USF_A4M |
| --- | --- | --- |

Operation : 	call <a2> ( <a1>

TIC syntax :	<a1> = call <a2>

Type :

| a1 | message |
| --- | --- |
| a2 | integer |

Description :	 Calls the function <a2> and stores the result in the destination location <a1>.

Format :

- Medium

| 47 | 31 | 15 |
| --- | --- | --- |
| 0xd5 | a1 | a2 |
| code | destination | operand |

| TIC_USF_OUT_A4M | Message Function | TIC_USF_OUT_A4M |
| --- | --- | --- |

Operation : 	call <a2> ( <a1>

TIC syntax :	<a1> = call <a2>

Type :

| a1 | message |
| --- | --- |
| a2 | integer |

Description :	 Calls the function <a2> and stores the result in the destination location <a1>.

Format :

- Medium

| 47 | 31 | 15 |
| --- | --- | --- |
| 0xd5 | a1 | a2 |
| code | destination | operand |

| TIC_STD_A4M | Message Function | TIC_STD_A4M |
| --- | --- | --- |

Operation : 	call <a2> ( <a1>

TIC syntax :	<a1> = call <a2>

Type :

| a1 | message |
| --- | --- |
| a2 | integer |

Description :	 Calls the function <a2> and stores the result in the destination location <a1>.

Format :

- Medium

| 47 | 31 | 15 |
| --- | --- | --- |
| 0xe0 | a1 | a2 |
| code | destination | operand |

| TIC_STD_OUT_A4M | Message Function | TIC_STD_OUT_A4M |
| --- | --- | --- |

Operation : 	call <a2> ( <a1>

TIC syntax :	<a1> = call <a2>

Type :

| a1 | message |
| --- | --- |
| a2 | integer |

Description :	 Calls the function <a2> and stores the result in the destination location <a1>.

Format :

- Medium

| 47 | 31 | 15 |
| --- | --- | --- |
| 0xe6 | a1 | a2 |
| code | destination | operand |

### Timer instructions

| TIC_A4T | Timer Function | TIC_A4T |
| --- | --- | --- |

Operation : 	call <a2> ( <a1>

TIC syntax :	<a1> = call <a2>

Type :

| a1 | timer |
| --- | --- |
| a2 | integer |

Description :	 Calls the function <a2> and stores the result in the destination location <a1>.

Format :

- Medium

| 47 | 31 | 15 |
| --- | --- | --- |
| 0x35 | a1 | a2 |
| code | destination | operand |

| TIC_OUT_A4T | Timer Function | TIC_OUT_A4T |
| --- | --- | --- |

Operation : 	call <a2> ( <a1>

TIC syntax :	<a1> = call <a2>

Type :

| a1 | timer |
| --- | --- |
| a2 | integer |

Description :	 Calls the function <a2> and stores the result in the destination location <a1>.

Format :

- Medium

| 47 | 31 | 15 |
| --- | --- | --- |
| 0xa0 | a1 | a2 |
| code | destination | operand |

| TIC_USF_A4T | Timer Function | TIC_USF_A4T |
| --- | --- | --- |

Operation : 	call <a2> ( <a1>

TIC syntax :	<a1> = call <a2>

Type :

| a1 | timer |
| --- | --- |
| a2 | integer |

Description :	 Calls the function <a2> and stores the result in the destination location <a1>.

Format :

- Medium

| 47 | 31 | 15 |
| --- | --- | --- |
| 0xd6 | a1 | a2 |
| code | destination | operand |

| TIC_USF_OUT_A4T | Timer Function | TIC_USF_OUT_A4T |
| --- | --- | --- |

Operation : 	call <a2> ( <a1>

TIC syntax :	<a1> = call <a2>

Type :

| a1 | timer |
| --- | --- |
| a2 | integer |

Description :	 Calls the function <a2> and stores the result in the destination location <a1>.

Format :

- Medium

| 47 | 31 | 15 |
| --- | --- | --- |
| 0xdc | a1 | a2 |
| code | destination | operand |

| TIC_STD_A4T | Timer Function | TIC_STD_A4T |
| --- | --- | --- |

Operation : 	call <a2> ( <a1>

TIC syntax :	<a1> = call <a2>

Type :

| a1 | timer |
| --- | --- |
| a2 | integer |

Description :	 Calls the function <a2> and stores the result in the destination location <a1>.

Format :

- Medium

| 47 | 31 | 15 |
| --- | --- | --- |
| 0xe1 | a1 | a2 |
| code | destination | operand |

| TIC_STD_OUT_A4T | Timer Function | TIC_STD_OUT_A4T |
| --- | --- | --- |

Operation : 	call <a2> ( <a1>

TIC syntax :	<a1> = call <a2>

Type :

| a1 | timer |
| --- | --- |
| a2 | integer |

Description :	 Calls the function <a2> and stores the result in the destination location <a1>.

Format :

- Medium

| 47 | 31 | 15 |
| --- | --- | --- |
| 0xe7 | a1 | a2 |
| code | destination | operand |

## SFC control functions instructions

Such instructions are function calls occuring in a parent SFC program, to control one of its child SFC programs. The address of the child program has been pushed as a parameter.

| TIC_SYS_GSTART | SFC control | TIC_SYS_GSTART |
| --- | --- | --- |

Operation : 	starts a SFC child

TIC syntax :	call GSTART

Type :

Description :	 Starts the SFC child which the name has been pushed.

Format :

- Medium

15

0xbb

code

| TIC_SYS_GFREEZE | SFC control | TIC_SYS_GFREEZE |
| --- | --- | --- |

Operation : 	freezes a SFC child

TIC syntax :	call GFREEZE

Type :

Description :	 Freezes the SFC child which the name has been pushed.

Format :

- Medium

15

0xbc

code

| TIC_SYS_GKILL | SFC control | TIC_SYS_GKILL |
| --- | --- | --- |

Operation : 	kills a SFC child

TIC syntax :	call GKILL

Type :

Description :	 Kills the SFC child which the name has been pushed.

Format :

- Medium

15

0xbd

code

| TIC_SYS_GRST | SFC control | TIC_SYS_GRST |
| --- | --- | --- |

Operation : 	restarts a SFC child

TIC syntax :	call GRST

Type :

Description :	 Restarts the SFC child which the name has been pushed.

Format :

- Medium

15

0xbe

code

## Activity control timer instructions

Such instructions are function calls occuring in a program, to control the updating of a timer variable. The address of the timer has been pushed as a parameter.

| TIC_SYS_TSTART | Timer control | TIC_SYS_TSTART |
| --- | --- | --- |

Operation : 	starts a timer

TIC syntax :	call TSTART

Type :

Description :	 Starts the timer which the name has been pushed.

Format :

- Medium

15

0xbf

code

| TIC_SYS_TSTOP | Timer control | TIC_SYS_TSTOP |
| --- | --- | --- |

Operation : 	stops a timer

TIC syntax :	call TSTOP

Type :

Description :	 Stops the timer which the name has been pushed.

Format :

- Medium

15

0xc0

Code

## Function system instructions

Such instructions are function calls occurring in a program, to system level functions supported by the ISaGRAF target. The parameter addresses have been pushed by 'param' instructions.

### Integer Instructions

| TIC_SYS_GSTATUS | Status system | TIC_SYS_GSTATUS |
| --- | --- | --- |

Operation : 	status of system ( <a1>

TIC syntax :	<a1> = call GSTATUS

Type :

| a1 | integer |
| --- | --- |

Description :	Reads the status of the system and stores the result in the destination location <a1>.

Format :

- Medium

15

0xc1

code

| TIC_SYS_SYSTEM | System call | TIC_SYS_SYSTEM |
| --- | --- | --- |

Operation : 	call system command( <a1>

TIC syntax :	<a1> = call SYSTEM

Type :

| a1 | integer |
| --- | --- |

Description :	Calls the function ' system ' and stores the result in the destination location <a1>.

Format :

- Medium

15

0xc2

code

| TIC_SYS_OPERATE | Operate | TIC_SYS_OPERATE |
| --- | --- | --- |

Operation : 	calls operate function( <a1>

TIC syntax :	<a1> = call OPERATE

Type :

| a1 | integer |
| --- | --- |

Description :	Calls the ' operate 'function and stores the result in the destination location <a1>.

Format :

- Medium

15

0xc3

code

| TIC_OUT_GSTATUS | Status system | TIC_OUT_GSTATUS |
| --- | --- | --- |

Operation : 	status of system ( <a1>

TIC syntax :	<a1> = call GSTATUS

Type :

| a1 | integer |
| --- | --- |

Description :	Reads the status of the system and stores the result in the destination location <a1>.

Format :

- Medium

15

0xc8

code

| TIC_OUT_SYSTEM | System call | TIC_OUT_SYSTEM |
| --- | --- | --- |

Operation : 	call system command( <a1>

TIC syntax :	<a1> = call SYSTEM

Type :

| a1 | integer |
| --- | --- |

Description :	Calls the function ' system ' and stores the result in the destination location <a1>.

Format :

- Medium

15

0xc9

code

| TIC_OUT_OPERATE | Operate | TIC_OUT_OPERATE |
| --- | --- | --- |

Operation : 	calls operate function( <a1>

TIC syntax :	<a1> = call OPERATE

Type :

| a1 | integer |
| --- | --- |

Description :	Calls the ' operate 'function and stores the result in the destination location <a1>.

Format :

- Medium

15

0xca

code

### Boolean instructions

| TIC_SYS_FEDGE | Fedge | TIC_SYS_FEDGE |
| --- | --- | --- |

Operation : 	falling edge state ( <a1>

TIC syntax :	<a1> = call FEDGE

Type :

| a1 | Boolean |
| --- | --- |

Description :	Reads if a falling edge is detected and stores the result in the destination location <a1>.

Format :

- Medium

15

0xc4

code

| TIC_SYS_REDGE | Redge | TIC_SYS_REDGE |
| --- | --- | --- |

Operation : 	rising edge state ( <a1>

TIC syntax :	<a1> = call REDGE

Type :

| a1 | Boolean |
| --- | --- |

Description :	Reads if a rising edge is detected and stores the result in the destination location <a1>.

Format :

- Medium

15

0xc5

code

| TIC_TRS_FEDGE | Fedge | TIC_TRS_FEDGE |
| --- | --- | --- |

Operation : 	falling edge state ( <a1>

TIC syntax :	<a1> = call FEDGE

Type :

| a1 | Boolean |
| --- | --- |

Description :	Reads if a falling edge is detected and stores the result in the destination location <a1>.

Format :

- Medium

15

0xc6

code

| TIC_TRS_REDGE | Redge | TIC_TRS_REDGE |
| --- | --- | --- |

Operation : 	rising edge state ( <a1>

TIC syntax :	<a1> = call REDGE

Type :

| a1 | Boolean |
| --- | --- |

Description :	Reads if a rising edge is detected and stores the result in the destination location <a1>.

Format :

- Medium

15

0xc7

code

| TIC_OUT_FEDGE | Fedge | TIC_OUT_FEDGE |
| --- | --- | --- |

Operation : 	falling edge state ( <a1>

TIC syntax :	<a1> = call FEDGE

Type :

| a1 | Boolean |
| --- | --- |

Description :	Reads if a falling edge is detected and stores the result in the destination location <a1>.

Format :

- Medium

15

0xcb

code

| TIC_OUT_REDGE | Redge | TIC_OUT_REDGE |
| --- | --- | --- |

Operation : 	rising edge state ( <a1>

TIC syntax :	<a1> = call REDGE

Type :

| a1 | Boolean |
| --- | --- |

Description :	Reads if a rising edge is detected and stores the result in the destination location <a1>.

Format :

- Medium

15

0xcc

code

## Conversion function instructions

The following instructions are used to call 'type conversion' functions. The value to be converted has been pushed as a parameter. The second and third arguments (#b and #c) are absolute values which identifies destination and source types, according to the following numbering: 1=boo / 2=ana / 3=real /4=msg.

| TIC_SYS_CNV | Convert function | TIC_SYS_CNV |
| --- | --- | --- |

Operation : 	converts parameter( <a1>

TIC syntax :	<a1> = call CONVERTION (#<a2>, #<a3>)

Type :

| a1 | depend of #<a2> |
| --- | --- |
| a2 | integer |
| a3 | integer |

Description :	Converts the parameter which has a type defined by #<a3> to a type defined by #<a2> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0xcd | a1 | a2 | a3 |
| code | destination | operand | operand |

| TIC_TRS_CNV | Convert function | TIC_TRS_CNV |
| --- | --- | --- |

Operation : 	converts parameter( <a1>

TIC syntax :	<a1> = call CONVERTION (#<a2>, #<a3>)

Type :

| a1 | depend of #<a2> |
| --- | --- |
| a2 | integer |
| a3 | integer |

Description :	Converts the parameter which has a type defined by #<a3> to a type defined by #<a2> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0xce | a1 | a2 | a3 |
| code | destination | operand | operand |

Notes :

#<a2> must be defined as a Boolean.

| TIC_OUT_CNV | Convert function | TIC_OUT_CNV |
| --- | --- | --- |

Operation : 	converts parameter( <a1>

TIC syntax :	<a1> = call CONVERTION (#<a2>, #<a3>)

Type :

| a1 | depend of #<a2> |
| --- | --- |
| a2 | integer |
| a3 | integer |

Description :	Converts the parameter which has a type defined by #<a3> to a type defined by #<a2> and stores the result in the destination location <a1>.

Format :

- Medium

| 63 | 47 | 31 | 15 |
| --- | --- | --- | --- |
| 0xcd | a1 | a2 | a3 |
| code | destination | operand | operand |

## Step activity instructions

The following instructions give access to the attributes of an SFC step (activity flag and activity duration). The second argument is the address of the SFC step.

### Boolean instructions

| TIC_SYS_TAC | Test Activity | TIC_SYS_TAC |
| --- | --- | --- |

Operation : 	reads activity of step number #<a2>( <a1>

TIC syntax :	<a1> = StepAct ( #<a2> )

Type :

| a1 | Boolean |
| --- | --- |
| a2 | integer |

Description :	 Reads the activity of step number #<a2> and stores the result in the destination location <a1>.

Format :

- Medium

| 47 | 31 | 15 |
| --- | --- | --- |
| 0xd0 | a1 | a2 |
| code | destination | operand |

### Timer instructions

| TIC_SYS_DAC | Duration Activity | TIC_SYS_DAC |
| --- | --- | --- |

Operation : 	reads duration of step number #<a2>( <a1>

TIC syntax :	<a1> = StepTime ( #<a2> )

Type :

| a1 | timer |
| --- | --- |
| a2 | integer |

Description :	 Reads the duration of step number #<a2> and stores the result in the destination location <a1>.

Format :

- Medium

| 47 | 31 | 15 |
| --- | --- | --- |
| 0xd1 | a1 | a2 |
| code | destination | operand |

## Calling function block instructions

| TIC_FBL | User C Blocks | TIC_FBL |
| --- | --- | --- |

Operation : 	Actives instance number #<a2> of the function block address <a1>

TIC syntax :	call <a1>, #<a2>

Type :

Description :	 Actives instance number #<a2> of the function block address <a1> with the parameters pushed

Format :

- Medium

| 47 | 31 | 15 |
| --- | --- | --- |
| 0xd8 | a1 | a2 |
| code | operand | operand |

| TIC_STD_FBL | Standard C Blocks | TIC_STD_FBL |
| --- | --- | --- |

Operation : 	Actives instance number #<a2> of the function block address <a1>

TIC syntax :	call <a1>, #<a2>

Type :

Description :	 Actives instance number #<a2> of the function block address <a1> with the parameters pushed

Format :

- Medium

| 47 | 31 | 15 |
| --- | --- | --- |
| 0xd9 | a1 | a2 |
| code | operand | operand |

## End of block instruction

This instruction occurs as a marker to indicate the end of a code sequence. It does not occur in a code sequence for the evaluation of a transition condition.

| TIC_END_BLOCK | End Code | TIC_END_BLOCK |
| --- | --- | --- |

Operation : 	marks the end of a block of code.

TIC syntax :	EndBlock

Type :

Description :	 Indicates the end of a code sequence.

Format :

- Medium

15

0xde

code

## Reserved TIC code

These instructions are never generated by the ISaGRAF compiler. They are reserved for the target kernel to perform debug operations on the downloaded code.

| TIC_BKP_BEG | Reserved | TIC_BKP_BEG |
| --- | --- | --- |

Operation : 	.

TIC syntax :

Type :

Description :

Format :

- Medium

15

0xf0

code

| TIC_BKP_END | Reserved | TIC_BKP_END |
| --- | --- | --- |

Operation : 	.

TIC syntax :

Type :

Description :

Format :

- Medium

15

0xf1

code

| TIC_BKP_TRA | Reserved | TIC_BKP_TRA |
| --- | --- | --- |

Operation : 	.

TIC syntax :

Type :

Description :

Format :

- Medium

15

0xf2

code

## Instruction summary

'TIC_A1NO.', 135

'TIC_A1SI', 65

'TIC_A1SR', 100

'TIC_A2AI', 68

'TIC_A2AM', 162

'TIC_A2ANO.', 139

'TIC_A2AR', 103

'TIC_A2AT', 189

'TIC_A2DI', 67

'TIC_A2DR', 102

'TIC_A2EQB', 136

'TIC_A2EQI', 74

'TIC_A2EQM', 167

'TIC_A2EQR', 109

'TIC_A2EQT', 195

'TIC_A2GEI', 73

'TIC_A2GEM', 166

'TIC_A2GER', 108

'TIC_A2GET', 194

'TIC_A2GTI', 71

'TIC_A2GTM', 164

'TIC_A2GTR', 106

'TIC_A2GTT', 192

'TIC_A2LEI', 72

'TIC_A2LEM', 165

'TIC_A2LER', 107

'TIC_A2LTI', 70

'TIC_A2LTM', 163

'TIC_A2LTR', 105

'TIC_A2LTT', 191

'TIC_A2MI', 66

'TIC_A2NEB', 137

'TIC_A2NEI', 75

'TIC_A2NEM', 168

'TIC_A2NER', 110

'TIC_A2NET', 196

'TIC_A2ORB', 138

'TIC_A2SI', 69

'TIC_A2SR', 104

'TIC_A2ST', 190

'TIC_A2XOB', 140

'TIC_A3B', 141

'TIC_A3I', 76

'TIC_A3M', 169

'TIC_A3R', 111

'TIC_A3T', 197

'TIC_A4B', 276

'TIC_A4I', 263

'TIC_A4M', 286

'TIC_A4N', 261

'TIC_A4R', 269

'TIC_A4T', 293

'TIC_A5B', 142

'TIC_A5I', 77

'TIC_A5M', 170

'TIC_A5R', 112

'TIC_A5T', 198

'TIC_A6B', 143

'TIC_A6I', 78

'TIC_A6M', 171

'TIC_A6R', 113

'TIC_A6T', 199

'TIC_BKP_BEG', 334

'TIC_BKP_END', 335

'TIC_BKP_TRA', 336

'TIC_C1B', 215

'TIC_C2B', 216

'TIC_END_BLOCK', 332

'TIC_FBL', 329

'TIC_I1', 217

'TIC_I2', 218

'TIC_L1', 219

'TIC_OUT_A1NO.', 152

'TIC_OUT_A1SI', 85

'TIC_OUT_A1SR', 120

'TIC_OUT_A2AI', 88

'TIC_OUT_A2AM', 178

'TIC_OUT_A2ANO.', 156

'TIC_OUT_A2AR', 123

'TIC_OUT_A2DI', 87

'TIC_OUT_A2DR', 122

'TIC_OUT_A2EQB', 153

'TIC_OUT_A2EQI', 94

'TIC_OUT_A2EQM', 183

'TIC_OUT_A2EQR', 129

'TIC_OUT_A2EQT', 210

'TIC_OUT_A2GEI', 93

'TIC_OUT_A2GEM', 182

'TIC_OUT_A2GER', 128

'TIC_OUT_A2GET', 209

'TIC_OUT_A2GTI', 91

'TIC_OUT_A2GTM', 180

'TIC_OUT_A2GTR', 126

'TIC_OUT_A2GTT', 207

'TIC_OUT_A2LEI', 92

'TIC_OUT_A2LEM', 181

'TIC_OUT_A2LER', 127

'TIC_OUT_A2LET', 208

'TIC_OUT_A2LTI', 90

'TIC_OUT_A2LTM', 179

'TIC_OUT_A2LTR', 125

'TIC_OUT_A2LTT', 206

'TIC_OUT_A2MI', 86

'TIC_OUT_A2MR', 121

'TIC_OUT_A2NEB', 154

'TIC_OUT_A2NEI', 95

'TIC_OUT_A2NEM', 184

'TIC_OUT_A2NER', 130

'TIC_OUT_A2NET', 211

'TIC_OUT_A2ORB', 155

'TIC_OUT_A2SI', 89

'TIC_OUT_A2SR', 124

'TIC_OUT_A2XOB', 157

'TIC_OUT_A3B', 158

'TIC_OUT_A3I', 96

'TIC_OUT_A3M', 185

'TIC_OUT_A3R', 131

'TIC_OUT_A3T', 212

'TIC_OUT_A4B', 278

'TIC_OUT_A4I', 264

'TIC_OUT_A4M', 287

'TIC_OUT_A4R', 270

'TIC_OUT_A4T', 294

'TIC_OUT_A5B', 159

'TIC_OUT_A5I', 97

'TIC_OUT_A5M', 186

'TIC_OUT_A5R', 132

'TIC_OUT_A5T', 213

'TIC_OUT_A6B', 160

'TIC_OUT_A6I', 98

'TIC_OUT_A6M', 187

'TIC_OUT_A6R', 133

'TIC_OUT_CNV', 324

'TIC_OUT_FEDGE', 319

'TIC_OUT_GSTATUS', 311

'TIC_OUT_OPERATE', 313

'TIC_OUT_REDGE', 320

'TIC_OUT_SYSTEM', 312

'TIC_P1B', 225

'TIC_P1C', 231

'TIC_P1F', 232

'TIC_P1I', 221

'TIC_P1M', 227

'TIC_P1R', 223

'TIC_P1S', 233

'TIC_P1T', 229

'TIC_STD_A4B', 282

'TIC_STD_A4I', 266

'TIC_STD_A4M', 290

'TIC_STD_A4R', 273

'TIC_STD_A4T', 297

'TIC_STD_FBL', 330

'TIC_STD_OUT_A4B', 284

'TIC_STD_OUT_A4M', 291

'TIC_STD_OUT_A4R', 274

'TIC_STD_OUT_A4T', 298

'TIC_STD_TRS_A4B', 283

'TIC_SYS_CNV', 322

'TIC_SYS_DAC', 327

'TIC_SYS_FEDGE', 315

'TIC_SYS_GFREEZE', 301

'TIC_SYS_GKILL', 302

'TIC_SYS_GPARB', 241

'TIC_SYS_GPARBLKB', 254

'TIC_SYS_GPARBLKI', 250

'TIC_SYS_GPARBLKM', 257

'TIC_SYS_GPARBLKT', 259

'TIC_SYS_GPARI', 235

'TIC_SYS_GPARM', 244

'TIC_SYS_GPARR', 238

'TIC_SYS_GPART', 247

'TIC_SYS_GRST', 303

'TIC_SYS_GSTART', 300

'TIC_SYS_GSTATUS', 308

'TIC_SYS_OPERATE', 310

'TIC_SYS_PPARB', 242

'TIC_SYS_PPARI', 236

'TIC_SYS_PPARM', 245

'TIC_SYS_PPARR', 239

'TIC_SYS_PPART', 248

'TIC_SYS_REDGE', 316

'TIC_SYS_SYSTEM', 309

'TIC_SYS_TAC', 325

'TIC_SYS_TSTART', 305

'TIC_SYS_TSTOP', 306

'TIC_TRS_A1NO.', 144

'TIC_TRS_A2ANO.', 148

'TIC_TRS_A2EQB', 145

'TIC_TRS_A2EQI', 83

'TIC_TRS_A2EQM', 176

'TIC_TRS_A2EQR', 118

'TIC_TRS_A2EQT', 204

'TIC_TRS_A2GEI', 82

'TIC_TRS_A2GEM', 175

'TIC_TRS_A2GER', 117

'TIC_TRS_A2GET', 203

'TIC_TRS_A2GTI', 80

'TIC_TRS_A2GTM', 173

'TIC_TRS_A2GTR', 115

'TIC_TRS_A2GTT', 201

'TIC_TRS_A2LEI', 81

'TIC_TRS_A2LEM', 174

'TIC_TRS_A2LER', 116

'TIC_TRS_A2LET', 202

'TIC_TRS_A2LTI', 79

'TIC_TRS_A2LTM', 172

'TIC_TRS_A2LTR', 114

'TIC_TRS_A2LTT', 200

'TIC_TRS_A2NEB', 146

'TIC_TRS_A2NEI', 84

'TIC_TRS_A2NEM', 177

'TIC_TRS_A2NER', 119

'TIC_TRS_A2NET', 205

'TIC_TRS_A2ORB', 147

'TIC_TRS_A2XOB', 149

'TIC_TRS_A3B', 150

'TIC_TRS_A4B', 277

'TIC_TRS_A5B', 151

'TIC_TRS_CNV', 323

'TIC_TRS_FEDGE', 317

'TIC_TRS_GPARBLKB', 255

'TIC_TRS_REDGE', 318

'TIC_USF_A4B', 279

'TIC_USF_A4I', 265

'TIC_USF_A4M', 288

'TIC_USF_A4R', 271

'TIC_USF_A4T', 295

'TIC_USF_OUT_A4B', 281

'TIC_USF_OUT_A4I', 267

'TIC_USF_OUT_A4M', 289

'TIC_USF_OUT_A4R', 272

'TIC_USF_OUT_A4T', 296

'TIC_USF_TRS_A4B', 280

# Appendix 3 : Communication Protocol definition

## Overview

This document gives information about the communication protocol implemented between the ISaGRAF Workbench and Target. It only covers the communication requests linked to the programming environment (program downloading and debugging). It does not describe the other communications capabilities of the ISaGRAF target (such as pure Modbus frame handling). The protocol described in this document is the one implemented in ISaGRAF V3.xx. It may evolve to included further capabilities in future releases of the ISaGRAF product.

## Main format

This section gives an overview of the protocol implemented between ISaGRAF Workbench and target. This document gives the detail of the frames exchanged on a standard serial link. The protocol is based on Modbus protocol, with dedicated function codes. The same frames, at the lowest level, are used in the case of a TCP-IP communication on Ethernet, or when the protocol is customized using the ISDK_COM programming tool.

### Exchange mechanism

ISaGRAF communication is based on a master/slave mechanism. The master is the debugger, the slave is the target system. The rules of exchange are:

- the master sends a question

- the slave answers the question

The slave system never sends data spontaneously. Several slaves can be connected to the same master, if the hardware link enables it. Each ISaGRAF target kernel is identified by an ISaGRAF slave number, used as a Modbus slave number in the standard communication protocol.

### Frame format

Below is the main format of the frames during a single exchange (question and answer). Each frame has a maximum length of 255 bytes (including header and CRC16). Any number expressed in more than one byte follows the Motorola convention: from the highest significant byte to the lowest significant byte.

snd:	[slv][fc][id][pn][No.][info(?)][crc(2)]

rcv:	[slv][fc][id][pn][No.][info(?)][crc(2)]

slv (1byte):	Modbus-like slave number

fc (1 byte):	Modbus function code

id (1 byte):	Exchange identifier

pn (1 byte):	Packet number (if splitted in several frames)

No. (1 byte):	Number of information bytes

info ('No.' bytes):	information data

crc (2 bytes):	CRC16 checksum

Important: In the case of TCP-IP implementation, each question or answer is embedded in a TCP-IP telegram. Each telegram contains exactly 256 bytes. If the frame is smaller than 256, the trailing transmitted bytes are not relevant and should be ignored.

### Slave number

The slave number stored in the frames is the ISaGRAF slave number which fully identifies an ISaGRAF target kernel. This is enough for serial link communication. In the case of TCP-IP or customized protocols, this slave number may be completed with the identification of a physical or logical node of the network. The slave number can take any value between 1 and 255. Code 0, reserved in Modbus protocol for broadcasting, is not implemented and is never used in the ISaGRAF protocol.

### Function codes

The Modbus function codes used for communication between the Workbench and the target are described below. They are extensions of the set of Modbus function codes (expressed here in decimal):

65	system/application control

67	application request

68	application request (see note)

69	start download

70	download

71	unused (reserved for extensions)

72	unused (reserved for extensions)

Note: The function code 67 is normally used for all application requests. In the case of a request splitted in several packets, the first exchange (1rst packet) uses functuon code 67, and the following exchanges (packets 2 to N) use function code 68.

Other standard Modbus function codes (read/write bits or words) are also supported by the ISaGRAF target, but are not used by the Workbench. Refer to the ISaGRAF Target User's Guide for further information about standard Modbus function code handling on the target.

### Frame identification

Each exchange (question and answer) is identified by a frame number expressed in one byte and stored in the third byte of the frame. This number is increased by the Workbench (the master) on each new exchange. The frame number is answered by an echo by the target (the slave).

When automatic retries are allowed on the Workbench, the same frame number is used if a single exchange fails.

### Packet numbering

Because each frame is limited to 255 characters, some messages (questions or answers) can be splitted into many single frames. This also occurs when using download messages. In such a case, the fourth byte of the frame contains the packet number. The following numbering is used:

0	this is the last packet

FDhex (253)	other packets are expected

FEhex (254)	other packets are expected (during file transfer)

FFhex (255)	exchange must be stopped after this packet

other	other packets are expected (during data transfer)

### CRC16 checksum

All the frames are completed by a CRC16 checksum. ISaGRAF uses an enhanced algorithm using preset tables for the calculation of the CRC16. All the bytes of the frame (including the header) are operated on by the CRC16 calculation. Below is the coding of the CRC16 used by ISaGRAF:

#define POLY_CRC16   0xA001

static BYTE TABLE1[256];   /* crc16 values */

static BYTE TABLE2[256];   /* crc16 values */

/*

crc_init: prepare crc16 preset tables

must be called once at init

(before any crc calculation)

*/

void crc_init (void)

{

WORD mask, bit, crc, mem;

for( mask = 0; mask < 0x100; mask++) {

crc = mask;

for( bit = 0; bit < 8; bit++) {

mem = crc & 0x0001 ;

crc /=  2;

if ( mem != 0 ) crc ^= POLY_CRC16 ;

}

TABLE2[mask] = crc & 0xff;

TABLE1[mask] = crc >> 8;

}

}

/*

crc_make: calculates a crc16

size: size of the frame (including header)

buff: pointer to the first byte of the frame

(slave number)

return: CRC16 in MOTOROLA format (high byte / low byte)

*/

WORD crc_make (WORD size, BYTE *buff)

{

BYTE car, i;

BYTE crc[2];

crc[0] = 0xff;

crc[1] = 0xff;

for ( i = 0; i < size; i++ ) {

car = buff[i];

car ^= crc[0];

crc[0] = crc[1] ^ TABLE2[car];

crc[1] = TABLE1[car];

}

return (*(WORD*)(&crc[0]));

}

## Download exchanges

Download exchanges are used to transfer files from the Workbench to the target. This applies to the following features:

- download the code of the application

- download the symbols of the application

- download new application code for on-line modification

The download communication is divided into three sequential phases:

- begin download (1 exchange)

- download packets (N exchanges)

- end download (1 exchange)

### Beginning of download

The first exchange of a download identifies the type of data to be downloaded, and gives the target the opportunity to accept or refuse the download. It uses the function code 69:

snd:	[slv][69][id][0][No.][typ][name(s)][0][size(4)][crc(2)]

rcv:	[slv][69][id][0][2][rc(2)][crc(2)]

slv (1byte):	Modbus-like slave number

id (1 byte):	Exchange identifier

No. (1 byte):	Number of information bytes = (strlen (name) + 6)

typ (1 byte):	Type of downloaded file

name (x bytes):	Name of the downloaded file (various length)

size (4 bytes):	Size of the downloaded file

rc (2 bytes):	Return check answered by the target

crc (2 bytes):	CRC16 checksum

The null byte stored after the name of the downloaded file is used as a marker to separate the 'name' and 'size' fields. The names used by the Workbench for download commands are:

<projname>.tel	normal download of the application code

<projname>.tst	download of the application symbols

<projname>.upd	download of the code for an on-line modification

The <projname> string is the name of the project such as defined in the Workbench. The 'typ' field is one ascii character which can take one of the following values:

'1' (49dec):	normal download of the application code

'2' (50dec):	download of the application symbols

'5' (53dec):	download for immediate On Line modification

'6' (54dec):	download for delayed On Line modification

Values 0, 3 and 4 are reserved for future extensions. The 'rc' field is a return check, expressed in two bytes, answered by the target to accept or refuse the downloading. The possible values for the return check are:

0	download is accepted

other	download s refused

### Downloading packets

The following exchanges are used to send the contents of the downloaded file. The packet number is used in this case to distinguish the last sent packet. These exchanges use the function code 70:

snd:	[slv][70][id][pn][No.][data(?)][crc(2)]

rcv:	[slv][70][id][0][2][rc(2)][crc(2)]

slv (1byte):	Modbus-like slave number

id (1 byte):	Exchange identifier

pn (1 byte):	Packet identifier

No. (1 byte):	Number of data bytes in the packet

data (No. bytes):	Packet of data bytes

rc (2 bytes):	Return check answered by the target

crc (2 bytes):	CRC16 checksum

The 'pn' field is used to distinguish the last downloaded packet. It can take one of two values:

0	this is the last packet

FEhex (254)	other packets will be sent after this one

The 'rc' field is a return check, expressed in two bytes, answered by the target to accept or refuse the packet. The possible values for the return check are:

0	OK

other	invalid packet or error during packet handling

### End of download

When all the packets have been sent, another single exchange is performed. It indicates that the target must perform the operation on the downloaded data. The operation performed by the target depends on the type of data downloaded. For the downloading of the application code, the target stores the code start of the new application. This exchange uses the function code 67:

snd:	[slv][67][id][0][No.][63][typ][pathname(s)][0][crc(2)]

rcv:	[slv][67][id][0][3][63][rc(2)][crc(2)]

slv (1byte):	Modbus-like slave number

id (1 byte):	Exchange identifier

No. (1 byte):	Number of information bytes = (strlen (pathname) + 2)

typ (1 byte):	Type of downloaded file

pathname (x bytes):	Pathame of the downloaded file (various length)

size (4 bytes):	Size of the downloaded file

rc (2 bytes):	Return check answered by the target

crc (2 bytes):	CRC16 checksum

The 'pathname' contains the same string as the 'name' indicated at the beginning of the download. It can include a full pathname in future extensions of the protocol. The pathname is always followed by a null byte. The 'typ' field is one ascii character which can take one of the following values:

1:	normal download of the application code

2:	download of the application symbols

5:	download for immediate On Line modification

6:	download for delayed On Line modification

Values 0, 3 and 4 are reserved for future extensions. The 'rc' field is a return check, expressed in two bytes, answered by the target to indicate whether the requested end of download has been correctly performed. The possible values for the return check are:

0	OK

other	operation has failed

## Requests used for Upload

This section details the format of the communication requests used to upload EZS (Embedded Source Code) from ISaGRAF 3.3 Target to ISaGRAF 3.3 Workbench. The implementation introduces a generic request used to upload any kind of target object. The EZS upload is implemented through ISaGRAF resources. This is an application request sent through function code #67, according to the standard ISaGRAF format.

# Request ID = 64 (decimal) - Name = GETOBJECT

Question:

| slv | 67 | fn | 0 | nb | 64 | ... | info | ... | Crc(2) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Answer:

| slv | 67 | fn | 0 | nb | 64 | Rc(2) | ... | info | ... | crc(2) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Arguments:

slv	slave number

fn	frame number (always changing)

nb	nb of bytes in request (request id + info)

crc	checksum

rc	request return check

info	arguments

Below are format and description of the request arguments:

Question:

| 64 | size | offset | ident |  |
| --- | --- | --- | --- | --- |
| 1 | 1 | 4 | <=31 + \0 | (bytes) |

# Answer

| 64 | rc | size | offset | Ident | data |  |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | 2 | 1 | 4 | <=31 + \0 | <=128 | (bytes) |

# Arguments

size	number of bytes to read (cannot exceed 128 bytes)

or 0 to get object length (4 bytes returned in this case)

offset	offset of the first byte to read

ident	object identification (type and name)

text string (max 31 characters) plus null termination character

data	read data (cannot exceed 128 bytes)

or object length if size is 0

rc	0=ok

1=invalid object

2=invalid size

3=invalid offset

Below is the standard format of the "object identification" used in communication protocol to identify a resource. All names are expressed in uppercase letters. The total string cannot exceed 31 characters

<type>[:<name>]

Below are the predefined object types:

| type | name | description |
| --- | --- | --- |
| R | resource name | application resource "EZS" is the name of embedded source code |
|  |  | (others to be defined in the future) |

Examples:

R:EZS	resource used to store zipped source code

R:MYRES	user defined resource

## Control exchanges

Control exchanges are used to control or monitor the state of the target PLC (start / stop application), and to monitor the state of the application which is actually running in the PLC (run, stop, breakpoint...). All these requests use the function code 65:

snd:	[slv][65][id][0][No.][rq][args(?)][crc(2)]

rcv:	[slv][65][id][0][No.][rq][rc(2)][data(?)][crc(2)]

slv (1byte):	Modbus-like slave number

id (1 byte):	Exchange identifier

No. (1 byte):	Number of information bytes (not including CRC)

rq (1 byte):	Control request code

args (x bytes):	Request arguments (various length)

rc (2 bytes):	Return check answered by the target

data (x bytes):	Answered data (various length)

crc (2 bytes):	CRC16 checksum

The following sections of this chapter details the contents of questions and answers, for the fields 'rq', 'rc', 'args' and 'data' only.

### Initiate communication

This exchange is the first sent by the debugger to open a communication session. It is mainly used by the target to initiate each of its communictaion layers. The request code is 0. There is no argument for this request.

snd:	[0]

rcv:	[0][rc(2)]

The 'rc' field is a return check expressed in two bytes. Its value is 0 if the request has been succesfully executed.

### Control PLC

This exchange is used to query the name and state of the application installed in the PLC. It is also used to start or stop the application (commmands of the Files menu in the debugger window). The request code is 10 (decimal). When the debugger queries the name and state of the current application the exchanged frames are:

snd:	[10][0][0]

rcv:	[10][rc(2)][0][state][vers(4)][len][name(s)][0]

rc (2 bytes):	Return check answered by the target

state (1 byte):	Status of the application (if exist)

vers (4 bytes):	Version number of the communication protocol

len (1 byte):	Length of the application name (if exist)

name (len bytes):	Name of the application (if exist)

The state of the application installed on the PLC can take one of the following values:

0	No application or application inactive

3	Application running in the PLC

When no application is running, the application name is empty. The 'len' field is equal to 0, and the null byte after the 'name' field still exists. Examples of typical answers are:

rcv:	[10][rc][0][0][vers][0][0]	= no application

rcv:	[10][rc][0][3][vers][3]['ABC'][0]	= appli 'ABC' running'

The 'vers' field is a 4 byte string containing the version number of the communication protocol. Current version number is '2.00'. The frames exchanged when the debugger send a 'STOP' command to deactivate an application are:

snd:	[10][0][1]

rcv:	[10][rc(2)]

The frames exchanged when the debugger send a 'START' command to activate an application are:

snd:	[10][0][2][len][name(s)][0]

rcv:	[10][rc(2)]

len (1 byte):	Length of the name of the application to be started

name (len bytes):	Name of the application to be started

The 'rc' field is a return check expressed in two bytes. Its value is 0 if the request has been succesfully executed.

### Monitor application state

Monitor exchanges are used by the Workbench to query the state of the application which is currently running on the PLC. The request code is 20 (decimal):

snd:	[20]

rcv:	[20][rc(2)][state]

rc (2 bytes):	Return check answered by the target

state (1 byte):	Running application state

The application state can take one of the following values:

0	Application is in normal 'real time' mode

1	Application is in 'cycle to cycle' mode

2	Application is stopped on a breakpoint

255	Application is aborted due to a fatal error

The 'rc' field is a return check expressed in two bytes. Its value is 0 if the request has been succesfully executed.

## Application level requests

Application level exchanges are used to monitor the components of the application (variables, programs, steps, transitions...). They also enable actions on application objects (write variable, set breakpoint...).

Such requests are always relative to the application currently running on the PLC. All these requests use the function code 67:

snd:	[slv][67][id][0][No.][rq][args(?)][crc(2)]

rcv:	[slv][67][id][0][No.][rq][rc(2)][data(?)][crc(2)]

slv (1byte):	Modbus-like slave number

id (1 byte):	Exchange identifier

No. (1 byte):	Number of information bytes (not including CRC)

rq (1 byte):	Control request code

args (x bytes):	Request arguments (various length)

rc (2 bytes):	Return check answered by the target

data (x bytes):	Answered data (various length)

crc (2 bytes):	CRC16 checksum

The 'rc' field is a return check expressed in two bytes. Its value is 0 if the request has been succesfully executed. Most of these requests have access to the ISaGRAF application object. The identification of an object is made through its VA (Virtual Address) which is the logical address of the ISaGRAF in its internal application Database. VAs are expressed in two bytes. The most significant 4 bits indicate the type of the object. The other bits contain the index of the object. Below is the coding of the ISaGRAF object types:

1	Boolean variable

2	Analog variable

3	Timer variable

4	Message string variable

5	Program

6	Real (floating pointing) analog variable

7	SFC step

8	SFC transition

13	(reserved for extensions)

15	System level information

The following sections of this chapter details the content of questions and answers for the fields 'rq', 'rc', 'args' and 'data' only. The list of supported requests is:

R_BKT	23	set breakpoint

R_WILR	24	(reserved for extensions)

R_WBOO	25	write boolean variable

R_WANA	26	write analog variable

R_WTMR	27	write timer variable

R_WMSG	28	write message variable

R_TSTART	30	start timer

R_TSTOP	31	stop timer

R_CC	32	set cycle by cycle mode

R_RT	33	set real time mode

R_EC	34	execute one cycle

R_TUC	35	transition unconditional clearing

R_TCC	36	transition conditional clearing

R_BKDEL	40	remove breakpoint

R_TCW	43	set cycle timing

R_TCR	44	read cycle timing

R_GSTART	45	start SFC program

R_GFREEZE	46	freeze SFC program

R_GKILL	47	kill SFC program

R_GRST	48	restart SFC program

R_GER	53	get last application error

R_UNLOCK	55	unlock I/O variable

R_LOCK	57	lock I/O variable

R_LOCKR	70	get list of locked I/O variables

R_APPL	72	get application identification

R_RANY	80	read a list of variables (all types)

R_UPMDF	62	realize delayed On-Line modification

R_WLIST	83	(reserved for extensions)

### R_BKT: set breakpoint

This request is sent by the debugger to set a breakpoint on a step or a transition. Its request code is 23. Below is the format of question and answers:

snd:	[23][va(2)][typ][ln(2)]

rcv:	[23][rc(2)]

va (2 bytes):	VA of the concerned step or transition

typ (1 byte):	Type of breakpoint

ln (2 bytes):	(reserved for extensions)

The 'typ' field indicates the type of breakpoint to be applied. It can take one of the following values:

1	breakpoint on step activation

2	breakpoint on step de-activation

3	breakpoint on transition clearing

4	(reserved for extensions)

### R_WBOO: write boolean variable

This request is sent by the debugger to force the value of a boolean variable. Its request code is 25. The format of questions and answers is:

snd:	[25][va(2)][act][1][value]

rcv:	[25][rc(2)]

va:	VA of the concerned boolean variable

act (1 byte):	Type of action to be performed

value (1 byte):	Boolean value (1=true / 0=false)

The 'act' field is the type of action that must be performed, according to the attribute of the variable:

0:	internal variable

2:	input variable (never used)

3:	output variable (I/O device must be updated)

### R_WANA: write analog variable

This request is sent by the debugger to force the value of an analog (integer or real) variable. Its request code is 26. Below is the format of question and answers:

snd:	[26][va(2)][act][1][value(4)]

rcv:	[26][rc(2)]

va:	VA of the analog variable concerned

act (1 byte):	Type of action to be performed

value (4 bytes):	Analog (integer or floating pointing) value

The 'act' field is the type of action that must be performed, according to the attribute of the variable:

0:	internal variable

2:	input variable (never used)

3:	output variable (I/O device must be updated)

### R_WTMR: write timer variable

This request is sent by the debugger to force the value of a timer variable. Its request code is 27. Below is the format of question and answers:

snd:	[27][va(2)][0][1][value(4)]

rcv:	[27][rc(2)]

va:	VA of the concerned timer variable

value (4 bytes):	Time value (expressed in milliseconds)

### R_WMSG: write message variable

This request is sent by the debugger to force the value of a message variable. Its request code is 28. Below is the format of question and answers:

snd:	[28][va(2)][act][1][No.c][value(s)][0]

rcv:	[28][rc(2)]

va:	VA of the concerned analog variable

act (1 byte):	Type of action to be performed

No.c (1 byte):	Number of character in string value

value (No.c bytes):	String value (characters)

The string value is always followed by a null byte. The 'act' field is the type of action that must be performed, according to the attribute of the variable:

0:	internal variable

2:	input variable (never used)

3:	output variable (I/O device must be updated)

### R_TSTART: start timer

This request is sent by the debugger to start a timer variable. Its request code is 30. The format of questions and answers is:

snd:	[30][1][va(2)]

rcv:	[30][rc(2)]

va (2 bytes):	VA of the timer variable to be started

### R_TSTOP: stop timer

This request is sent by the debugger to stop a timer variable. Its request code is 31. The format of questions and answers is:

snd:	[31][1][va(2)]

rcv:	[31][rc(2)]

va (2 bytes):	VA of the timer variable to be stopped

### R_CC: set cycle by cycle mode

This request is sent by the debugger to set the 'cycle to cycle' execution mode. Its request code is 32. The format of questions and answers is:

snd:	[32]

rcv:	[32][rc(2)]

### R_RT: set real time mode

This request is sent by the debugger to set the 'real time' execution mode. Its request code is 33. The format of questions and answers is:

snd:	[33]

rcv:	[33][rc(2)]

### R_EC: execute one cycle

This request is sent by the debugger to execute one cycle, when the target is in 'cycle to cycle' mode. Its request code is 34. The format of questions and answers is:

snd:	[34]

rcv:	[34][rc(2)]

### R_TUC: transition unconditional clearing

This request is sent by the debugger to force the unconditional clearing of an SFC transition. Its request code is 35. The format of questions and answers is:

snd:	[35][1][va(2)]

rcv:	[35][rc(2)]

va (2 bytes):	VA of the SFC transition to be cleared

### R_TCC: transition conditional clearing

This request is sent by the debugger to force the conditional clearing of an SFC transition. Its request code is 36. The format of questions and answers is:

snd:	[36] [1][va(2)]

rcv:	[36][rc(2)]

va (2 bytes):	VA of the SFC transition to be cleared

### R_BKDEL: remove breakpoint

This request is sent by the debugger to remove a breakpoint currentlt installed on an SFC step or transition. Its request code is 40. The format of questions and answers is:

snd:	[40][1][va(2)]

rcv:	[40][rc(2)]

va (2 bytes):	VA of step or transition where breakpoint is installed

This request can also be used to remove all the existing installed breakpoints, using the following format:

snd:	[40][0]

rcv:	[40][rc(2)]

### R_TCW: set cycle timing

This request is sent by the debugger to force the application cycle timing (sampling period). Its request code is 43. The format of questions and answers is:

snd:	[43][timing(4)]

rcv:	[43][rc(2)]

timing (4 bytes):	New cycle timing

### R_TCR: read cycle timing

This request is sent by the debugger to read the application cycle timing components. Its request code is 44. The format of questions and answers is:

snd:	[44]

rcv:	[44][rc(2)][smp(4)][curr(4)][max(4)][over(4)]

smp (4 bytes):	Programmed time (sampling period) in milliseconds

curr (4 bytes):	Last measured cycle timing in milliseconds

max (4 bytes):	Maximum detected cycle timing in milliseconds

over (4 bytes):	Number of cycle timing overflows

### R_GSTART: start SFC program

This request is sent by the debugger to start an SFC program. Its request code is 45. The format of questions and answers is:

snd:	[45][1][pnum]

rcv:	[45][rc(2)]

pnum (1 byte):	SFC program number

The program number is the lower byte of its VA, and does not include the 'program' object type. There is a maximum of 255 SFC programs in an application.

### R_GFREEZE: freeze SFC program

This request is sent by the debugger to freeze an SFC program. Its request code is 46. The format of questions and answers is:

snd:	[46][1][pnum]

rcv:	[46][rc(2)]

pnum (1 byte):	SFC program number

The program number is the lower byte of its VA, and does not include the 'program' object type. There is a maximum of 255 SFC programs in an application.

### R_GKILL: kill SFC program

This request is sent by the debugger to kill an SFC program. Its request code is 47. The format of questions and answers is:

snd:	[47][1][pnum]

rcv:	[47][rc(2)]

pnum (1 byte):	SFC program number

The program number is the lower byte of its VA, and does not include the 'program' object type. There is a maximum of 255 SFC programs in an application.

### R_GRST: restart SFC program

This request is sent by the debugger to restart a frozen SFC program. Its request code is 48. The format of questions and answers is:

snd:	[48][1][pnum]

rcv:	[48][rc(2)]

pnum (1 byte):	SFC program number

The program number is the lower byte of its VA, and does not include the 'program' object type. There is a maximum of 255 SFC programs in an application.

### R_GER: get last application error

This request is sent by the debugger to read the code of the last detected application error. Its request code is 53. The format of questions and answers is:

snd:	[53]

rcv:	[53][rc(2)][code(2)][arg(2)]

code (2 bytes):	Error code number (0 if no error detected)

arg (2 bytes):	Error argument (VA or numerical info)

### R_UNLOCK: unlock I/O variable

This request is sent by the debugger to unlock an I/O variable. Its request code is 55. The format of questions and answers is:

snd:	[55][1][va(2)]

rcv:	[55][rc(2)]

va (2 bytes):	VA of the I/O variable to be unlocked

The same request can also be used to unlock all the currently locked I/O variable, using the following format:

snd:	[55][0]

rcv:	[55][rc(2)]

### R_LOCK: lock I/O variable

This request is sent by the debugger to lock an I/O variable. Its request code is 57. The format of questions and answers is:

snd:	[57][1][va(2)]

rcv:	[57][rc(2)]

va (2 bytes):	VA of the I/O variable to be locked

### R_LOCKR: get list of locked I/O variables

This request is sent by the debugger to get the list of thhe currently locked I/O variables. Its request code is 70 The format of questions and answers is:

snd:	[70]

rcv:	[70][rc(2)][No.(2)] { [va(2)] }

No. (2 bytes):	number of locked variables

va (2 bytes):	VA of a locked I/O variable

(the frame contains a list of No. VAs)

### R_APPL: get application identification

This request is sent by the debugger to get the identification of the application currently running in the PLC. Its request code is 72. The format of questions and answers is:

snd:	[72]

rcv:	[72][rc(2)][vers(2)][dttm(4)][crc(4)]

vers (2 bytes):	Application code version number

dttm (4 bytes):	Date and time of code generation

crc (4 bytes):	CRC of the application symbols

### R_RANY: read a list of variables (all types)

This request is sent by the debugger to read the values of a list of objects from all types. Its request code is 80. The format of questions and answers is:

snd:	[rq][No.] {[va(2)][act]}

rcv:	[rq][rc(2)][AB(hex)][CD(hex)][No.]	{[type][value(?)]}

No. (1 byte):	number of variables

act (1 byte):	Type of action to be performed

va (2 bytes):	VA of a locked I/O variable

(the frame contains a list of No. [act+va] fields)

type (1 byte):	Type of value (see below)

value (X bytes):	Value of an object (various length: see format below)

(the frame contains a list of No. [type+value] fields)

The 'act' field is the type of action that must be performed, according to the attribute of the variable. This field is 0 if the object to be read is not a variable.

0:	internal variable (or not a variable)

1:	output variable

3:	input variable

The format and the meaning of a value depends on its type. The following table gives the relation ship between the data type (expressed in the 'type' field), the length of the 'value' field, and its meaning

type	length	meaning

1	1	boolean value (0=false / 1=true)

2	4	analog (integer or floating pointing) value

3	4	timer value (expressed in milliseconds)

4	2+No.c	string value: length + No.c characters + null byte

5	1	SFC program state (4=inactive / 2=active / 6=frozen)

7	1	step:	bit 0(mask 01hex) = step activity flag

bit 7(mask 80hex) = breakpoint on activation

bit 6(mask 40hex) = breakpoint on de-activation

8	1	transition:	bit 0(mask 01hex) = transition validity

bit 7(mask 80hex) = breakpoint

13	8	(reserved for extensions)

15	4	detected error code and argument (see GER request)

("f000" is used as a VA to query detected errors)

### R_UPMDF: realize delayed On-Line modification

This request is sent by the debugger to realize a delayed On Line modification (corresponds to the 'realize update' command of the debugger 'Files' menu). Its request code is 62. The format of questions and answers is:

snd:	[62]

rcv:	[62][rc(2)]

## Summary

Start download:

snd:	[slv][69][id][0][No.][typ][..name..][0][size(4)][crc(2)]

rcv:	[slv][69][id][0][2][rc(2)][crc(2)]

Downloading packets:

snd:	[slv][70][id][pn][No.][..data..][crc(2)]

rcv:	[slv][70][id][0][2][rc(2)][crc(2)]

End of download:

snd:	[slv][67][id][0][No.][63][typ][pathname(2)][0][crc(2)]

rcv:	[slv][67][id][0][3][63][rc(2)][crc(2)]

Control exchanges: Main format:

snd:	[slv][65][id][0][No.][rq][...args...][crc(2)]

rcv:	[slv][65][id][0][No.][rq][rc(2)][...data...][crc(2)]

Control exchanges: Request format:

Init:		snd: [0]

rcv: [0][rc(2)]

Read PLC status:	snd: [10][0][0]

(no appli)	rcv: [10][rc][0][0][vers(4)][0][0]

Read PLC status:	snd: [10][0][0]

(appli active)	rcv: [10][rc(2)][0][3]

[vers(4)][len][name(s)][0]

Stop appli:	snd: [10][0][1]

rcv: [10][rc(2)]

Activate appli:	snd: [10][0][2][len][name(s)][0]

rcv: [10][rc(2)]

Read status:	snd: [20]

rcv: [20][rc(2)][state]

Application level exchanges: Main format:

snd:	[slv][67][id][0][No.][rq][...args...][crc(2)]

rcv:	[slv][67][id][0][No.][rq][rc(2)][...data...][crc(2)]

Application level exchanges: Request format:

R_WBOO:	snd: [25][va(2)][act][1][value]

rcv: [25][rc(2)]

R_WANA:	snd: [26][va(2)][act][1][value(4)]

rcv: [26][rc(2)]

R_WTMR:	snd: [27][va(2)][0][1][value(4)]

rcv: [27][rc(2)]

R_WMSG:	snd: [28][va(2)][act][1]

[No.c][value(s)][0]

rcv: [28][rc(2)]

R_TSTART:	snd: [30][1][va(2)]

rcv: [30][rc(2)]

R_TSTOP:	snd: [31][1][va(2)]

rcv: [31][rc(2)]

R_CC:   	snd: [32]

rcv: [32][rc(2)]

R_RT:   	snd: [33]

rcv: [33][rc(2)]

R_EC:   	snd: [34]

rcv: [34][rc(2)]

R_TUC:	snd: [35][1][va(2)]

rcv: [35][rc(2)]

R_TCC:	snd: [36][1][va(2)]

rcv: [36][rc(2)]

R_BKT:	snd: [23][va(2)][typ][ln(2)]

rcv: [23][rc(2)]

R_BKDEL:	snd: [40][1][va(2)]

rcv: [40][rc(2)]

R_BKDEL all:	snd: [40][0]

rcv: [40][rc(2)]

R_TCW:	snd: [43][timing(4)]

rcv: [43][rc(2)]

R_TCR:	snd: [44]

rcv: [44][rc(2)]

[smp(4)][cur(4)][max(4)][ovr(4)]

R_GSTART:	snd: [45][1][pnum]

rcv: [45][rc(2)]

R_GFREEZE:	snd: [46][1][pnum]

rcv: [46][rc(2)]

R_GKILL:	snd: [47][1][pnum]

rcv: [47][rc(2)]

R_GRST:	snd: [48][1][pnum]

rcv: [48][rc(2)]

R_GER:	snd: [53]

rcv: [53][rc(2)][code(2)][arg(2)]

R_UNLOCK:	snd: [55][1][va(2)]

rcv: [55][rc(2)]

R_UNLOCK all:	snd: [55][0]

rcv: [55][rc(2)]

R_LOCK:	snd: [57][1][va(2)]

rcv: [57][rc(2)]

R_LOCKR:	snd: [70]

rcv: [70][rc(2)][No.(2)] { [va(2)] }

R_APPL:	snd: [72]

rcv: [72][rc(2)]

[vers(2)][dttm(4)][crc(4)]

R_UPMDF:	snd: [62]

rcv: [62][rc(2)]

R_RANY:	snd: [rq][No.] { [va(2)] [act]}

rcv: [rq][rc(2)][AB][CD]

[No.] { [typ][values(?)] }

R_RANY: format of values:

1=boolean	[boo_val] (0=false / 1=true)

2=analog	[anaval(4)]

3=timer	[tmrval(4)]

4=string	[len][characters(s)][0]

5=program	[state]

(0=inact. / 1=act. / 3= frozen)

7=step	[state]

(80h=bk_act | 40h=bk_de | 01h=activity)

8=transition	[state] (80h=breakpoint | 01h=validity)

15=appli error	[code(2)][arg(2)]

# Appendix 4 : C code definition

## Introduction

ISaGRAF V3.04 or later allows the generation of various target codes. One of them is the C code which can be compiled with the ISaGRAF Kernel.

This manual contains detailed information about the contents of the files generated by the C code generator. In particular, all the tables and data structures generated are described as are the set of C code instructions produced.

This document assumes user knowledge of certain concepts. The knowledge prerequisites are :

- ISaGRAF architecture

- TIC code.

For further information on these concepts you can consult the official documents on ISaGRAF.

## General principle of C code generation

### Principle

The aim of the C code generation is to produce one executable file including the application written with ISaGRAF Workbench and ISaGRAF Kernel. This executable file is able to run on the chosen target.

To achieve it, the application ; programs and I/O connections etc. are translated into C code files. These files are compiled and linked with ISaGRAF Kernel across a C compiler compatible with the target, to obtain an executable file.

The compilation technique (as opposed to the interpretation technique) suppresses a few functions:

- on-line modification

It’s impossible to modify an application during its execution.

- breakpoints

It’s impossible to put breakpoints into processing code (IL, ST, FBD, LD).

- resources management

In this version of C code generator, the resource management is not supported, because it does not represent a great interest.

- automatic downloads

The generated code must be manually downloaded.

## Architecture

Translating an ISaGRAF application creates two files named : appli.h and appli.c. appli.h is an include file which contains external declarations only used by ISaGRAF Kernel. Appli.c is a source file which contains the data and the code of application.

This chapter describes the data structures and C instructions generated.

### Compliance

For obvious reasons normalized C code (according to C-Ansi) is generated.

### Data representation

Data represents the application parameters for the Kernel : number of variables for each type, number of steps or transitions in SFC charts, etc.

Data is represented by structures and organized in tables. The size of tables depends on the application. Therefore, the size of data structures is wholly defined.

All the tables are defined with a global scope but they are initialized by function. The access to these tables is ' read only ' to the rest of the Kernel.

### Code representation

Application code represents the translation of the application instructions described with the IEC 1131-3 language (IL, ST, FBD, LD) into C code.

A subset of the C language is generated by the C code generator. This chapter describes all the possibilities of these generated C code instructions.

#### Set of the basic C instructions

This chapter syntactically describes the set of basic C instructions used by the C code generator.

##### Variables

The variables employed in the instructions can represent a single-element or multi-elements.

A single-element is a value or an address. A multi-element is an array.

##### Operation instructions

- Assignment instruction

<variable> = <variable> ;

- Unary operator

<variable> = - <variable> ;

<variable> = !<variable> ;

- Binary analog operator

<variable> = <variable> + <variable> ;

<variable> = <variable> * <variable> ;

<variable> = <variable> - <variable> ;

<variable> = <variable> / <variable> ;

- Binary Boolean operator

The result of a Boolean expression is stored in a Boolean variable. For ISaGRAF Kernel, a Boolean is represented by an unsigned char (uchar). Also, all the Boolean expressions are converted to uchar type.

<variable> = (uchar)(<variable> > <variable>);

<variable> = (uchar)(<variable> <= <variable>);

<variable> = (uchar)(<variable> >= <variable>);

<variable> = (uchar)(<variable> == <variable>);

<variable> = (uchar)(<variable> != <variable>);

<variable> = (uchar)(<variable> | <variable>);

<variable> = (uchar)(<variable> & <variable>);

<variable> = (uchar)(<variable> ^ <variable>);

##### Control instructions

- if

if (<expression>) goto <label>

if ( !(<expression>) ) goto <label>

if (<expression>) { <instructions> } else { <instructions> }

- goto

goto <label>

- label

<identifier> :

- return

return ((unsigned char) (<expression> ))

- switch

switch ( <ana_expression> ) { { case <value> : <instruction> ; break; } default : <instruction> break; }

### Function call of Kernel

The following functions are defined in the kernel. They can be called in appli.c.

| Management | Function prototype |
| --- | --- |
| TIC code | uchar tic_dec(uint16 *) |
|  | extern uint16 *blk_seq(uint16); |
|  | void tic_cnv( uint16,uint16,uint16,uint16) |
| I/O access | void ios_ana_ref(uint16) |
|  | void ios_boo_ref(uint16) |
|  | void ios_msg_ref(uint16) |
| SFC evolution | uchar evo_sfc_start(uchar) |
|  | uchar evo_sfc_rstart(uchar) |
|  | uchar evo_sfc_kill(uchar) |
|  | uchar evo_sfc_freeze(uchar) |
|  | uchar ste_testact(uint16) |
|  | uint32 ste_readtim(uint16) |
| Timer | uchar tmr_active(uint16) |
|  | uchar tmr_deactive(uint16) |
|  | uint32 tmr_read(uint16) |
|  | void tmr_write(uint16, uint32); |
|  | void tmr_duplicate(uint16, uint16); |
| Message | uchar msg_len (uint16) |
|  | void msg_concat (uint16, uint16, uint16) |
|  | uchar msg_equ (uint16, uint16) |
|  | uchar msg_lexcmp (uint16, uint16) |
|  | void msg_set(uint16, uint16) |
|  | void msg_write(uint16, uchar, uchar *) |
|  | uchar sys_strlen(char*) |
| Function and | int32 usf_mic(uint16, uint16 *, uchar *) |
| Function Block | int32 usf_std(uint16, uint16 *, uchar *) |
|  | void fbl_active(uint16, uint16, uint16 *, uchar *) |
|  | void fbl_std(uint16, uint16, uint16 *) |
|  | int32 fbl_readpa(uint16, uint16, uint16) |
| Program | extern uchar prg_get_status(uchar) |
| System | int32 sys_call(int32, int32) |
|  | void sys_err(uint16,uint16) |
| I/O special process | int32 ios_boo_operate(uint16, int32, int32 ) |
|  | int32 ios_ana_operate(uint16, int32, int32) |
|  | int32 ios_msg_operate(uint16, int32, int32) |

### TIC code representation

The translation method is to translate each TIC code into a list of C instructions. The following table details the correspondence between TIC code and C code.

Notation :

- op1, op2, op3 and op4 are index values resolved by ISaGRAF linker.

- label is an identifier generated by the C code generator.

- Index is a value generated by the C code generator.

| TIC code | Corresponding C code |
| --- | --- |
| TIC_OUT_A1SI | ios_ana_ref(op1); BF_ANA[op1] = -BF_ANA[op2]; |
| TIC_A1SI | BF_ANA[op1] = -BF_ANA[op2]; |
| TIC_OUT_A1NO. | ios_boo_ref(op1); BF_BOO[op1] = !BF_BOO[op2]; |
| TIC_A1NO. | BF_BOO[op1] = !BF_BOO[op2]; |
| TIC_OUT_A2MI | ios_ana_ref(op1); BF_ANA[op1] = BF_ANA[op2] * BF_ANA[op3]; |
| TIC_A2MI | BF_ANA[op1] = BF_ANA[op2] * BF_ANA[op3]; |
| TIC_OUT_A2LTI | ios_boo_ref(op1); BF_BOO[op1] = (unsigned char) (BF_ANA[op2] < BF_ANA[op3]); |
| TIC_A2LTI | BF_BOO[op1] = (unsigned char) (BF_ANA[op2] < BF_ANA[op3]); |
| TIC_OUT_A2DI | ios_ana_ref(op1); if (BF_ANA[op3]) { BF_ANA[op1] = BF_ANA[op2] / BF_ANA[op3] ; } else { sys_err(64L,op3 ¦ 0x2000L); if (BF_ANA[op2] > 0 ) { BF_ANA[op1] = MAX_INT; } else { BF_ANA[op1] = - MAX_INT; } ; } ; |
| TIC_A2DI | if (BF_ANA[op3]) { BF_ANA[op1] = BF_ANA[op2] / BF_ANA[op3] ; } else { sys_err(64L,op3 ¦ 0x2000L); if (BF_ANA[op2] > 0 ) { BF_ANA[op1] = MAX_INT; } else { BF_ANA[op1] = - MAX_INT; } ; } ; |
| TIC_OUT_A2AI | ios_ana_ref(op1); BF_ANA[op1] = BF_ANA[op2] + BF_ANA[op3]; |
| TIC_A2AI | BF_ANA[op1] = BF_ANA[op2] + BF_ANA[op3]; |
| TIC_OUT_A2SI | ios_ana_ref(op1); BF_ANA[op1] = BF_ANA[op2] - BF_ANA[op3]; |
| TIC_A2SI | BF_ANA[op1] = BF_ANA[op2] - BF_ANA[op3]; |
| TIC_OUT_A1SR | ios_ana_ref(op1); ((floating point*)BF_ANA)[op1] = -((floating point*)BF_ANA)[op2]; |
| TIC_A1SR | ((floating point*)BF_ANA)[op1] = -((floating point*)BF_ANA)[op2]; |
| TIC_OUT_A2MR | ios_ana_ref(op1); ((floating point*)BF_ANA)[op1] = ((floating point*)BF_ANA)[op2] * ((floating point*)BF_ANA)[op3]; |
| TIC_A2MR | ((floating point*)BF_ANA)[op1] = ((floating point*)BF_ANA)[op2] * ((floating point*)BF_ANA)[op3]; |
| TIC_OUT_A2DR | ios_ana_ref(op1); if (((floating point*)BF_ANA)[op3]) { ((floating point*)BF_ANA)[op1] = ((floating point*)BF_ANA)[op2] / ((floating point*)BF_ANA)[op3] ; } else { sys_err(64L,op3 ¦ 0x2000L); if (((floating point*)BF_ANA)[op2] > 0 ) { ((floating point*)BF_ANA)[op1] = MAX_REA; } else { ((floating point*)BF_ANA)[op1] = - MAX_REA; } ; } ; |
| TIC_A2DR | if (((floating point*)BF_ANA)[op3]) { ((floating point*)BF_ANA)[op1] = ((floating point*)BF_ANA)[op2] / ((floating point*)BF_ANA)[op3] ; } else { sys_err(64L,op3 ¦ 0x2000L); if (((floating point*)BF_ANA)[op2] > 0 ) { ((floating point*)BF_ANA)[op1] = MAX_REA; } else { ((floating point*)BF_ANA)[op1] = - MAX_REA; } ; } ; |
| TIC_OUT_A2AR | ios_ana_ref(op1); ((floating point*)BF_ANA)[op1] = ((floating point*)BF_ANA)[op2] + ((floating point*)BF_ANA)[op3]; |
| TIC_A2AR | ((floating point*)BF_ANA)[op1] = ((floating point*)BF_ANA)[op2] + ((floating point*)BF_ANA)[op3]; |
| TIC_OUT_A2SR | ios_ana_ref(op1); ((floating point*)BF_ANA)[op1] = ((floating point*)BF_ANA)[op2] - ((floating point*)BF_ANA)[op3]; |
| TIC_A2SR | ((floating point*)BF_ANA)[op1] = ((floating point*)BF_ANA)[op2] - ((floating point*)BF_ANA)[op3]; |
| TIC_OUT_A2LTR | ios_boo_ref(op1); BF_BOO[op1] = (unsigned char) (((floating point*)BF_ANA)[op2] < ((floating point*)BF_ANA)[op3]); |
| TIC_A2LTR | BF_BOO[op1] = (unsigned char) (((floating point*)BF_ANA)[op2] < ((floating point*)BF_ANA)[op3]); |
| TIC_OUT_A2GTR | ios_boo_ref(op1); BF_BOO[op1] = (unsigned char) (((floating point*)BF_ANA)[op2] > ((floating point*)BF_ANA)[op3]); |
| TIC_A2GTR | BF_BOO[op1] = (unsigned char) (((floating point*)BF_ANA)[op2] > ((floating point*)BF_ANA)[op3]); |
| TIC_OUT_A2LER | ios_boo_ref(op1); BF_BOO[op1] = (unsigned char) (((floating point*)BF_ANA)[op2] <= ((floating point*)BF_ANA)[op3]); |
| TIC_A2LER | BF_BOO[op1] = (unsigned char) (((floating point*)BF_ANA)[op2] <= ((floating point*)BF_ANA)[op3]); |
| TIC_OUT_A2GER | ios_boo_ref(op1); BF_BOO[op1] = (unsigned char) (((floating point*)BF_ANA)[op2] >= ((floating point*)BF_ANA)[op3]); |
| TIC_A2GER | BF_BOO[op1] = (unsigned char) (((floating point*)BF_ANA)[op2] >= ((floating point*)BF_ANA)[op3]); |
| TIC_OUT_A2EQR | ios_boo_ref(op1); BF_BOO[op1] = (unsigned char) (((floating point*)BF_ANA)[op2] == ((floating point*)BF_ANA)[op3]); |
| TIC_A2EQR | BF_BOO[op1] = (unsigned char) (((floating point*)BF_ANA)[op2] == ((floating point*)BF_ANA)[op3]); |
| TIC_OUT_A2NER | ios_boo_ref(op1); BF_BOO[op1] = (unsigned char) (((floating point*)BF_ANA)[op2] != ((floating point*)BF_ANA)[op3]); |
| TIC_A2NER | BF_BOO[op1] = (unsigned char) (((floating point*)BF_ANA)[op2] != ((floating point*)BF_ANA)[op3]); |
| TIC_OUT_A3R | ios_ana_ref(op1); ((floating point*)BF_ANA)[op1] = ((floating point*)BF_ANA)[op2]; |
| TIC_A3R | ((floating point*)BF_ANA)[op1] = ((floating point*)BF_ANA)[op2]; |
| TIC_A4R | tic_dec(blk_seq(op2)); ((floating point*)BF_ANA)[op1] = LGC_RET_SUB; |
| TIC_SYS_GPARR | BF_ANA[op1] = BF_ANA[LGC_P_NUM[op2 - 1L]]; |
| TIC_SYS_PPARR | LGC_RET_SUB = BF_ANA[op2]; |
| TIC_TRS_A2LTR | return ((unsigned char)( (((floating point*)BF_ANA)[op2] < ((floating point*)BF_ANA)[op3]))); |
| TIC_TRS_A2GTR | return ((unsigned char)( (((floating point*)BF_ANA)[op2] > ((floating point*)BF_ANA)[op3]))); |
| TIC_TRS_A2LER | return ((unsigned char)( (((floating point*)BF_ANA)[op2] <= ((floating point*)BF_ANA)[op3]))); |
| TIC_TRS_A2GER | return ((unsigned char)( (((floating point*)BF_ANA)[op2] >= ((floating point*)BF_ANA)[op3]))); |
| TIC_TRS_A2EQR | return ((unsigned char)( (((floating point*)BF_ANA)[op2] == ((floating point*)BF_ANA)[op3]))); |
| TIC_TRS_A2NER | return ((unsigned char)( (((floating point*)BF_ANA)[op2] != ((floating point*)BF_ANA)[op3]))); |
| TIC_A2AT | tmr_write(op1, tmr_read(op2) + tmr_read(op3)); |
| TIC_OUT_A2LTT | ios_boo_ref(op1); BF_BOO[op1] = (unsigned char) (tmr_read(op2) < tmr_read(op3)); |
| TIC_A2LTT | BF_BOO[op1] = (unsigned char) (tmr_read(op2) < tmr_read(op3)); |
| TIC_OUT_A2GTT | ios_boo_ref(op1); BF_BOO[op1] = (unsigned char) (tmr_read(op2) > tmr_read(op3)); |
| TIC_A2GTT | BF_BOO[op1] = (unsigned char) (tmr_read(op2) > tmr_read(op3)); |
| TIC_OUT_A2LET | ios_boo_ref(op1); BF_BOO[op1] = (unsigned char) (tmr_read(op2) <= tmr_read(op3)); |
| TIC_A2LET | BF_BOO[op1] = (unsigned char) (tmr_read(op2) <= tmr_read(op3)); |
| TIC_A2ST | tmr_write(op1, tmr_read(op2) - tmr_read(op3)); |
| TIC_OUT_A2GET | ios_boo_ref(op1); BF_BOO[op1] = (unsigned char) (tmr_read(op2) >= tmr_read(op3)); |
| TIC_A2GET | BF_BOO[op1] = (unsigned char) (tmr_read(op2) >= tmr_read(op3)); |
| TIC_OUT_A2EQT | ios_boo_ref(op1); BF_BOO[op1] = (unsigned char) (tmr_read(op2) == tmr_read(op3)); |
| TIC_A2EQT | BF_BOO[op1] = (unsigned char) (tmr_read(op2) == tmr_read(op3)); |
| TIC_OUT_A2NET | ios_boo_ref(op1); BF_BOO[op1] = (unsigned char) (tmr_read(op2) != tmr_read(op3)); |
| TIC_A2NET | BF_BOO[op1] = (unsigned char) (tmr_read(op2) != tmr_read(op3)); |
| TIC_A3T | tmr_write(op1, tmr_read(op2)); |
| TIC_A4T | tic_dec(blk_seq(op2)); tmr_write(op1, LGC_RET_SUB); |
| TIC_SYS_GPART | tmr_write(op1, tmr_read(LGC_P_NUM[op2 - 1L]) ); |
| TIC_SYS_PPART | LGC_RET_SUB = tmr_read(op2); |
| TIC_SYS_A3T | tmr_duplicate(op1,op2) ; |
| TIC_SYS_TSTART | tmr_active(LGC_P_NUM[0L]); |
| TIC_SYS_TSTOP | tmr_deactive(LGC_P_NUM[0L]); |
| TIC_TRS_A2LTT | return ((unsigned char)( (tmr_read(op2) < tmr_read(op3)))); |
| TIC_TRS_A2GTT | return ((unsigned char)( (tmr_read(op2) > tmr_read(op3)))); |
| TIC_TRS_A2LET | return ((unsigned char)( (tmr_read(op2) <= tmr_read(op3)))); |
| TIC_TRS_A2GET | return ((unsigned char)( (tmr_read(op2) >= tmr_read(op3)))); |
| TIC_TRS_A2EQT | return ((unsigned char)( (tmr_read(op2) == tmr_read(op3)))); |
| TIC_TRS_A2NET | return ((unsigned char)( (tmr_read(op2) != tmr_read(op3)))); |
| TIC_OUT_A2AM | ios_msg_ref (op1); msg_concat (op1, op2,op3); |
| TIC_A2AM | msg_concat (op1, op2,op3); |
| TIC_OUT_A2LTM | ios_boo_ref(op1); BF_BOO[op1] = (unsigned char) (msg_lexcmp(op2,op3,' == 2')); |
| TIC_A2LTM | BF_BOO[op1] = (unsigned char) (msg_lexcmp(op2,op3,' == 2')); |
| TIC_OUT_A2GTM | ios_boo_ref(op1); BF_BOO[op1] = (unsigned char) (msg_lexcmp(op2,op3,' == 4')); |
| TIC_A2GTM | BF_BOO[op1] = (unsigned char) (msg_lexcmp(op2,op3,' == 4')); |
| TIC_OUT_A2LEM | ios_boo_ref(op1); BF_BOO[op1] = (unsigned char) (msg_lexcmp(op2,op3,' != 4')); |
| TIC_A2LEM | BF_BOO[op1] = (unsigned char) (msg_lexcmp(op2,op3,' != 4')); |
| TIC_OUT_A2GEM | ios_boo_ref(op1); BF_BOO[op1] = (unsigned char) (msg_lexcmp(op2,op3,' != 2')); |
| TIC_A2GEM | BF_BOO[op1] = (unsigned char) (msg_lexcmp(op2,op3,' != 2')); |
| TIC_OUT_A2EQM | ios_boo_ref(op1); BF_BOO[op1] = (unsigned char) (msg_equ(op2,op3)); |
| TIC_A2EQM | BF_BOO[op1] = (unsigned char) (msg_equ(op2,op3)); |
| TIC_OUT_A2NEM | ios_boo_ref(op1); BF_BOO[op1] = (unsigned char) (!msg_equ(op2,op3)); |
| TIC_A2NEM | BF_BOO[op1] = (unsigned char) (!msg_equ(op2,op3)); |
| TIC_OUT_A3M | ios_msg_ref (op1); msg_set(op1,op2); |
| TIC_A3M | msg_set(op1,op2); |
| TIC_SYS_GPARM | msg_set(op1, LGC_P_NUM[op2 -1]); |
| TIC_TRS_A2LTM | return ((unsigned char)((unsigned char) (msg_lexcmp(op2,op3) == 2))); |
| TIC_TRS_A2GTM | return ((unsigned char)((unsigned char) (msg_lexcmp(op2,op3) == 4))); |
| TIC_TRS_A2LEM | return ((unsigned char)((unsigned char) (msg_lexcmp(op2,op3) != 4))); |
| TIC_TRS_A2GEM | return ((unsigned char)((unsigned char) (msg_lexcmp(op2,op3) != 2))); |
| TIC_TRS_A2EQM | return ((unsigned char)((unsigned char) (msg_equ(op2,op3)))); |
| TIC_TRS_A2NEM | return ((unsigned char)((unsigned char) (!msg_equ(op2,op3)))); |
| TIC_OUT_A2GTI | ios_boo_ref(op1); BF_BOO[op1] = (unsigned char) (BF_ANA[op2] > BF_ANA[op3]); |
| TIC_A2GTI | BF_BOO[op1] = (unsigned char) (BF_ANA[op2] > BF_ANA[op3]); |
| TIC_OUT_A2LEI | ios_boo_ref(op1); BF_BOO[op1] = (unsigned char) (BF_ANA[op2] <= BF_ANA[op3]); |
| TIC_A2LEI | BF_BOO[op1] = (unsigned char) (BF_ANA[op2] <= BF_ANA[op3]); |
| TIC_OUT_A2GEI | ios_boo_ref(op1); BF_BOO[op1] = (unsigned char) (BF_ANA[op2] >= BF_ANA[op3]); |
| TIC_A2GEI | BF_BOO[op1] = (unsigned char) (BF_ANA[op2] >= BF_ANA[op3]); |
| TIC_OUT_A2EQI | ios_boo_ref(op1); BF_BOO[op1] = (unsigned char) (BF_ANA[op2] == BF_ANA[op3]); |
| TIC_A2EQI | BF_BOO[op1] = (unsigned char) (BF_ANA[op2] == BF_ANA[op3]); |
| TIC_OUT_A2EQB | ios_boo_ref(op1); BF_BOO[op1] = (unsigned char) (BF_BOO[op2] == BF_BOO[op3]); |
| TIC_A2EQB | BF_BOO[op1] = (unsigned char) (BF_BOO[op2] == BF_BOO[op3]); |
| TIC_OUT_A2NEI | ios_boo_ref(op1); BF_BOO[op1] = (unsigned char) (BF_ANA[op2] != BF_ANA[op3]); |
| TIC_A2NEI | BF_BOO[op1] = (unsigned char) (BF_ANA[op2] != BF_ANA[op3]); |
| TIC_OUT_A2NEB | ios_boo_ref(op1); BF_BOO[op1] = (unsigned char) (BF_BOO[op2] != BF_BOO[op3]); |
| TIC_A2NEB | BF_BOO[op1] = (unsigned char) (BF_BOO[op2] != BF_BOO[op3]); |
| TIC_OUT_A2ORB | ios_boo_ref(op1); BF_BOO[op1] = (unsigned char) (BF_BOO[op2] ¦ BF_BOO[op3]); |
| TIC_A2ORB | BF_BOO[op1] = (unsigned char) (BF_BOO[op2] ¦ BF_BOO[op3]); |
| TIC_OUT_A2ANO. | ios_boo_ref(op1); BF_BOO[op1] = (unsigned char) (BF_BOO[op2] & BF_BOO[op3]); |
| TIC_A2ANO. | BF_BOO[op1] = (unsigned char) (BF_BOO[op2] & BF_BOO[op3]); |
| TIC_OUT_A2XOB | ios_boo_ref(op1); BF_BOO[op1] = (unsigned char) (BF_BOO[op2] ^ BF_BOO[op3]); |
| TIC_A2XOB | BF_BOO[op1] = (unsigned char) (BF_BOO[op2] ^ BF_BOO[op3]); |
| TIC_OUT_A3B | ios_boo_ref(op1); BF_BOO[op1] = BF_BOO[op2]; |
| TIC_A3B | BF_BOO[op1] = BF_BOO[op2]; |
| TIC_OUT_A3I | ios_ana_ref(op1); BF_ANA[op1] = BF_ANA[op2]; |
| TIC_A3I | BF_ANA[op1] = BF_ANA[op2]; |
| TIC_USF_A4B | LGC_P_TYP [index] = 0; BF_BOO[op1] = (unsigned char) (usf_mic(op2,&LGC_P_NUM[0],&LGC_P_TYP[0])); |
| TIC_STD_A4B | LGC_P_TYP [index] = 0; BF_BOO [op1] = (unsigned char) (usf_std (op2,&LGC_P_NUM[0],&LGC_P_TYP[0])); |
| TIC_USF_A4I | LGC_P_TYP_ [index] = 0; BF_ANA[op1] = usf_mic(op2,&LGC_P_NUM[0],&LGC_P_TYP[0]); |
| TIC_STD_A4I | LGC_P_TYP [index] = 0; BF_ANA[op1] = usf_std(op2,&LGC_P_NUM[0],&LGC_P_TYP[0]); |
| TIC_USF_A4R | LGC_P_TYP[index] = 0; BF_ANA[op1] = usf_mic(op2,&LGC_P_NUM[0],&LGC_P_TYP[0]); |
| TIC_STD_A4R | LGC_P_TYP[index] = 0 ; BF_ANA[op1] = usf_std(op2,&LGC_P_NUM[0],&LGC_P_TYP[0]); |
| TIC_USF_A4T | LGC_P_TYP[index] = 0; tmr_write((op1, usf_mic(op2,&LGC_P_NUM[0],&LGC_P_TYP[0])); |
| TIC_USF_A4M | LGC_P_TYP[index] = 0; msg_write(op1,sys_strlen(usf_mic(op2,&LGC_P_NUM[0],&LGC_P_TYP[0])), usf_mic(op2,&LGC_P_NUM[0],&LGC_P_TYP[0])); |
| TIC_STD_A4M | LGC_P_TYP[index] = 0; msg_write(op1,sys_strlen(usf_std(op2,&LGC_P_NUM[0],&LGC_P_TYP[0])), usf_std(op2,&LGC_P_NUM[0],&LGC_P_TYP[0])); |
| TIC_TRS_A4B | tic_dec(blk_seq(op2)) ; return ((unsigned char)( ((unsigned char) (LGC_RET_SUB)))); |
| TIC_OUT_A4B | ios_boo_ref(op1); tic_dec(blk_seq(op2)); BF_BOO[op1] = (unsigned char) (LGC_RET_SUB); |
| TIC_A4B | tic_dec(blk_seq(op2)); BF_BOO[op1] = (unsigned char) (LGC_RET_SUB); |
| TIC_OUT_A4I | ios_ana_ref(op1); |
| TIC_A4I | tic_dec(blk_seq(op2)); BF_ANA[op1] = LGC_RET_SUB; |
| TIC_OUT_A4M | ios_msg_ref (op1); tic_dec(blk_seq(op2)); msg_set(op1,(unsigned char) (LGC_RET_SUB)); |
| TIC_A4M | tic_dec(blk_seq(op2)); msg_set(op1,(unsigned char) (LGC_RET_SUB)); |
| TIC_FBL | LGC_P_TYP [index] = 0; fbl_active( op1, op2, &LGC_P_NUM[0], &LGC_P_TYP[0]); |
| TIC_STD_FBL | fbl_std(op1, op2, &LGC_P_NUM[0]); |
| TIC_SYS_GPARBLKB | BF_BOO[op1] = (unsigned char) (fbl_readpa(op3, op4, op2 )); |
| TIC_SYS_GPARBLKI | BF_ANA[op1] = fbl_readpa(op3, op4, op2 ); |
| TIC_SYS_GPARBLKR | BF_ANA[op1] = fbl_readpa(op3, op4, op2 ); |
| TIC_SYS_GPARBLKT | tmr_write((op1, fbl_readpa(op3, op4, op2 ) ); |
| TIC_SYS_GPARBLKM | msg_write(op1,sys_strlen(fbl_readpa(op3,op4,op2 )),fbl_readpa(op3,op4,op2)); |
| TIC_C1B | if (BF_BOO[op1] ) goto label; |
| TIC_C2B | if (!(BF_BOO[op1])) goto label |
| TIC_I1 | goto label |
| TIC_I2 | return ((unsigned char)( 0 )); |
| TIC_P1S | LGC_P_NUM[index] = op1; |
| TIC_P1C | LGC_P_NUM[index] = op1; |
| TIC_P1F | LGC_P_NUM[index] = op1; |
| TIC_P1B | LGC_P_TYP[index] = BOO; LGC_P_NUM[index] = op1; |
| TIC_P1I | LGC_P_TYP[index] = ANA; LGC_P_NUM[index] = op1; |
| TIC_P1R | LGC_P_TYP[index] = REA; LGC_P_NUM[index] = op1; |
| TIC_P1T | LGC_P_TYP[index] = TMR; LGC_P_NUM[index] = op1; |
| TIC_P1M | LGC_P_TYP [index] = MSG; LGC_P_NUM [index] = op1; |
| TIC_L1 | label : |
| TIC_SYS_GPARB | BF_BOO[op1] = BF_BOO[LGC_P_NUM[op2 - 1L]]; |
| TIC_SYS_GPARI | BF_ANA[op1] = BF_ANA[LGC_P_NUM[op2 - 1L]]; |
| TIC_SYS_PPARB | LGC_RET_SUB = BF_BOO[op2]; |
| TIC_SYS_PPARI | LGC_RET_SUB = BF_ANA[op2]; |
| TIC_SYS_PPARM | LGC_RET_SUB = op2; |
| TIC_TRS_PPARB | return ((unsigned char)( BF_BOO[op2])); |
| TIC_SYS_GSTART | evo_sfc_start((unsigned char) LGC_P_NUM[0L]); |
| TIC_SYS_GFREEZE | evo_sfc_freeze((unsigned char) LGC_P_NUM[0L]); |
| TIC_SYS_GKILL | evo_sfc_kill((unsigned char) LGC_P_NUM[0L]); |
| TIC_SYS_GRST | evo_sfc_rstart((unsigned char) LGC_P_NUM[0L]); |
| TIC_OUT_GSTATUS | ios_ana_ref(op1); BF_ANA[op1] = prg_get_status((unsigned char)LGC_P_NUM[0]); |
| TIC_SYS_GSTATUS | BF_ANA[op1] = prg_get_status((unsigned char)LGC_P_NUM[0]); |
| TIC_SYS_OPERATE | LGC_P_TYP[index] = 0; switch (LGC_P_TYP[0L]) { case BOO : BF_ANA[op1] = ios_boo_operate(LGC_P_NUM[0], BF_ANA[LGC_P_NUM[2]], BF_ANA[LGC_P_NUM[1]]); break; case ANA : BF_ANA[op1] = ios_ana_operate(LGC_P_NUM[0], BF_ANA[LGC_P_NUM[2]], BF_ANA[LGC_P_NUM[1]]) ; break; case REA : BF_ANA[op1] = ios_ana_operate(LGC_P_NUM[0], BF_ANA[LGC_P_NUM[2]], BF_ANA[LGC_P_NUM[1]]) ; break; case MSG : BF_ANA[op1] = ios_msg_operate(LGC_P_NUM[0], BF_ANA[LGC_P_NUM[2]], BF_ANA[LGC_P_NUM[1]]) ; break; default : sys_err(69L,1L); break; } |
| TIC_SYS_FEDGE | LGC_BVAL = BF_BOO(LGC_P_NUM[0L]); BF_BOO[op1] = (unsigned char) ( !BF_BOO(LGC_P_NUM[0L]) & BF_BOO(LGC_P_NUM[1L])); BF_BOO(LGC_P_NUM[1L] = LGC_BVAL; |
| TIC_SYS_REDGE | LGC_BVAL = BF_BOO(LGC_P_NUM[0L]); BF_BOO[op1] = (unsigned char) (BF_BOO(LGC_P_NUM[0L]) & !BF_BOO(LGC_P_NUM[1L])); BF_BOO(LGC_P_NUM[1L] = LGC_BVAL; |
| TIC_OUT_CNV | switch(op1) { case:TIC_BOO: ios_boo_ref(op1); break; case:TIC_ANA: ios_ana_ref(op1); break; case:TIC_MSG: ios_msg_ref (op1); break; default: sys_err(14L,7L); break; } tic_cnv(LGC_P_NUM[0],op1,op2,op3 ); |
| TIC_SYS_CNV | tic_cnv(LGC_P_NUM[0],op1,op2,op3 ); |
| TIC_SYS_TAC | BF_BOO[op1] = (unsigned char) (ste_testact(op2)); |
| TIC_SYS_DAC | tmr_write(op1, ste_readtim(op2)); |
| TIC_SYS_SYSTEM | BF_ANA[op1] = sys_call(BF_ANA[LGC_P_NUM[0]],BF_ANA[LGC_P_NUM[1]]); |
| TIC_TRS_A1NO. | return ((unsigned char)( !BF_BOO[op2])); |
| TIC_TRS_A2LTI | return ((unsigned char)( (BF_ANA[op2] < BF_ANA[op3]))); |
| TIC_TRS_A2GTI | return ((unsigned char)( (BF_ANA[op2] > BF_ANA[op3]))); |
| TIC_TRS_A2LEI | return ((unsigned char)( (BF_ANA[op2] <= BF_ANA[op3]))); |
| TIC_TRS_A2GEI | return ((unsigned char)( (BF_ANA[op2] >= BF_ANA[op3]))); |
| TIC_TRS_A2EQI | return ((unsigned char)( (BF_ANA[op2] == BF_ANA[op3]))); |
| TIC_TRS_A2NEI | return ((unsigned char)( (BF_ANA[op2] != BF_ANA[op3]))); |
| TIC_TRS_A2EQB | return ((unsigned char)( (BF_BOO[op2] == BF_BOO[op3]))); |
| TIC_TRS_A2NEB | return ((unsigned char)( (BF_BOO[op2] != BF_BOO[op3]))); |
| TIC_TRS_A2ORB | return ((unsigned char)( (BF_BOO[op2] ¦ BF_BOO[op3]))); |
| TIC_TRS_A2ANO. | return ((unsigned char)( (BF_BOO[op2] & BF_BOO[op3]))); |
| TIC_TRS_A2XOB | return ((unsigned char)( (BF_BOO[op2] ^ BF_BOO[op3]))); |
| TIC_TRS_A3B | return ((unsigned char)( BF_BOO[op2])); |
| TIC_END_BLOCK | return ((unsigned char)( 0 )); |

## Description of generated files

This chapter describes wholly the generated files.

### Appli.h structure

Appli.h contains all the declarations in external mode of data and functions defined in appli.c and used by the Kernel. Also, it is not necessary to include appli.h in appli.c.

### Appli.c structure

Appli.c is structured in two parts : a declaration zone and a definition zone. The first part contains all the declarations : data structures, tables, functions etc. The second part consists of functions which contain the application code and the initialization of the data tables.

|  | Include |
| --- | --- |
|  | Data structures and tables |
|  | External functions |
|  | External data |
|  | Static data |
|  | Declaration of the initialization functions |
|  | Declaration of the processing code functions |
|  | Initialization code |
|  | Application code |

#### Include

This section contains all the target Includes useful for the file compilation. These Includes are the same for all C code files generated.

Includes need in appli.c

#include <tasy0def.h>

#include <take0pro.h>

#include <take0blk.h>

#include <take0ste.h>

#include <take0msg.h>

#include <take0prg.h>

#include <tasy0apl.h>

#include <taio0def.h>

#### Data structures and tables

This section declares  the data structures and the tables which contain them.

The number and the size of these tables depend on the application.

##### Specification of the description

The following table specifies the notation used to describe the tables and data structures.

| Data type | Size in bytess | Corresponding ' C ' type | Comments |
| --- | --- | --- | --- |
| uint16 | 2 | unsigned short |  |
| int32 | 4 | long |  |
| uint32 | 4 | unsigned long | can contain an address |
| uchar | 1 | unsigned char |  |
| charx | x | char t[x] | x depends on the application |

##### Data structure and table descriptions

###### List of Tables

The following table contains the list of tables generated in appli.c. For each table, the size (in bytes) is calculated. Sometimes, the table size is not fixed, it is application dependant. In these cases, the table size is represented by a formula containing a variable 'x'.

| Name Table | Size (bytes) | Comments |
| --- | --- | --- |
| __MAIN | 64 |  |
| __DEFPROD | 24 |  |
| __DEFAPPLI | 32 |  |
| __DEFUSF | 4+12x | x = number of functions |
| __DEFFBL | 6+16x | x = number of blocks |
| __DEFFCNV | 4+16x | x = number of conversion functions |
| __DEFTCNV | 4+8x | x = number of tables |
| __DEFVAR | 32 |  |
| __CODEVAR | 36 |  |
| __INITBOO | 2x | x = number of Boolean variables to be set |
| __INITANA | 6x | x = number of analogs to be initialized |
| __INITTMR | 6x | x = number of timers to be initialized |
| __INITMSG | 7x | x = number of messages to be initialized |
| __LNGMSG | x | x = number of messages |
| __DEFMODBUS | 16 | the information are not structured |
| __DEFMDBBOO | 2x | x = number of Boolean variables Modbus |
| __DEFMDBANA | 2x | x = number of analogs Modbus |
| __DEFMDBTMR | 2x | x = number of timers Modbus |
| __DEFMDBMSG | 2x | x = number of messages Modbus |
| __BACKUP | 80 |  |
| __DEFOEM | 6 |  |
| __CODEOEM | 16 |  |
| __DEFBOO | 8x | x = number of I/O Boolean variables |
| __DEFANA | 8x | x = number of I/O analogs |
| __DEFMSG | 8x | x = number of I/O messages |
| __DEFBRD | 4x | x = number of board |
| __DEFBRD_n | 14+ 2m (if type = uint16) 16+ 4m (if type = uint32) 28+ 16m (if type=16 uchar) | m = number of specific fields |
| __DEFHIE | 12+2x | x=begin+end+main+child+function |
| __DEFPROG | 2x | x = number of programs * 2 |
| __CODEPROG | 4x | x = number of programs |
| __PrgName_CODE | 4x | x = number of block programs |
| __LINKSFC | 4x | x = number of programs |
| __PrgName_LINK | 2x | x = depend of SFC structures |
| __RESSOURCE | x |  |

###### Table hierarchies

To improve the understanding of the table organization, the following figure presents the hierarchy of the tables.

###### Detailed description

This chapter describes all the data structures and tables manipulated in appli.c. and includes:

- the structure of their elements

- the table declaration

- the table size in bytes

Table name : __MAIN

- Data structure

Structure defined in ' tasy0apl.h '

typedef struct

{

uint32 def_flag;

uint32 def_prod;

uint32 def_appli;

uint32 def_usf;

uint32 def_fbl;

uint32 def_fcnv;

uint32 def_tcnv;

uint32 def_var;

uint32 tab_init;

uint32 def_ios;

uint32 def_oem;

uint32 def_hie;

uint32 def_prog;

uint32 tab_code;

uint32 tab_link;

uint32 def_res;

}

str_header;

- Table declaration

str_header __MAIN;

- Table Size

16*4 = 64

Table name : __DEFPROD

- Data structure

Structure defined in ' tasy0apl.h '

typedef struct

{

char name[16];

char version[8];

}

str_def_prod;

- Table declaration

str_def_prod __DEFPROD;

Structure defined in ' tasy0apl.h '

- Table Size

24

Table name : __DEFAPPLI

- Data structure

Structure defined in ' tasy0apl.h '

typedef struct

{

char name[16];

uint32 date;

uint32 crc;

uint16 version;

uint16 error_level;

uint16 start_mode;

uint16 cycle_duration;

}

str_def_appli;

- Table declaration

str_def_appli __DEFAPPLI;

- Table Size

32

Table name : __DEFUSF

- Data structure

Structure defined in ' tasy0apl.h '

typedef struct

{

uint16 libno

char name[10];

}

str_dfusf;

Structure defined in ' appli.c ' and ' appli.h '

typedef struct

{

uint16 usfNo.;

uint16 reserved;

str_dfusf usf[x];

}

str_dfusf_head;

- Table declaration

str_dfusf_head __DEFUSF;

- Table Size

(2+2) + (2+10)*x = 4+12x

Table name : __DEFFBL

- Data structure

Structure defined in ' tasy0apl.h '

typedef struct

{

uint16 libno;

uint16 No.inst;

char name[12];

}

str_def_fbl;

Structure defined in ' appli.c ' and ' appli.h '

typedef struct

{

uint16 fblNo.;

uint16 reserved;

str_def_fbl fbl[x];

uint16 align16;

}

str_def_fbl_head;

- Table declaration

str_def_fbl_head __DEFFBL;

- Table Size

(2+2) + (2+2+12)*x + 2 = 6+16x

Table name : __DEFFCNV

- Data structure

Structure defined in ' tasy0apl.h '

typedef struct

{

uint16 libno;

uint16 reserve;

char name[10];

uint16 reserve2;

}

str_dfcnv;

Structure defined in ' appli.c ' and ' appli.h '

typedef struct

{

uint16 No.;

uint16 reserve;

str_dfcnv fcnv[x];

}

str_def_fcnv_head;

- Table declaration

str_def_fcnv_head __DEFFCNV;

- Table Size

(2+2)+(2+2+10+2)*x = 4+16x

Table name : __DEFTCNV

- Data structure

Structure defined in ' taio0tab.c ', ' appli.c ' and ' appli.h '

typedef struct

{

floating point x;

floating point y;

}

str_point;

Structure defined in ' appli.c ' and ' appli.h '

typedef struct

{

uint16 tabNo.;

uint16 No.pt;

str_point *pt;

}

str_dftcnv;

Structure defined in ' appli.c ' and ' appli.h '

typedef struct

{

uint16 No.;

uint16 reserve;

str_dftcnv tcnv[x];

}

str_def_tcnv_head;

- Table declaration

str_def_tcnv_head __DEFTCNV;

- Table Size

(2+2)+(2+2+4)*x = 4+8x

Table name : __DEFVAR

- Data structure

Structure defined in ' tasy0apl.h '

typedef struct

{

uint16 boo_int;

uint16 boo_inp;

uint16 boo_out;

uint16 reserve1;

uint16 ana_int;

uint16 ana_inp;

uint16 ana_out;

uint16 reserve2;

uint16 tmr_int;

uint16 reserve3;

uint16 reserve4;

uint16 reserve5;

uint16 msg_int;

uint16 msg_inp;

uint16 msg_out;

uint16 reserve6;

}

str_def_var;

- Table declaration

str_def_var __DEFVAR;

- Data size

2*16 = 32

Table name : __CODEVAR

- Data structure

Structure defined in ' tasy0apl.h '

typedef struct

{

uint32 init_boo;

uint32 init_ana;

uint32 init_tmr;

uint32 init_msg;

uint32 lng_msg;

uint32 def_mdb;

uint32 retain;

uint16 No._var_boo;

uint16 No._var_ana;

uint16 No._var_tmr;

uint16 No._var_msg;

}

str_def_init;

- Table declaration

str_def_init __CODEVAR;

- Table Size

4*7+ 4*2 = 36

Table name : __INITBOO

- Data structure

uint16

- Table declaration

uint16 __INITBOO[x];

- Table Size

2x

Table name : __INITANA

- Data structure

Structure defined in ' appli.c '

typedef struct

{

uint16 No.;

uint32 value;

}

str_init_ana;

- Table declaration

str_init_ana __INITANA[x];

- Data size

(2+4)x = 6x

Table name : __INITTMR

- Data structure

Structure defined in ' appli.c '

typedef struct

{

uint16 No.;

uint32 value;

}

str_init_tmr;

- Table declaration

str_init_tmr __INITTMR[x];

- Table Size

(2+4)x = 6x

Table name : __INITMSG

- Data structure

Structure defined in ' appli.c '

typedef struct

{

char *mes;

uint16 No.;

uchar len;

}

str_init_msg;

- Table declaration

str_init_msg __INITMSG[x];

- Table Size

(4+2+1)x = 7x

Table name : __LNGMSG

- Data structure

unsigned char

- Table declaration

unsigned char __LNGMSG [x];

- Table Size

1x = x

Table name : __DEFMODBUS

- Data structure

unsigned char

- Table declaration

unsigned char __DEFMODBUS [16];

- Table Size

16

Table name : __DEFMDBBOO

- Data structure

uint16

- Table declaration

uint16 __DEFMDBBOO [x];

- Table Size

2x

Table name : __DEFMDBANA

- Data structure

uint16

- Table declaration

uint16 __DEFMDBANA [x];

- Table Size

2x

Table name : __DEFMDBTMR

- Data structure

uint16

- Table declaration

uint16 __DEFMDBTMR [x];

- Table Size

2x

Table name : __DEFMDBMSG

- Data structure

uint16

- Table declaration

uint16 __DEFMDBMSG [x];

- Table Size

2x

Table name : __BACKUP

- Data structure

Structure defined in ' tasy0apl.h '

typedef struct

{

char param[64];

uint16 No._boo;

uint16 num_boo;

uint16 No._ana;

uint16 num_ana;

uint16 No._tmr;

uint16 num_tmr;

uint16 No._msg;

uint16 num_msg;

}

str_def_retain;

- Table declaration

str_def_retain __BACKUP;

- Table Size

64+(8*2) = 80

Table name : __DEFOEM

- Data structure

Structure defined in ' tasy0apl.h '

typedef struct

{

uint16 inp_brd;

uint16 out_brd;

uint16 cnv_real;

}

str_def_ios;

- Table declaration

str_def_ios __DEFOEM;

- Table Size

2*3 = 6

Table name : __CODEOEM

- Data structure

Structure defined in ' tasy0apl.h '

typedef struct

{

uint32 oem_boo;

uint32 oem_ana;

uint32 oem_msg;

uint32 oem_brd;

}

str_def_oem;

- Table declaration

str_def_ oem __ CODEOEM;

- Table Size

4*4 = 16

Table name : __DEFBOO

- Data structure

Structure defined in ' taio0def.h '

typedef struct

{

uint16 vnum;

uchar rack;

uchar slot;

uchar channel;

uchar out;

uchar conv_len;

uchar rea_ana;

}

str_dfvar;

- Table declaration

str_dfvar __DEFBOO[x];

- Table Size

(2+6)x = 8x

Table name : __DEFANA

- Data structure

Structure defined in ' taio0def.h '

typedef struct

{

uint16 vnum;

uchar rack;

uchar slot;

uchar channel;

uchar out;

uchar conv_len;

uchar rea_ana;

}

str_dfvar;

- Table declaration

str_dfvar __DEFANA[x];

- Table Size

(2+6)x = 8x

Table name : __DEFMSG

- Data structure

Structure defined in ' taio0def.h '

typedef struct

{

uint16 vnum;

uchar rack;

uchar slot;

uchar channel;

uchar out;

uchar conv_len;

uchar rea_ana;

}

str_dfvar;

- Table declaration

str_dfvar __DEFMSG[x];

- Table Size

(2+6)x = 8x

Table name : __DEFBRD

- Data structure

uchar *

- Table declaration

uchar *__DEFBRD[x];

- Table Size

4x

Table name : __DEFBRD_n

- Data structure

Structure defined in ' appli.c '

typedef struct

{

uint16 total_size;

uint16 oem_key;

uint16 first_var;

uchar rack;

uchar slot;

uchar real;

uchar type;

uchar out_brd;

uchar No.channel ;

<type> field_0;

...

<type> field_m;

}

str_dfbrd_n;

Note :

<type> is : uint16 , uint32 or table of 16 uchar.

- Table declaration

str_dfbrd_n __DEFBRD_n;

- Table Size

3*2 + 6*1 + (m+1)*2   = 14+ 2m    (if type = uint16)

3*2 + 6*1 + (m+1)*4   = 16+ 4m    (if type = uint32)

3*2 + 6*1 + (m+1)*16   = 28+ 16m    (if type = 16 uchar)

Table name : __DEFHIE

- Data structure

Structure defined in  ' appli.c ' and ' appli.h '

typedef struct

{

uint16 begin;

uint16 end;

uint16 main;

uint16 child;

uint16 function;

uint16 reserve;

uint16 numlevel[x];

}

str_dfhie;

- Table declaration

str_dfhie __DEFHIE;

- Table Size

2*6+(begin+end+main.child+function)*2 = 12+(begin+end+main+child+function)*2

Table name : __DEFPROG

- Data structure

uint16

- Table declaration

uint16 __DEFPROG[x];

- Table Size

2x

Table name : __CODEPROG

- Data structure

unsigned char (**)(void);

- Table declaration

unsigned char (**__CODEPROG [x])(void);

- Table Size

4x

Table name : __ ProgName_CODE

- Data structure

unsigned char (*)(void);

- Table declaration

unsigned char (*__ProgName_CODE [x])(void);

- Table Size

4x

Table name : __LINKSFC

- Data structure

uint16 *

- Table declaration

uint16 *__LINKSFC [x];

- Table Size

4x

Table name : __ ProgName_LINK

- Data structure

uint16

- Table declaration

uint16 __ProgName_LINK [x];

- Table Size

2x

Table name : __RESSOURCE

- Data structure

uchar

- Table declaration

uchar __RESOURCE [x];

- Table Size

x

#### External function

Declaration

extern void tic_cnv(unsigned short,unsigned short,unsigned short,unsigned short );

#### External data

BF_BOO and BF_ANA are the two external variables used in this file. BF_BOO is a pointer to the memory block containing all the Boolean data of the application. BF_ANA is same as BF_BOO for the analog data.

| Declaration | Meaning |
| --- | --- |
| extern long *BF_ANA |  |
| extern unsigned char *BF_BOO |  |

#### Static data

Local variables are use to store the relative address of function parameters.

| Declaration | Meaning |
| --- | --- |
| static long LGC_RET_SUB |  |
| static unsigned short LGC_P_NUM[32] |  |
| static unsigned char LGC_P_TYP[32] |  |
| static unsigned char LGC_BVAL |  |

#### Declaration of the initialization function

This section declares the functions use to initialize the data tables. The number of functions is variable and depends on the application.

| Initialization Function Prototype | Comment |
| --- | --- |
| independent of the application |  |
| void apl_init_TABLE (void) ; | This function calls all others |
| void apl_init___MAIN (void) ; |  |
| void apl_init___DEFAPPLI (void) ; |  |
| void apl_init___DEFPROD (void) ; |  |
| void apl_init___DEFFCNV (void) ; |  |
| void apl_init___DEFTCNV (void) ; |  |
| void apl_init___DEFOEM (void) ; |  |
| void apl_init___CODEOEM (void) ; |  |
| void apl_init___DEFBRD (void) ; |  |
| void apl_init___DEFBOO (void) ; |  |
| void apl_init___DEFANA (void) ; |  |
| void apl_init___DEFMSG (void) ; |  |
| void apl_init___CODEVAR (void) ; |  |
| void apl_init___BACKUP (void) ; |  |
| void apl_init___INITBOO (void) ; |  |
| void apl_init___INITANA (void) ; |  |
| void apl_init___INITTMR (void) ; |  |
| void apl_init___INITMSG (void) ; |  |
| void apl_init___DEFMODBUS (void) ; |  |
| void apl_init___DEFMDBBOO (void) ; |  |
| void apl_init___DEFMDBANA (void) ; |  |
| void apl_init___DEFMDBTMR (void) ; |  |
| void apl_init___DEFMDBMSG (void) ; |  |
| void apl_init___DEFHIE (void) ; |  |
| void apl_init___DEFPROG (void) ; |  |
| void apl_init___CODEPROG (void) ; |  |
| void apl_init___LINKSFC (void) ; |  |
| void apl_init___DEFUSF (void) ; |  |
| void apl_init___DEFFBL (void) ; |  |
| void apl_init___DEFVAR (void) ; |  |
| void apl_init___LNGMSG (void) ; |  |
| void apl_init___RESOURCE (void); |  |
| application dependent |  |
| void apl_init___ProgName1_LINK (void); | for the program named : ProgName1 |
| void apl_init___ProgName2_LINK (void); | for the program named : ProgName2 |
| void apl_init___ProgName3_LINK (void); | for the program named : ProgName3 |
| .......... | .......... |
| void apl_init___ProgName1_CODE (void); | for the program named : ProgName1 |
| void apl_init___ProgName2_CODE (void); | for the program named : ProgName2 |
| void apl_init___ProgName3_CODE (void); | for the program named : ProgName3 |
| .......... | .......... |

#### Declaration of the processing code function

This section declares the functions containing the application code. The number of functions is variable and depends on the application.

| Function Prototype | Comment |
| --- | --- |
| unsigned char __ ProgName1_CODE_TRT (void) | TRT = processing code for ProgName1 |
| unsigned char __ ProgName2_CODE_ESTP0001 (void) | ESTP0001 = step number 1 of the SFC ProgName2 |
| unsigned char __ ProgName2_CODE_TRS0002 (void) | TRS0002 = transition 2 of the SFC ProgName2 |
| .......... | .......... |

NOTE :

ProgName1 declaration means ProgName1 is not a SFC (program, function etc.).

ProgName2 declaration means ProgName2 is a SFC.

#### Initialization data

These functions allow to initialize the data tables.

NOTE : the values used to initialize the tables are just some examples.

##### apl_init_TABLE

void apl_init_TABLE (void)

{

apl_init___MAIN ();

apl_init___DEFAPPLI ();

apl_init___DEFPROD ();

apl_init___DEFFCNV ();

apl_init___DEFTCNV ();

apl_init___DEFOEM ();

apl_init___CODEOEM ();

apl_init___DEFBRD ();

apl_init___DEFBOO ();

apl_init___DEFANA ();

apl_init___DEFMSG ();

apl_init___CODEVAR ();

apl_init___BACKUP ();

apl_init___INITBOO ();

apl_init___INITANA ();

apl_init___INITTMR ();

apl_init___INITMSG ();

apl_init___DEFMODBUS ();

apl_init___DEFMDBBOO ();

apl_init___DEFMDBANA ();

apl_init___DEFMDBTMR ();

apl_init___DEFMDBMSG ();

apl_init___DEFHIE ();

apl_init___DEFPROG ();

apl_init___CODEPROG ();

apl_init___LINKSFC ();

apl_init___DEFUSF ();

apl_init___DEFFBL ();

apl_init___DEFVAR ();

apl_init___LNGMSG ();

apl_init___ ProgName1_LINK ();

apl_init___ ProgName2_LINK ();

....................................................

apl_init___RESOURCE ();

apl_init___ ProgName1_CODE ();

apl_init___ ProgName2_CODE ();

......................................................

}

##### apl_init___MAIN

void apl_init___MAIN (void)

{

__MAIN.def_flag = 0x00000001;

__MAIN.def_prod = 0x00000064;

__MAIN.def_appli = 0x00000040;

__MAIN.def_usf = 0x000001f0;

__MAIN.def_fbl = 0x000001f4;

__MAIN.def_fcnv = 0x0000007c;

__MAIN.def_tcnv = 0x00000080;

__MAIN.def_var = 0x00000348;

__MAIN.tab_init = 0x000000ac;

__MAIN.def_ios = 0x00000084;

__MAIN.def_oem = 0x0000008c;

__MAIN.def_hie = 0x000001a8;

__MAIN.def_prog = 0x000001c0;

__MAIN.tab_code = 0x000001d0;

__MAIN.tab_link = 0x000001e0;

__MAIN.def_res = 0x0000091c;

}

##### apl_init___DEFAPPLI

void apl_init___DEFAPPLI (void)

{

sys_strcpy(__DEFAPPLI.name, 'rfwash');

__DEFAPPLI.date = 0x32a4ce5a;

__DEFAPPLI.crc = 0x0ae95f5c;

__DEFAPPLI.version = 0x0032;

__DEFAPPLI.error_level = 0x0001;

__DEFAPPLI.start_mode = 0x0000;

__DEFAPPLI.cycle_duration = 0x0000;

}

##### apl_init___DEFPROD

void apl_init___DEFPROD (void)

{

sys_strcpy(__DEFPROD.name, 'CC86M');

sys_strcpy(__DEFPROD.version, '1.00');

}

##### apl_init___DEFFCNV

void apl_init___DEFFCNV (void)

{

__DEFFCNV.No. = 0x0000;

__DEFFCNV.reserve = 0x0000;

}

##### apl_init___DEFTCNV

void apl_init___DEFTCNV (void)

{

__DEFTCNV.No. = 0x0000;

__DEFTCNV.reserve = 0x0000;

}

##### apl_init___DEFOEM

void apl_init___DEFOEM (void)

{

__DEFOEM.inp_brd = 0x0000;

__DEFOEM.out_brd = 0x0000;

__DEFOEM.cnv_real = 0x0000;

}

##### apl_init___CODEOEM

void apl_init___CODEOEM (void)

{

__CODEOEM[0]=0xa0;

.....................................

__CODEOEM[15]=0x00;

}

##### apl_init___DEFBRD

void apl_init___DEFBRD (void)

{

__DEFBRD[0] = (void*)0;

}

##### apl_init___DEFBOO

void apl_init___DEFBOO (void)

{

__DEFBOO[0].vnum = 0x0000;

__DEFBOO[0].rack = 0x00;

__DEFBOO[0].slot = 0x00;

__DEFBOO[0].channel = 0x00;

__DEFBOO[0].out = 0x00;

__DEFBOO[0].conv_len = 0x00;

__DEFBOO[0].rea_ana = 0x00;

}

##### apl_init___DEFANA

void apl_init___DEFANA (void)

{

__DEFANA[0].vnum = 0x0000;

__DEFANA[0].rack = 0x00;

__DEFANA[0].slot = 0x00;

__DEFANA[0].channel = 0x00;

__DEFANA[0].out = 0x00;

__DEFANA[0].conv_len = 0x00;

__DEFANA[0].rea_ana = 0x00;

}

##### apl_init___DEFMSG

void apl_init___DEFMSG (void)

{

__DEFMSG[0].vnum = 0x0000;

__DEFMSG[0].rack = 0x00;

__DEFMSG[0].slot = 0x00;

__DEFMSG[0].channel = 0x00;

__DEFMSG[0].out = 0x00;

__DEFMSG[0].conv_len = 0x00;

__DEFMSG[0].rea_ana = 0x00;

}

##### apl_init___CODEVAR

void apl_init___CODEVAR (void)

{

__CODEVAR.init_boo = 0x00000120;

__CODEVAR.init_ana = 0x00000124;

__CODEVAR.init_tmr = 0x00000150;

__CODEVAR.init_msg = 0x00000164;

__CODEVAR.lng_msg = 0x00000164;

__CODEVAR.def_mdb = 0x00000168;

__CODEVAR.retain = 0x000000d0;

__CODEVAR.No._var_boo = 0x0000;

__CODEVAR.No._var_ana = 0x0001;

__CODEVAR.No._var_tmr = 0x0000;

__CODEVAR.No._var_msg = 0x0000;

}

##### apl_init___BACKUP

void apl_init___BACKUP (void)

{

__BACKUP.param[0] = 0x00;

__BACKUP.param[1] = 0x00;

..............................................

__BACKUP.param[63] = 0x00;

__BACKUP.No._boo = 0x0000;

__BACKUP.num_boo = 0x0000;

__BACKUP.No._ana = 0x0000;

__BACKUP.num_ana = 0x0000;

__BACKUP.No._tmr = 0x0000;

__BACKUP.num_tmr = 0x0000;

__BACKUP.No._msg = 0x0000;

__BACKUP.num_msg = 0x0000;

}

##### apl_init___INITBOO

void apl_init___INITBOO (void)

{

__INITBOO[0] = 0x000d;

__INITBOO[1] = 0x0000;

.......................................

}

##### apl_init___INITANA

void apl_init___INITANA (void)

{

__INITANA[0].No. = 0x0001;

__INITANA[0].value = 0x00000064;

__INITANA[1].No. = 0x0009;

__INITANA[1].value = 0x00000000;

......................................................

}

##### apl_init___INITTMR

void apl_init___INITTMR (void)

{

__INITTMR[0].No. = 0x0001;

__INITTMR[0].value = 0x0000012c;

....................................................

}

##### apl_init___INITMSG

void apl_init___INITMSG (void)

{

__INITMSG[0].No. = 0x0000;

__INITMSG[0].len = 0x00;

__INITMSG[0].mes = 0x00000000;

.....................................................

}

##### apl_init___DEFMODBUS

void apl_init___DEFMODBUS (void)

{

__DEFMODBUS[0]=0x78;

.............................................

__DEFMODBUS[15]=0x00;

}

##### apl_init___DEFMDBBOO

void apl_init___DEFMDBBOO (void)

{

__DEFMDBBOO[0] = 0x0000;

................................................

__DEFMDBBOO[5] = 0x0000;

}

##### apl_init___DEFMDBANA

void apl_init___DEFMDBANA (void)

{

__DEFMDBANA[0] = 0x0000;

...............................................

__DEFMDBANA[5] = 0x0000;

}

##### apl_init___DEFMDBTMR

void apl_init___DEFMDBTMR (void)

{

__DEFMDBTMR[0] = 0x0000;

................................................

__DEFMDBTMR[5] = 0x0000;

}

##### apl_init___DEFMDBMSG

void apl_init___DEFMDBMSG (void)

{

__DEFMDBMSG[0] = 0x0000;

..................................................

__DEFMDBMSG[5] = 0x0000;

}

##### apl_init___DEFHIE

void apl_init___DEFHIE (void)

{

__DEFHIE.begin = 0x0000;

__DEFHIE.end = 0x0001;

__DEFHIE.main = 0x0001;

__DEFHIE.child = 0x0001;

__DEFHIE.function = 0x0001;

__DEFHIE.reserve = 0x0000;

__DEFHIE.sfc_num = 0x0002;

__DEFHIE.sfc_level = 0x0000;

}

##### apl_init___DEFPROG

void apl_init___DEFPROG (void)

{

__DEFPROG[0] = 0x0002;

...........................................

}

void apl_init___CODEPROG (void)

{

__CODEPROG[0]=__SIMULATE_CODE;

...................................................................

}

##### apl_init___LINKSFC

void apl_init___LINKSFC (void)

{

__LINKSFC[0]=(void*)0;

__LINKSFC[1]=__WASHMAIN_LINK;

__LINKSFC[2]=__AGITATE_LINK;

__LINKSFC[3]=(void*)0;

}

##### apl_init___DEFUSF

void apl_init___DEFUSF (void)

{

__DEFUSF.usfNo. = 0x0000;

__DEFUSF.reserved = 0x0000;

}

##### apl_init___DEFFBL

void apl_init___DEFFBL (void)

{

__DEFFBL.fblNo. = 0x0015;

__DEFFBL.reserved = 0x0000;

__DEFFBL.fbl[0].libno = 0x0001;

__DEFFBL.fbl[0].No.inst = 0x0000;

sys_strcpy(__DEFFBL.fbl[0].name, '#SIG_GEN');

__DEFFBL.fbl[1].libno = 0x0002;

__DEFFBL.fbl[1].No.inst = 0x0000;

sys_strcpy(__DEFFBL.fbl[1].name, '#RS');

__DEFFBL.fbl[2].libno = 0x0003;

__DEFFBL.fbl[2].No.inst = 0x0000;

sys_strcpy(__DEFFBL.fbl[2].name, '#SR');

__DEFFBL.fbl[3].libno = 0x0004;

__DEFFBL.fbl[3].No.inst = 0x0000;

sys_strcpy(__DEFFBL.fbl[3].name, '#R_TRIG');

__DEFFBL.fbl[4].libno = 0x0005;

__DEFFBL.fbl[4].No.inst = 0x0000;

sys_strcpy(__DEFFBL.fbl[4].name, '#F_TRIG');

__DEFFBL.fbl[5].libno = 0x0006;

__DEFFBL.fbl[5].No.inst = 0x0000;

sys_strcpy(__DEFFBL.fbl[5].name, '#CTU');

__DEFFBL.fbl[6].libno = 0x0007;

__DEFFBL.fbl[6].No.inst = 0x0000;

sys_strcpy(__DEFFBL.fbl[6].name, '#CTD');

__DEFFBL.fbl[7].libno = 0x0008;

__DEFFBL.fbl[7].No.inst = 0x0000;

sys_strcpy(__DEFFBL.fbl[7].name, '#CTUD');

__DEFFBL.fbl[8].libno = 0x0009;

__DEFFBL.fbl[8].No.inst = 0x0000;

sys_strcpy(__DEFFBL.fbl[8].name, '#TON');

__DEFFBL.fbl[9].libno = 0x000a;

__DEFFBL.fbl[9].No.inst = 0x0000;

sys_strcpy(__DEFFBL.fbl[9].name, '#TOF');

__DEFFBL.fbl[10].libno = 0x000b;

__DEFFBL.fbl[10].No.inst = 0x0000;

sys_strcpy(__DEFFBL.fbl[10].name, '#TP');

__DEFFBL.fbl[11].libno = 0x000c;

__DEFFBL.fbl[11].No.inst = 0x0000;

sys_strcpy(__DEFFBL.fbl[11].name, '#SEMA');

__DEFFBL.fbl[12].libno = 0x000d;

__DEFFBL.fbl[12].No.inst = 0x0000;

sys_strcpy(__DEFFBL.fbl[12].name, '#CMP');

__DEFFBL.fbl[13].libno = 0x000e;

__DEFFBL.fbl[13].No.inst = 0x0000;

sys_strcpy(__DEFFBL.fbl[13].name, '#STACKINT');

__DEFFBL.fbl[14].libno = 0x000f;

__DEFFBL.fbl[14].No.inst = 0x0000;

sys_strcpy(__DEFFBL.fbl[14].name, '#DERIVATE');

__DEFFBL.fbl[15].libno = 0x0010;

__DEFFBL.fbl[15].No.inst = 0x0000;

sys_strcpy(__DEFFBL.fbl[15].name, '#HYSTER');

__DEFFBL.fbl[16].libno = 0x0011;

__DEFFBL.fbl[16].No.inst = 0x0000;

sys_strcpy(__DEFFBL.fbl[16].name, '#AVERAGE');

__DEFFBL.fbl[17].libno = 0x0012;

__DEFFBL.fbl[17].No.inst = 0x0000;

sys_strcpy(__DEFFBL.fbl[17].name, '#LIM_ALRM');

__DEFFBL.fbl[18].libno = 0x0013;

__DEFFBL.fbl[18].No.inst = 0x0000;

sys_strcpy(__DEFFBL.fbl[18].name, '#BLINK');

__DEFFBL.fbl[19].libno = 0x0014;

__DEFFBL.fbl[19].No.inst = 0x0000;

sys_strcpy(__DEFFBL.fbl[19].name, '#INTEGRAL');

__DEFFBL.fbl[20].libno = 0x0015;

__DEFFBL.fbl[20].No.inst = 0x0000;

sys_strcpy(__DEFFBL.fbl[20].name, '#PID');

}

##### apl_init___DEFVAR

void apl_init___DEFVAR (void)

{

__DEFVAR.boo_int = 0x0011;

__DEFVAR.boo_inp = 0x0000;

__DEFVAR.boo_out = 0x0000;

__DEFVAR.reserve1 = 0x0000;

__DEFVAR.ana_int = 0x0012;

__DEFVAR.ana_inp = 0x0000;

__DEFVAR.ana_out = 0x0000;

__DEFVAR.reserve2 = 0x0000;

__DEFVAR.tmr_int = 0x0009;

__DEFVAR.reserve3 = 0x0000;

__DEFVAR.reserve4 = 0x0000;

__DEFVAR.reserve5 = 0x0000;

__DEFVAR.msg_int = 0x0000;

__DEFVAR.msg_inp = 0x0000;

__DEFVAR.msg_out = 0x0000;

__DEFVAR.reserve6 = 0x0000;

}

##### apl_init___LNGMSG

void apl_init___LNGMSG (void)

{

__LNGMSG[0]=0x00;

....................................

}

##### apl_init___ProgName1_LINK

void apl_init___ProgName1_LINK (void)

{

__ ProgName1_LINK[0] = 0x0001;

....................................

}

##### apl_init___ProgName2_LINK

void apl_init___ProgName2_LINK (void)

{

__ ProgName2_LINK[0] = 0x000e;

......................................

}

##### apl_init___RESOURCE

void apl_init___RESOURCE (void)

{

__RESOURCE[0]=0x00;

.......................................

}

##### apl_init___ProgName_CODE

void apl_init___ProgName1_CODE (void)

{

__ ProgName1 _CODE[0]=__ ProgName1_CODE_TRT;

...............................................

}

void apl_init___ ProgName2_CODE (void)

{

__ ProgName2_CODE[0]=__ ProgName2_CODE_BSTP0000;

__ ProgName2_CODE[1]=(void*)0;

...............................................

}

#### Application code

These functions contain the code of the application. The details of the C instructions representing the body of these functions are defined in chapter C.

##### __ ProgName_CODE_Name

unsigned char __ ProgName1_CODE_TRT(void)

{

........   processing code of the application

........   see chapter G. 3.  for detail of C code

}

unsigned char __ ProgName2_CODE_BSTP0000(void)

{

........   processing code of the application

........   see chapter G. 3.  for detail of C code

}

## EXAMPLE : RFWASH

This chapter shows an example of C code generated by ISaGRAF V3.20. For this example C code is produced for the application RFWASH (as delivered with the product). RFWASH is compiled without optimization.

### Appli.h

#ifndef LGC_VERS2

typedef struct

{

uint32 def_flag;

uint32 def_prod;

uint32 def_appli;

uint32 def_usf;

uint32 def_fbl;

uint32 def_fcnv;

uint32 def_tcnv;

uint32 def_var;

uint32 tab_init;

uint32 def_ios;

uint32 def_oem;

uint32 def_hie;

uint32 def_prog;

uint32 tab_code;

uint32 tab_link;

uint32 def_res;

}

str_header;

#endif

extern str_header __MAIN;

extern str_def_appli __DEFAPPLI;

extern str_def_prod __DEFPROD;

#ifndef LGC_VERS2

typedef struct

{

uint16 libno;

uint16 reserve;

char name[10];

uint16 reserve2;

}

str_dfcnv;

#endif

typedef struct

{

uint16 No.;

uint16 reserve;

str_dfcnv fcnv[1];

}

str_def_fcnv_head;

extern str_def_fcnv_head __DEFFCNV;

typedef struct

{

floating point x;

floating point y;

}

str_point;

typedef struct

{

uint16 tabNo.;

uint16 No.pt;

str_point *pt;

}

str_dftcnv;

typedef struct

{

uint16 No.;

uint16 reserve;

str_dftcnv tcnv[1];

}

str_def_tcnv_head;

extern str_def_tcnv_head __DEFTCNV;

extern str_def_ios __DEFOEM;

extern unsigned char __CODEOEM [16];

typedef struct

{

uint16 total_size;

uint16 oem_key;

uint16 first_var;

uchar rack;

uchar slot;

uchar real;

uchar type;

uchar out_brd;

uchar No.channel;

}

str_dfbrd_0;

extern str_dfbrd_0 __DEFBRD_0;

typedef struct

{

uint16 total_size;

uint16 oem_key;

uint16 first_var;

uchar rack;

uchar slot;

uchar real;

uchar type;

uchar out_brd;

uchar No.channel;

}

str_dfbrd_1;

extern str_dfbrd_1 __DEFBRD_1;

extern uchar *__DEFBRD[2];

extern str_dfvar __DEFBOO[16];

extern str_dfvar __DEFANA[1];

extern str_dfvar __DEFMSG[1];

extern str_def_init __CODEVAR;

extern str_def_retain __BACKUP;

extern uint16 __INITBOO[2];

typedef struct

{

uint16 No.;

uint32 value;

}

str_init_ana;

extern str_init_ana __INITANA[1];

typedef struct

{

uint16 No.;

uint32 value;

}

str_init_tmr;

extern str_init_tmr __INITTMR[1];

typedef struct

{

char *mes;

uint16 No.;

uchar len;

}

str_init_msg;

extern str_init_msg __INITMSG[1];

extern unsigned char __DEFMODBUS [16];

extern uint16 __DEFMDBBOO[6];

extern uint16 __DEFMDBANA[6];

extern uint16 __DEFMDBTMR[6];

extern uint16 __DEFMDBMSG[6];

extern str_def_hie __DEFHIE;

extern uint16 __DEFPROG[4];

extern unsigned char (**__CODEPROG [2])(void);

extern uint16 *__LINKSFC [2];

#ifndef LGC_VERS2

typedef struct

{

uint16 libno;

char name[10];

}

str_dfusf;

#endif

typedef struct

{

uint16 usfNo.;

uint16 reserved;

}

str_dfusf_head;

extern str_dfusf_head __DEFUSF;

#ifndef LGC_VERS2

typedef struct

{

uint16 libno;

uint16 No.inst;

char name[12];

}

str_def_fbl;

#endif

typedef struct

{

uint16 fblNo.;

uint16 reserved;

str_def_fbl fbl[20];

}

str_def_fbl_head;

extern str_def_fbl_head __DEFFBL;

extern str_def_var __DEFVAR;

extern unsigned char __LNGMSG [4];

extern uint16 __RUNSTOP_LINK[46];

extern unsigned char __RESOURCE [8];

extern unsigned char (*__COMMAND_CODE [1])(void);

extern unsigned char (*__RUNSTOP_CODE [13])(void);

extern void apl_init_TABLE (void);

### Appli.c

INCLUDE

#include <tasy0def.h>

#include <take0pro.h>

#include <take0blk.h>

#include <take0ste.h>

#include <take0msg.h>

#include <take0prg.h>

#include <tasy0apl.h>

#include <taio0def.h>

DATA STRUCTURES AND TABLES

#ifndef LGC_VERS2

typedef struct

{

uint32 def_flag;

uint32 def_prod;

uint32 def_appli;

uint32 def_usf;

uint32 def_fbl;

uint32 def_fcnv;

uint32 def_tcnv;

uint32 def_var;

uint32 tab_init;

uint32 def_ios;

uint32 def_oem;

uint32 def_hie;

uint32 def_prog;

uint32 tab_code;

uint32 tab_link;

uint32 def_res;

}

str_header;

#endif

str_header __MAIN;

str_def_appli __DEFAPPLI;

str_def_prod __DEFPROD;

#ifndef LGC_VERS2

typedef struct

{

uint16 libno;

uint16 reserve;

char name[10];

uint16 reserve2;

}

str_dfcnv;

#endif

typedef struct

{

uint16 No.;

uint16 reserve;

str_dfcnv fcnv[1];

}

str_def_fcnv_head;

str_def_fcnv_head __DEFFCNV;

typedef struct

{

floating point x;

floating point y;

}

str_point;

typedef struct

{

uint16 tabNo.;

uint16 No.pt;

str_point *pt;

}

str_dftcnv;

typedef struct

{

uint16 No.;

uint16 reserve;

str_dftcnv tcnv[1];

}

str_def_tcnv_head;

str_def_tcnv_head __DEFTCNV;

str_def_ios __DEFOEM;

unsigned char __CODEOEM [16];

typedef struct

{

uint16 total_size;

uint16 oem_key;

uint16 first_var;

uchar rack;

uchar slot;

uchar real;

uchar type;

uchar out_brd;

uchar No.channel;

}

str_dfbrd_0;

str_dfbrd_0 __DEFBRD_0;

typedef struct

{

uint16 total_size;

uint16 oem_key;

uint16 first_var;

uchar rack;

uchar slot;

uchar real;

uchar type;

uchar out_brd;

uchar No.channel;

}

str_dfbrd_1;

str_dfbrd_1 __DEFBRD_1;

uchar *__DEFBRD[2];

str_dfvar __DEFBOO[16];

str_dfvar __DEFANA[1];

str_dfvar __DEFMSG[1];

str_def_init __CODEVAR;

str_def_retain __BACKUP;

uint16 __INITBOO[2];

typedef struct

{

uint16 No.;

uint32 value;

}

str_init_ana;

str_init_ana __INITANA[1];

typedef struct

{

uint16 No.;

uint32 value;

}

str_init_tmr;

str_init_tmr __INITTMR[1];

typedef struct

{

char *mes;

uint16 No.;

uchar len;

}

str_init_msg;

str_init_msg __INITMSG[1];

unsigned char __DEFMODBUS [16];

uint16 __DEFMDBBOO[6];

uint16 __DEFMDBANA[6];

uint16 __DEFMDBTMR[6];

uint16 __DEFMDBMSG[6];

str_def_hie __DEFHIE;

uint16 __DEFPROG[4];

unsigned char (**__CODEPROG [2])(void);

uint16 *__LINKSFC [2];

#ifndef LGC_VERS2

typedef struct

{

uint16 libno;

char name[10];

}

str_dfusf;

#endif

typedef struct

{

uint16 usfNo.;

uint16 reserved;

}

str_dfusf_head;

str_dfusf_head __DEFUSF;

#ifndef LGC_VERS2

typedef struct

{

uint16 libno;

uint16 No.inst;

char name[12];

}

str_def_fbl;

#endif

typedef struct

{

uint16 fblNo.;

uint16 reserved;

str_def_fbl fbl[20];

}

str_def_fbl_head;

str_def_fbl_head __DEFFBL;

str_def_var __DEFVAR;

unsigned char __LNGMSG [4];

uint16 __RUNSTOP_LINK[46];

unsigned char __RESOURCE [8];

unsigned char (*__COMMAND_CODE [1])(void);

unsigned char (*__RUNSTOP_CODE [13])(void);

EXTERNAL FUNCTION

extern void tic_cnv(unsigned short,unsigned short,unsigned short,unsigned short );

EXTERNAL DATA

#ifndef DEF_NO_GLOBALS

extern long *BF_ANA;

extern unsigned char *BF_BOO;

#endif

STATIC DATA

static long LGC_RET_SUB;

static unsigned short LGC_P_NUM[32];

static unsigned char LGC_P_TYP[32];

static unsigned char LGC_BVAL;

DECLARATION OF THE INITIALIZATION FUNCTIONS

void apl_init_TABLE (void);

void apl_init___MAIN (void);

void apl_init___DEFAPPLI (void);

void apl_init___DEFPROD (void);

void apl_init___DEFFCNV (void);

void apl_init___DEFTCNV (void);

void apl_init___DEFOEM (void);

void apl_init___CODEOEM (void);

void apl_init___DEFBRD (void);

void apl_init___DEFBOO (void);

void apl_init___DEFANA (void);

void apl_init___DEFMSG (void);

void apl_init___CODEVAR (void);

void apl_init___BACKUP (void);

void apl_init___INITBOO (void);

void apl_init___INITANA (void);

void apl_init___INITTMR (void);

void apl_init___INITMSG (void);

void apl_init___DEFMODBUS (void);

void apl_init___DEFMDBBOO (void);

void apl_init___DEFMDBANA (void);

void apl_init___DEFMDBTMR (void);

void apl_init___DEFMDBMSG (void);

void apl_init___DEFHIE (void);

void apl_init___DEFPROG (void);

void apl_init___CODEPROG (void);

void apl_init___LINKSFC (void);

void apl_init___DEFUSF (void);

void apl_init___DEFFBL (void);

void apl_init___DEFVAR (void);

void apl_init___LNGMSG (void);

void apl_init___RUNSTOP_LINK (void);

void apl_init___RESOURCE (void);

void apl_init___COMMAND_CODE (void);

void apl_init___RUNSTOP_CODE (void);

Declaration of the processing code functions

unsigned char __COMMAND_CODE_TRT (void);

unsigned char __RUNSTOP_CODE_BSTP0002 (void);

unsigned char __RUNSTOP_CODE_ESTP0002 (void);

unsigned char __RUNSTOP_CODE_TRS0002 (void);

unsigned char __RUNSTOP_CODE_TRS0003 (void);

INITIALIZATION CODE

void apl_init_TABLE (void)

{

apl_init___MAIN ();

apl_init___DEFAPPLI ();

apl_init___DEFPROD ();

apl_init___DEFFCNV ();

apl_init___DEFTCNV ();

apl_init___DEFOEM ();

apl_init___CODEOEM ();

apl_init___DEFBRD ();

apl_init___DEFBOO ();

apl_init___DEFANA ();

apl_init___DEFMSG ();

apl_init___CODEVAR ();

apl_init___BACKUP ();

apl_init___INITBOO ();

apl_init___INITANA ();

apl_init___INITTMR ();

apl_init___INITMSG ();

apl_init___DEFMODBUS ();

apl_init___DEFMDBBOO ();

apl_init___DEFMDBANA ();

apl_init___DEFMDBTMR ();

apl_init___DEFMDBMSG ();

apl_init___DEFHIE ();

apl_init___DEFPROG ();

apl_init___CODEPROG ();

apl_init___LINKSFC ();

apl_init___DEFUSF ();

apl_init___DEFFBL ();

apl_init___DEFVAR ();

apl_init___LNGMSG ();

apl_init___RUNSTOP_LINK ();

apl_init___RESOURCE ();

apl_init___COMMAND_CODE ();

apl_init___RUNSTOP_CODE ();

}

void apl_init___MAIN (void)

{

__MAIN.def_flag = 0x00000001;

__MAIN.def_prod = 0x00000064;

__MAIN.def_appli = 0x00000040;

__MAIN.def_usf = 0x00000230;

__MAIN.def_fbl = 0x00000234;

__MAIN.def_fcnv = 0x0000007c;

__MAIN.def_tcnv = 0x00000080;

__MAIN.def_var = 0x00000378;

__MAIN.tab_init = 0x00000140;

__MAIN.def_ios = 0x00000084;

__MAIN.def_oem = 0x0000008c;

__MAIN.def_hie = 0x00000204;

__MAIN.def_prog = 0x00000218;

__MAIN.tab_code = 0x00000220;

__MAIN.tab_link = 0x00000228;

__MAIN.def_res = 0x00000470;

}

void apl_init___DEFAPPLI (void)

{

sys_strcpy(__DEFAPPLI.name, 'rfsample');

__DEFAPPLI.date = 0x32a86613;

__DEFAPPLI.crc = 0x0034eb4e;

__DEFAPPLI.version = 0x0009;

__DEFAPPLI.error_level = 0x0010;

__DEFAPPLI.start_mode = 0x0000;

__DEFAPPLI.cycle_duration = 0x0000;

}

void apl_init___DEFPROD (void)

{

sys_strcpy(__DEFPROD.name, 'CC86M');

sys_strcpy(__DEFPROD.version, '1.00');

}

void apl_init___DEFFCNV (void)

{

__DEFFCNV.No. = 0x0000;

__DEFFCNV.reserve = 0x0000;

}

void apl_init___DEFTCNV (void)

{

__DEFTCNV.No. = 0x0000;

__DEFTCNV.reserve = 0x0000;

}

void apl_init___DEFOEM (void)

{

__DEFOEM.inp_brd = 0x0001;

__DEFOEM.out_brd = 0x0001;

__DEFOEM.cnv_real = 0x0000;

}

void apl_init___CODEOEM (void)

{

__CODEOEM[0]=0xb8;__CODEOEM[1]=0x00;__CODEOEM[2]=0x00;__CODEOEM[3]=0x00;

__CODEOEM[4]=0x38;__CODEOEM[5]=0x01;__CODEOEM[6]=0x00;__CODEOEM[7]=0x00;

__CODEOEM[8]=0x3c;__CODEOEM[9]=0x01;__CODEOEM[10]=0x00;__CODEOEM[11]=0x00;

__CODEOEM[12]=0x9c;__CODEOEM[13]=0x00;__CODEOEM[14]=0x00;__CODEOEM[15]=0x00;

}

void apl_init___DEFBRD (void)

{

__DEFBRD[0] = (uchar *)&__DEFBRD_0;

__DEFBRD_0.total_size = 0x000c;

__DEFBRD_0.oem_key = 0x0000;

__DEFBRD_0.first_var = 0x0001;

__DEFBRD_0.rack = 0x00;

__DEFBRD_0.slot = 0x00;

__DEFBRD_0.real = 0x01;

__DEFBRD_0.type = 0x01;

__DEFBRD_0.out_brd = 0x00;

__DEFBRD_0.No.channel = 0x08;

__DEFBRD[1] = (uchar *)&__DEFBRD_1;

__DEFBRD_1.total_size = 0x000c;

__DEFBRD_1.oem_key = 0x0000;

__DEFBRD_1.first_var = 0x0009;

__DEFBRD_1.rack = 0x00;

__DEFBRD_1.slot = 0x01;

__DEFBRD_1.real = 0x01;

__DEFBRD_1.type = 0x01;

__DEFBRD_1.out_brd = 0x01;

__DEFBRD_1.No.channel = 0x08;

}

void apl_init___DEFBOO (void)

{

__DEFBOO[0].vnum = 0x0001;

__DEFBOO[0].rack = 0x00;

__DEFBOO[0].slot = 0x00;

__DEFBOO[0].channel = 0x00;

__DEFBOO[0].out = 0x00;

__DEFBOO[0].conv_len = 0x00;

__DEFBOO[0].rea_ana = 0x00;

__DEFBOO[1].vnum = 0x0002;

__DEFBOO[1].rack = 0x00;

__DEFBOO[1].slot = 0x00;

__DEFBOO[1].channel = 0x01;

__DEFBOO[1].out = 0x00;

__DEFBOO[1].conv_len = 0x00;

__DEFBOO[1].rea_ana = 0x00;

__DEFBOO[2].vnum = 0x0003;

__DEFBOO[2].rack = 0x00;

__DEFBOO[2].slot = 0x00;

__DEFBOO[2].channel = 0x02;

__DEFBOO[2].out = 0x00;

__DEFBOO[2].conv_len = 0x00;

__DEFBOO[2].rea_ana = 0x00;

__DEFBOO[3].vnum = 0x0004;

__DEFBOO[3].rack = 0x00;

__DEFBOO[3].slot = 0x00;

__DEFBOO[3].channel = 0x03;

__DEFBOO[3].out = 0x00;

__DEFBOO[3].conv_len = 0x00;

__DEFBOO[3].rea_ana = 0x00;

__DEFBOO[4].vnum = 0x0005;

__DEFBOO[4].rack = 0x00;

__DEFBOO[4].slot = 0x00;

__DEFBOO[4].channel = 0x04;

__DEFBOO[4].out = 0x00;

__DEFBOO[4].conv_len = 0x00;

__DEFBOO[4].rea_ana = 0x00;

__DEFBOO[5].vnum = 0x0006;

__DEFBOO[5].rack = 0x00;

__DEFBOO[5].slot = 0x00;

__DEFBOO[5].channel = 0x05;

__DEFBOO[5].out = 0x00;

__DEFBOO[5].conv_len = 0x00;

__DEFBOO[5].rea_ana = 0x00;

__DEFBOO[6].vnum = 0x0007;

__DEFBOO[6].rack = 0x00;

__DEFBOO[6].slot = 0x00;

__DEFBOO[6].channel = 0x06;

__DEFBOO[6].out = 0x00;

__DEFBOO[6].conv_len = 0x00;

__DEFBOO[6].rea_ana = 0x00;

__DEFBOO[7].vnum = 0x0008;

__DEFBOO[7].rack = 0x00;

__DEFBOO[7].slot = 0x00;

__DEFBOO[7].channel = 0x07;

__DEFBOO[7].out = 0x00;

__DEFBOO[7].conv_len = 0x00;

__DEFBOO[7].rea_ana = 0x00;

__DEFBOO[8].vnum = 0x0009;

__DEFBOO[8].rack = 0x00;

__DEFBOO[8].slot = 0x01;

__DEFBOO[8].channel = 0x00;

__DEFBOO[8].out = 0x01;

__DEFBOO[8].conv_len = 0x00;

__DEFBOO[8].rea_ana = 0x00;

__DEFBOO[9].vnum = 0x000a;

__DEFBOO[9].rack = 0x00;

__DEFBOO[9].slot = 0x01;

__DEFBOO[9].channel = 0x01;

__DEFBOO[9].out = 0x01;

__DEFBOO[9].conv_len = 0x00;

__DEFBOO[9].rea_ana = 0x00;

__DEFBOO[10].vnum = 0x000b;

__DEFBOO[10].rack = 0x00;

__DEFBOO[10].slot = 0x01;

__DEFBOO[10].channel = 0x02;

__DEFBOO[10].out = 0x01;

__DEFBOO[10].conv_len = 0x00;

__DEFBOO[10].rea_ana = 0x00;

__DEFBOO[11].vnum = 0x000c;

__DEFBOO[11].rack = 0x00;

__DEFBOO[11].slot = 0x01;

__DEFBOO[11].channel = 0x03;

__DEFBOO[11].out = 0x01;

__DEFBOO[11].conv_len = 0x00;

__DEFBOO[11].rea_ana = 0x00;

__DEFBOO[12].vnum = 0x000d;

__DEFBOO[12].rack = 0x00;

__DEFBOO[12].slot = 0x01;

__DEFBOO[12].channel = 0x04;

__DEFBOO[12].out = 0x01;

__DEFBOO[12].conv_len = 0x00;

__DEFBOO[12].rea_ana = 0x00;

__DEFBOO[13].vnum = 0x000e;

__DEFBOO[13].rack = 0x00;

__DEFBOO[13].slot = 0x01;

__DEFBOO[13].channel = 0x05;

__DEFBOO[13].out = 0x01;

__DEFBOO[13].conv_len = 0x00;

__DEFBOO[13].rea_ana = 0x00;

__DEFBOO[14].vnum = 0x000f;

__DEFBOO[14].rack = 0x00;

__DEFBOO[14].slot = 0x01;

__DEFBOO[14].channel = 0x06;

__DEFBOO[14].out = 0x01;

__DEFBOO[14].conv_len = 0x00;

__DEFBOO[14].rea_ana = 0x00;

__DEFBOO[15].vnum = 0x0010;

__DEFBOO[15].rack = 0x00;

__DEFBOO[15].slot = 0x01;

__DEFBOO[15].channel = 0x07;

__DEFBOO[15].out = 0x01;

__DEFBOO[15].conv_len = 0x00;

__DEFBOO[15].rea_ana = 0x00;

}

void apl_init___DEFANA (void)

{

__DEFANA[0].vnum = 0x0000;

__DEFANA[0].rack = 0x00;

__DEFANA[0].slot = 0x00;

__DEFANA[0].channel = 0x00;

__DEFANA[0].out = 0x00;

__DEFANA[0].conv_len = 0x00;

__DEFANA[0].rea_ana = 0x00;

}

void apl_init___DEFMSG (void)

{

__DEFMSG[0].vnum = 0x0000;

__DEFMSG[0].rack = 0x00;

__DEFMSG[0].slot = 0x00;

__DEFMSG[0].channel = 0x00;

__DEFMSG[0].out = 0x00;

__DEFMSG[0].conv_len = 0x00;

__DEFMSG[0].rea_ana = 0x00;

}

void apl_init___CODEVAR (void)

{

__CODEVAR.init_boo = 0x000001b4;

__CODEVAR.init_ana = 0x000001b8;

__CODEVAR.init_tmr = 0x000001bc;

__CODEVAR.init_msg = 0x000001c0;

__CODEVAR.lng_msg = 0x000001c0;

__CODEVAR.def_mdb = 0x000001c4;

__CODEVAR.retain = 0x00000164;

__CODEVAR.No._var_boo = 0x0000;

__CODEVAR.No._var_ana = 0x0000;

__CODEVAR.No._var_tmr = 0x0000;

__CODEVAR.No._var_msg = 0x0000;

}

void apl_init___BACKUP (void)

{

__BACKUP.param[0] = 0x00;

__BACKUP.param[1] = 0x00;

__BACKUP.param[2] = 0x00;

__BACKUP.param[3] = 0x00;

__BACKUP.param[4] = 0x00;

__BACKUP.param[5] = 0x00;

__BACKUP.param[6] = 0x00;

__BACKUP.param[7] = 0x00;

__BACKUP.param[8] = 0x00;

__BACKUP.param[9] = 0x00;

__BACKUP.param[10] = 0x00;

__BACKUP.param[11] = 0x00;

__BACKUP.param[12] = 0x00;

__BACKUP.param[13] = 0x00;

__BACKUP.param[14] = 0x00;

__BACKUP.param[15] = 0x00;

__BACKUP.param[16] = 0x00;

__BACKUP.param[17] = 0x00;

__BACKUP.param[18] = 0x00;

__BACKUP.param[19] = 0x00;

__BACKUP.param[20] = 0x00;

__BACKUP.param[21] = 0x00;

__BACKUP.param[22] = 0x00;

__BACKUP.param[23] = 0x00;

__BACKUP.param[24] = 0x00;

__BACKUP.param[25] = 0x00;

__BACKUP.param[26] = 0x00;

__BACKUP.param[27] = 0x00;

__BACKUP.param[28] = 0x00;

__BACKUP.param[29] = 0x00;

__BACKUP.param[30] = 0x00;

__BACKUP.param[31] = 0x00;

__BACKUP.param[32] = 0x00;

__BACKUP.param[33] = 0x00;

__BACKUP.param[34] = 0x00;

__BACKUP.param[35] = 0x00;

__BACKUP.param[36] = 0x00;

__BACKUP.param[37] = 0x00;

__BACKUP.param[38] = 0x00;

__BACKUP.param[39] = 0x00;

__BACKUP.param[40] = 0x00;

__BACKUP.param[41] = 0x00;

__BACKUP.param[42] = 0x00;

__BACKUP.param[43] = 0x00;

__BACKUP.param[44] = 0x00;

__BACKUP.param[45] = 0x00;

__BACKUP.param[46] = 0x00;

__BACKUP.param[47] = 0x00;

__BACKUP.param[48] = 0x00;

__BACKUP.param[49] = 0x00;

__BACKUP.param[50] = 0x00;

__BACKUP.param[51] = 0x00;

__BACKUP.param[52] = 0x00;

__BACKUP.param[53] = 0x00;

__BACKUP.param[54] = 0x00;

__BACKUP.param[55] = 0x00;

__BACKUP.param[56] = 0x00;

__BACKUP.param[57] = 0x00;

__BACKUP.param[58] = 0x00;

__BACKUP.param[59] = 0x00;

__BACKUP.param[60] = 0x00;

__BACKUP.param[61] = 0x00;

__BACKUP.param[62] = 0x00;

__BACKUP.param[63] = 0x00;

__BACKUP.No._boo = 0x0000;

__BACKUP.num_boo = 0x0000;

__BACKUP.No._ana = 0x0000;

__BACKUP.num_ana = 0x0000;

__BACKUP.No._tmr = 0x0000;

__BACKUP.num_tmr = 0x0000;

__BACKUP.No._msg = 0x0000;

__BACKUP.num_msg = 0x0000;

}

void apl_init___INITBOO (void)

{

__INITBOO[0] = 0x0012;

__INITBOO[1] = 0x0000;

}

void apl_init___INITANA (void)

{

__INITANA[0].No. = 0x0000;

__INITANA[0].value = 0x00000000;

}

void apl_init___INITTMR (void)

{

__INITTMR[0].No. = 0x0000;

__INITTMR[0].value = 0x00000000;

}

void apl_init___INITMSG (void)

{

__INITMSG[0].No. = 0x0000;

__INITMSG[0].len = 0x00;

__INITMSG[0].mes = 0x00000000;

}

void apl_init___DEFMODBUS (void)

{

__DEFMODBUS[0]=0xd4;__DEFMODBUS[1]=0x01;__DEFMODBUS[2]=0x00;__DEFMODBUS[3]=0x00;

__DEFMODBUS[4]=0xe0;__DEFMODBUS[5]=0x01;__DEFMODBUS[6]=0x00;__DEFMODBUS[7]=0x00;

__DEFMODBUS[8]=0xec;__DEFMODBUS[9]=0x01;__DEFMODBUS[10]=0x00;__DEFMODBUS[11]=0x00;

__DEFMODBUS[12]=0xf8;__DEFMODBUS[13]=0x01;__DEFMODBUS[14]=0x00;__DEFMODBUS[15]=0x00;

}

void apl_init___DEFMDBBOO (void)

{

__DEFMDBBOO[0] = 0x0000;

__DEFMDBBOO[1] = 0x0000;

__DEFMDBBOO[2] = 0x0000;

__DEFMDBBOO[3] = 0x0000;

__DEFMDBBOO[4] = 0x0000;

__DEFMDBBOO[5] = 0x0000;

}

void apl_init___DEFMDBANA (void)

{

__DEFMDBANA[0] = 0x0000;

__DEFMDBANA[1] = 0x0000;

__DEFMDBANA[2] = 0x0000;

__DEFMDBANA[3] = 0x0000;

__DEFMDBANA[4] = 0x0000;

__DEFMDBANA[5] = 0x0000;

}

void apl_init___DEFMDBTMR (void)

{

__DEFMDBTMR[0] = 0x0000;

__DEFMDBTMR[1] = 0x0000;

__DEFMDBTMR[2] = 0x0000;

__DEFMDBTMR[3] = 0x0000;

__DEFMDBTMR[4] = 0x0000;

__DEFMDBTMR[5] = 0x0000;

}

void apl_init___DEFMDBMSG (void)

{

__DEFMDBMSG[0] = 0x0000;

__DEFMDBMSG[1] = 0x0000;

__DEFMDBMSG[2] = 0x0000;

__DEFMDBMSG[3] = 0x0000;

__DEFMDBMSG[4] = 0x0000;

__DEFMDBMSG[5] = 0x0000;

}

void apl_init___DEFHIE (void)

{

__DEFHIE.begin = 0x0001;

__DEFHIE.end = 0x0000;

__DEFHIE.main = 0x0001;

__DEFHIE.child = 0x0000;

__DEFHIE.function = 0x0000;

__DEFHIE.reserve = 0x0000;

__DEFHIE.sfc_num = 0x0002;

__DEFHIE.sfc_level = 0x0000;

}

void apl_init___DEFPROG (void)

{

__DEFPROG[0] = 0x0001;

__DEFPROG[1] = 0x0000;

__DEFPROG[2] = 0x0003;

__DEFPROG[3] = 0x0000;

}

void apl_init___CODEPROG (void)

{

__CODEPROG[0]=__COMMAND_CODE;__CODEPROG[1]=__RUNSTOP_CODE;

}

void apl_init___LINKSFC (void)

{

__LINKSFC[0]=(void*)0;__LINKSFC[1]=__RUNSTOP_LINK;

}

void apl_init___DEFUSF (void)

{

__DEFUSF.usfNo. = 0x0000;

__DEFUSF.reserved = 0x0000;

}

void apl_init___DEFFBL (void)

{

__DEFFBL.fblNo. = 0x0014;

__DEFFBL.reserved = 0x0000;

__DEFFBL.fbl[0].libno = 0x0001;

__DEFFBL.fbl[0].No.inst = 0x0000;

sys_strcpy(__DEFFBL.fbl[0].name, '#SIG_GEN');

__DEFFBL.fbl[1].libno = 0x0002;

__DEFFBL.fbl[1].No.inst = 0x0000;

sys_strcpy(__DEFFBL.fbl[1].name, '#RS');

__DEFFBL.fbl[2].libno = 0x0003;

__DEFFBL.fbl[2].No.inst = 0x0000;

sys_strcpy(__DEFFBL.fbl[2].name, '#SR');

__DEFFBL.fbl[3].libno = 0x0004;

__DEFFBL.fbl[3].No.inst = 0x0000;

sys_strcpy(__DEFFBL.fbl[3].name, '#R_TRIG');

__DEFFBL.fbl[4].libno = 0x0005;

__DEFFBL.fbl[4].No.inst = 0x0000;

sys_strcpy(__DEFFBL.fbl[4].name, '#F_TRIG');

__DEFFBL.fbl[5].libno = 0x0006;

__DEFFBL.fbl[5].No.inst = 0x0000;

sys_strcpy(__DEFFBL.fbl[5].name, '#CTU');

__DEFFBL.fbl[6].libno = 0x0007;

__DEFFBL.fbl[6].No.inst = 0x0000;

sys_strcpy(__DEFFBL.fbl[6].name, '#CTD');

__DEFFBL.fbl[7].libno = 0x0008;

__DEFFBL.fbl[7].No.inst = 0x0000;

sys_strcpy(__DEFFBL.fbl[7].name, '#CTUD');

__DEFFBL.fbl[8].libno = 0x0009;

__DEFFBL.fbl[8].No.inst = 0x0000;

sys_strcpy(__DEFFBL.fbl[8].name, '#TON');

__DEFFBL.fbl[9].libno = 0x000a;

__DEFFBL.fbl[9].No.inst = 0x0000;

sys_strcpy(__DEFFBL.fbl[9].name, '#TOF');

__DEFFBL.fbl[10].libno = 0x000b;

__DEFFBL.fbl[10].No.inst = 0x0000;

sys_strcpy(__DEFFBL.fbl[10].name, '#TP');

__DEFFBL.fbl[11].libno = 0x000c;

__DEFFBL.fbl[11].No.inst = 0x0000;

sys_strcpy(__DEFFBL.fbl[11].name, '#SEMA');

__DEFFBL.fbl[12].libno = 0x000d;

__DEFFBL.fbl[12].No.inst = 0x0000;

sys_strcpy(__DEFFBL.fbl[12].name, '#CMP');

__DEFFBL.fbl[13].libno = 0x000e;

__DEFFBL.fbl[13].No.inst = 0x0000;

sys_strcpy(__DEFFBL.fbl[13].name, '#STACKINT');

__DEFFBL.fbl[14].libno = 0x000f;

__DEFFBL.fbl[14].No.inst = 0x0000;

sys_strcpy(__DEFFBL.fbl[14].name, '#DERIVATE');

__DEFFBL.fbl[15].libno = 0x0010;

__DEFFBL.fbl[15].No.inst = 0x0000;

sys_strcpy(__DEFFBL.fbl[15].name, '#HYSTER');

__DEFFBL.fbl[16].libno = 0x0011;

__DEFFBL.fbl[16].No.inst = 0x0000;

sys_strcpy(__DEFFBL.fbl[16].name, '#AVERAGE');

__DEFFBL.fbl[17].libno = 0x0012;

__DEFFBL.fbl[17].No.inst = 0x0000;

sys_strcpy(__DEFFBL.fbl[17].name, '#LIM_ALRM');

__DEFFBL.fbl[18].libno = 0x0013;

__DEFFBL.fbl[18].No.inst = 0x0000;

sys_strcpy(__DEFFBL.fbl[18].name, '#BLINK');

__DEFFBL.fbl[19].libno = 0x0014;

__DEFFBL.fbl[19].No.inst = 0x0000;

sys_strcpy(__DEFFBL.fbl[19].name, '#INTEGRAL');

}

void apl_init___DEFVAR (void)

{

__DEFVAR.boo_int = 0x0004;

__DEFVAR.boo_inp = 0x0008;

__DEFVAR.boo_out = 0x0008;

__DEFVAR.reserve1 = 0x0000;

__DEFVAR.ana_int = 0x0001;

__DEFVAR.ana_inp = 0x0000;

__DEFVAR.ana_out = 0x0000;

__DEFVAR.reserve2 = 0x0000;

__DEFVAR.tmr_int = 0x0000;

__DEFVAR.reserve3 = 0x0000;

__DEFVAR.reserve4 = 0x0000;

__DEFVAR.reserve5 = 0x0000;

__DEFVAR.msg_int = 0x0000;

__DEFVAR.msg_inp = 0x0000;

__DEFVAR.msg_out = 0x0000;

__DEFVAR.reserve6 = 0x0000;

}

void apl_init___LNGMSG (void)

{

__LNGMSG[0]=0x00;__LNGMSG[1]=0x00;__LNGMSG[2]=0x00;__LNGMSG[3]=0x00;

}

void apl_init___RUNSTOP_LINK (void)

{

__RUNSTOP_LINK[0] = 0x0001;

__RUNSTOP_LINK[1] = 0x0004;

__RUNSTOP_LINK[2] = 0x0001;

__RUNSTOP_LINK[3] = 0x0003;

__RUNSTOP_LINK[4] = 0x0024;

__RUNSTOP_LINK[5] = 0x0028;

__RUNSTOP_LINK[6] = 0x002c;

__RUNSTOP_LINK[7] = 0x0032;

__RUNSTOP_LINK[8] = 0x0036;

__RUNSTOP_LINK[9] = 0x003a;

__RUNSTOP_LINK[10] = 0x0000;

__RUNSTOP_LINK[11] = 0x003e;

__RUNSTOP_LINK[12] = 0x0042;

__RUNSTOP_LINK[13] = 0x0046;

__RUNSTOP_LINK[14] = 0x004a;

__RUNSTOP_LINK[15] = 0x004e;

__RUNSTOP_LINK[16] = 0x0052;

__RUNSTOP_LINK[17] = 0x0056;

__RUNSTOP_LINK[18] = 0x0001;

__RUNSTOP_LINK[19] = 0x0000;

__RUNSTOP_LINK[20] = 0x0002;

__RUNSTOP_LINK[21] = 0x0000;

__RUNSTOP_LINK[22] = 0x0004;

__RUNSTOP_LINK[23] = 0x0002;

__RUNSTOP_LINK[24] = 0x0000;

__RUNSTOP_LINK[25] = 0x0003;

__RUNSTOP_LINK[26] = 0x0000;

__RUNSTOP_LINK[27] = 0x0003;

__RUNSTOP_LINK[28] = 0x0000;

__RUNSTOP_LINK[29] = 0x0004;

__RUNSTOP_LINK[30] = 0x0000;

__RUNSTOP_LINK[31] = 0x0001;

__RUNSTOP_LINK[32] = 0x0000;

__RUNSTOP_LINK[33] = 0x0001;

__RUNSTOP_LINK[34] = 0x0000;

__RUNSTOP_LINK[35] = 0x0002;

__RUNSTOP_LINK[36] = 0x0000;

__RUNSTOP_LINK[37] = 0x0002;

__RUNSTOP_LINK[38] = 0x0000;

__RUNSTOP_LINK[39] = 0x0003;

__RUNSTOP_LINK[40] = 0x0000;

__RUNSTOP_LINK[41] = 0x0003;

__RUNSTOP_LINK[42] = 0x0000;

__RUNSTOP_LINK[43] = 0x0002;

__RUNSTOP_LINK[44] = 0x0000;

__RUNSTOP_LINK[45] = 0x0000;

}

void apl_init___RESOURCE (void)

{

__RESOURCE[0]=0x00;__RESOURCE[1]=0x00;__RESOURCE[2]=0x00;__RESOURCE[3]=0x00;

__RESOURCE[4]=0xa2;__RESOURCE[5]=0xf3;__RESOURCE[6]=0xf1;__RESOURCE[7]=0xff;

}

void apl_init___COMMAND_CODE (void)

{

__COMMAND_CODE[0]=__COMMAND_CODE_TRT;

}

void apl_init___RUNSTOP_CODE (void)

{

__RUNSTOP_CODE[0]=(void*)0;__RUNSTOP_CODE[1]=(void*)0;__RUNSTOP_CODE[2]=(void*)0;__RUNSTOP_CODE[3]=(void*)0;

__RUNSTOP_CODE[4]=(void*)0;__RUNSTOP_CODE[5]=(void*)0;__RUNSTOP_CODE[6]=__RUNSTOP_CODE_BSTP0002;__RUNSTOP_CODE[7]=(void*)0;

__RUNSTOP_CODE[8]=__RUNSTOP_CODE_ESTP0002;__RUNSTOP_CODE[9]=(void*)0;__RUNSTOP_CODE[10]=(void*)0;__RUNSTOP_CODE[11]=__RUNSTOP_CODE_TRS0002;

__RUNSTOP_CODE[12]=__RUNSTOP_CODE_TRS0003;

}

unsigned char __RUNSTOP_CODE_BSTP0002 (void)

{

ios_boo_ref(9);

BF_BOO[9] = BF_BOO[18];

return ((unsigned char)(0));

}

APPLICATION CODE

unsigned char __COMMAND_CODE_TRT (void)

{

BF_BOO[20] = (unsigned char)(BF_BOO[1] & BF_BOO[2]);

BF_BOO[17] = BF_BOO[20];

_LAB1:;

return ((unsigned char)(0));

}

unsigned char __RUNSTOP_CODE_ESTP0002 (void)

{

ios_boo_ref(9);

BF_BOO[9] = BF_BOO[19];

return ((unsigned char)(0));

}

unsigned char __RUNSTOP_CODE_TRS0002 (void)

{

return ((unsigned char)(BF_BOO[17]));

}

unsigned char __RUNSTOP_CODE_TRS0003 (void)

{

BF_BOO[20] =  ! BF_BOO[17];

return ((unsigned char)(BF_BOO[20]));

}