THE CECDRIVE.EXE, GPIB.DLL, and GPIB-32.DLL UTILITIES
------------------------------------------------
The CECDRIVE.EXE program is designed to enhance the
PC<>488, 488EX, 4x488, and PS<>488 
products from Capital Equipment Corp. 
by allowing application programs written for
the NI GPIB cards to run without modification.
This allows our boards to run any combination of programs:
those written specifically for CEC cards as well as those
written for NI cards, including LabWindows and LabView.

FILES INCLUDED
--------------------------------------------------
CECDRIVE.EXE            DOS support for NI compatibility
GPIB.DLL                MS Windows support for NI compatibility
GPIB-32.DLL             MS 32-bit Windows support for NI compatibility
GPIB.INI                Configuration settings file
CECDRIVE.DOC            This documentation file (text).


DOS INSTALLATION
--------------------------------------------------
Files are normally installed as part of standard CEC488 software
installation, using SETUP.
Typically, files are places in the C:\CEC488 directory.


1) Add the following command line to your AUTOEXEC.BAT file:

      C:\CEC488\CECDRIVE\CECDRIVE

That's it!  Once CECDRIVE runs, it is installed in memory.

REMOVING CECDRIVE FROM MEMORY
------------------------------------------------------------

If you no longer need CECDRIVE, and want to free up the
memory it is using, use the command:

      C:\CEC488\CECDRIVE>  CECDRIVE /R

WINDOWS INSTALLATION
------------------------------------------------------------
Files are automatically installed when you run SETUP from
the CEC488 software disk.
The required .DLL files are placed in your Windows directory.



RE-CONFIGURING CECDRIVE
----------------------------------------------------

For some application programs, the default configuration
of CECDRIVE will work.
However, some programs require that the driver be configured
with non-default device names or device settings.

To modify the CECDRIVE configuration, edit the file
GPIB.INI.
 
For DOS, CECDRIVE.EXE will find GPIB.INI by searching the DOS 
PATH (this may include looking in the Windows directory, if
you have Windows installed.)
After you have modified GPIB.INI, run CECDRIVE again so it
will read the file again and modify its settings.
For Windows, GPIB.DLL will find GPIB.INI in the Windows
directory.
To avoid confusion, keep only one copy of GPIB.INI on your
disk.  If you have multiple copies, and modify the copy that
is not being used by CECDRIVE, the modifications will have
no effect.

GPIB.INI is an ASCII text file containing the settings for
one or more GPIB boards and up to 32 GPIB devices.
Each device section begins with a label, like this:

  [DEV1]

To change the name of an existing device entry, just edit
this label.  Leave the square brackets - they are not part
of the device name.

In each section, there are settings, given as a setting name
followed by an equals sign, followed by the value.
The file contains comments describing the allowed choices
for values.


MULTIPLE CECDRIVE CONFIGURATIONS (CONFIGURATION FILES)
---------------------------------------------------

CECDRIVE.EXE can load a configuration file of your choice
instead of the default file GPIB.INI.
Just specify the file name on the CECDRIVE command line.

You can modify the configuration of CECDRIVE even if it
is already loaded, just by giving the CECDRIVE command
again, with a new configuration file name.

For example:

      C>  CECDRIVE mygpib.cfg

NOTE:
 Do not name the configuration file with the same name as
 one of your device names in the file.
 (For example, don't set a device name to [SCOPE] and then
 call the file SCOPE.CFG).
 This would cause problems, because CECDRIVE adds the device
 names to DOS' list of devices, and DOS does not allow
 devices and disk files to have the same name (regardless
 of the .xxx extension).

USING AN EXISTING NI CONFIGURATION FILE
--------------------------------------------------------
If you have a running system under Windows using an NI
board, you can copy its GPIB.INI file for use with
our GPIB.DLL.  The formats are compatible.

USING AN OLD FORMAT CECDRIVE CONFIGURATION FILE
--------------------------------------------------------
Previous versions of CECDRIVE used a different configuration
file format and command line option. These will still work
with the current version of CECDRIVE.
For example:
            CECDRIVE  /CONFIG=lecroy.cfg