HPIB plotters and AutoCAD

        AutoCAD for Windows:

           See the file PLOTTER.DOC for information on configuring
           HPIB plotters in Windows for use with any programs.

        Instructions for using HPIB (IEEE-488, GPIB) plotters with
        AutoCAD(r) release 9 or later, in DOS:

        1) Install the AutoCAD software on your computer according to the 
           usual instructions in the AutoCAD manual. 

        2) Install your PC-488 interface card according to the 
           instructions in the PC-488 manual.

        3) Copy the file PRINTER.EXE from the disk supplied with your PC-
           488 interface card to your AutoCAD working disk (normally your 
           hard disk).  The file should be placed in the root directory 
           (see your DOS manual for an explanation of directories).
           For example:
                copy a:\utility\printer.exe c:\dos

        4) Determine the HPIB address of your plotter.  For Hewlett-Packard 
           plotters, the address is usually 5 (five). The address is 
           determined by switches on the plotter. The rest of these 
           instructions assume you have a parallel printer port on your 
           computer (PRN or LPT1). The PRINTER software will make AutoCAD 
           think that the HPIB plotter is on LPT2. 

        5) Add a line to your AUTOEXEC.BAT file on your disk to run the 
           PRINTER program: 

              PRINTER P1 5

           If you don't already have a file named \AUTOEXEC.BAT, you should 
           create one.  You can create or modify this file with any word 
           processor software you have, even the EDLIN program supplied 
           with DOS.  If your word processor software has a "non-document" 
           mode for storing files, use it. In the sample command line 
           given above, P1 refers to parallel port #1, which will remain 
           as LPT1.  The numeral 5 refers to the HPIB address of your 
           plotter, which will become LPT2. If your plotter is at a 
           different address, use that number instead.

        6) Re-boot your PC to install the PRINTER software.  This 
           installation will occur automatically each time you turn your 
           PC on.  Notice that PRINTER reports the configuration of the 
           ports when it runs. 

        7) Run AutoCAD, according to the usual instructions.

        8) Choose "Configure Autocad" from the main menu. Next, choose 
           "Configure plotter".  Answer the questions just as you normally 
           would, until you get to the prompt "Write the plot to a file 
           <N>: ".  Type "Y" and hit return.  This will cause AutoCAD to 
           ask for a file name whenever you try to plot a drawing. 
           Finally, exit the configuration menu and save the new 
           configuration. 

        9) Now you're ready to go!  Just run AutoCAD the way you normally 
           would. When you want to plot a drawing, AutoCAD will ask you 
           for the file name to plot to.  Type "LPT2" and return, and the 
           plotter will go. 

        * AutoCAD is a trademark of Autodesk, Inc.