------------------------------------------------------
   Using CEC 488 interfaces with other operating systems
   ------------------------------------------------------

   (This discussion is fairly technical, because it is designed to cover 
   any possible operating system, even one custom-written for your 
   application.  If you have specific questions about an operating 
   system, gather any technical data you can on the requirements listed 
   below and give us a call at CEC and we'll help you.) 

   CEC 488 software support is provided for the DOS, Windows,
   Windows 95, Windows NT, and OS/2 operating systems.
   Supports for some varieties of UNIX are also available separately.
   Many programming languages are supported in these environments. 

   The software that comes with your board can be used with other 
   operating systems, as long as certain conditions are met: 

   1) You must be able to use the Microsoft library file
      IEEE488.LIB in building your application programs.

      If your operating environment allows you to write code using the 
      standard Microsoft C compiler and linker, or provides equivalent 
      tools that use the same file formats, you can use the library file 
      provided with CEC 488. 

   2) Your program must have the ability (permission) to execute
      input/output instructions.

      Any program can do I/O operations in DOS, or in any system which 
      runs the computer's processor in "real" mode. If your system runs 
      on an 80286 or 80386 in "protected" mode, some restrictions may 
      apply.  In order to use CEC 488, your operating system must allow 
      an application program (or at least the IEEE 488 code segment) to 
      do direct I/O operations.  In OS/2, for example, I/O privilege can 
      be granted to specific code segments when the program is linked. 
            
   3) The library does make one BIOS function call (software
      interrupt 15 hex, function C0 hex), which must be allowed.

      If your operating system does not allow an application program to 
      make this call, you can set the variable ieee488_os2mode to 1 in an 
      initialization procedure (see below).  Note that setting 
      ieee488_os2mode to 1 disables the use of DMA, and requires you to 
      set ieee488_ps2 to 1 in your initialization procedure IF you are 
      running on a Microchannel (PS/2) computer. 
     
   4) The CEC 488 library needs read access to a system timer
      memory location.

      A single word memory location must be available which increments on 
      a periodic timebase.  The default location assumed in segment 40 
      hex, offset 6C hex, which is used by the normal PC BIOS for time 
      counting.  The default increment rate is once every 55 msec.
      If these assumptions are not correct for your system, you can 
      change the value of the timer location and rate in an 
      initialization procedure (see below). If your system runs in 
      "protected" mode, make sure that the program has read access to the 
      segment selector used in the timer location pointer.    


   Initialization procedures:
   --------------------------
   
        The CEC 488 library consists of two segments, a code
        segment named ieee488_text, and a data segment named
        ieee488_data, declared as shown below:

                  ieee488_text segment public 'CODE'

                  ieee488_data segment public 'DATA'

        Certain variables in the data segment are preset to
        match the normal DOS environment.

        IF you need to change these values for your environment, 
        you can create an initialization procedure which is 
        called BEFORE you call any of the routines in the CEC 
        488 library. 

        The variables you may wish to change are shown below:

            ieee488_timerdata dd 40006CH  ; pointer to timer word
            ieee488_timer     dw 55       ; msec/timer tick
            ieee488_ps2       db 0        ; set to 1 for Microchannel
                                          ; (PS/2) computer
            ieee488_os2mode   db 0        ; set to 1 for OS/2
                                     ; (this only disables DMA, 
                                     ; and skips setting ieee488_ps2
                                     ; by making an INT 15H call
                                     ; to the PC BIOS)
            ieee488_segincr   dw 1000H    ; amount to increment
                                          ; segment selector by when
                                          ; offset wraps around
                                          ; at 64K (see #5, below)

        An example of an initialization procedure is shown:

            ieee488_data segment public 'DATA'
                  extrn   ieee488_timer:word
            ieee488_data ends

            _TEXT segment public 'CODE'
                  assume cs:_TEXT
                  public _init_488lib
            _init_488lib proc near
                  mov     ax,ieee488_data         ; set segment
                  mov     es,ax
                  assume  es:ieee488_data
                  mov     ieee488_timer,30        ; set timer rate
                                                  ;  to 30 msec/tick
                  ret                             ; return
            _init_488lib endp
            _TEXT ends
                  end

        This would be called in C as:

                  init_488lib();



   Additional notes for "protected" mode:
   --------------------------------------

   5) The TARRAY and RARRAY procedures allow "huge" pointers
      to variables which may span more than 64K bytes.  In
      order to handle this, these procedures increment the
      segment portion of the memory address whenever the
      offset portion overflows.  In "real" mode, the correct
      increment value is always 64K bytes, or 1000H paragraphs
      of 16 bytes each, so the variable ieee488_segincr is
      set the 1000H by default.

      In protected mode, you have two choices.  One is to avoid
      using "huge" variables which cause the offset to wrap
      around at 64K.

      The other choice is to make sure the valid segment 
      selectors for the data area involved are in sequence,
      with some constant increment.  Set the variable 
      ieee488_segincr to that increment value in an
      initialization routine.  This is the
      approach used in OS/2, which provides a system call to
      obtain the correct increment value.

   6) DMA (direct memory access) always uses absolute physical
      addressing.  Therefore DMA must be used cautiously if
      at all when operating in protected mode.

      One choice is to avoid using DMA at all.  Just don't call
      the dmachannel() procedure to enable it.

      The other choice is to use DMA by enabling it and then
      calling rarray() or tarray().  In this case, the data
      pointers passed to these procedures MUST be "real" mode
      memory addresses.  You will need a method of converting
      proctected mode pointers to real mode addresses, and 
      making sure that the memory region is not swapped out
      to disk or otherwise re-used during the DMA operation.