Calling 488 subroutines in ROM directly
        ---------------------------------------

        PC<>488 and 488EX contain read-only-memories (ROM) which have
        488 subroutines in them.
        (The ROM in 488EX must be enabled by turning switch 1 position 
         7 ON.)

        If you have a language or application which cannot use the
        Microsoft library version of the 488 support routines (IEEE488.LIB),
        you may be able to call the ROM routines directly.

        The ROM routines are called by pushing the arguments on the
        processor stack in left-to-right order.  All arguments are passed
        as 16-bit offset values within the current data segment (DS
        register).  This implies that all arguments MUST be within the
        same 64K segment of memory.

        String arguments are passed as a 16-bit offset of a string descriptor
        in memory.  The descriptor itself consists of a 16-bit string
        length followed by a 16-bit offset of the string data.

        Below are examples of calls written in Microsoft assembler:

        ROM     segment at 0CC00H
                org     0
        initialize proc far
        initialize endp
                org     36
        send    proc    far
        send    endp
        ROM     ends

        DATA    segment
        myaddr  dw      21
        level   dw      0
        addr    dw      3
        str     db      'MEASURE'       ; string
        desc    dw      $-str           ; descriptor - length
                dw      offset str      ;            - address
        status  dw      ?
        DATA    ends

        CODE    segment
                assume  cs:CODE,ds:DATA
                mov     ax,DATA
                mov     ds,ax

                mov     ax,offset myaddr ; push offsets of args on stack
                push    ax
                mov     ax,offset level
                push    ax
                call    initialize      ; FAR call to ROM

                mov     ax,offset addr
                push    ax
                mov     ax,offset desc
                push    ax
                mov     ax,offset status
                push    ax
                call    send
        CODE    ends
                end

        Other routines are called in a similar manner.
        The origin for each routine within the ROM segment is:

        initialize      0
        send            36
        enter           39
        transmit        30
        receive         33
        spoll           12
        ppoll           15
        tarray          200
        rarray          203
        dma2            206