Using CEC-488 boards in Microsoft Windows
------------------------
              
  For writing 16-bit Windows programs:
  -------------------------
         1)   Copy the file WIN488.DLL from the \WINDOWS directory
              on the CEC-488 software disk to the Windows directory
              on your computer.
         
         For C or C++ programming:
              Write your code as described in the manual.
              Link with the library file:
                        WIN488.LIB
              instead of the DOS library (IEEE488.LIB).

         For Visual BASIC programming:
              a) Copy the file IEEEVB.BAS from the \VB directory
                 on the CEC-488 software disk to any directory of your
                 choice on your computer.
              b) Use the File/Add menu in VB to add this file to
                 your Visual BASIC project.
              c) Write your code according to the manual, just as
                 for QuickBASIC, except that Enter and Receive are
                 slightly different.  See Appendix K for more details.

              NOTE: For Visual BASIC 3.0 and earlier, use the file
                    IEEEVB3.BAS instead of IEEEVB.BAS!


  For writing 32-bit Windows programs:                                     
  -------------------------
         1)   Copy the file IEEE_32M.DLL from the \WIN32 directory
              on the CEC-488 software disk to the Windows directory
              on your computer.
         2)   If you are using Windows NT (not Windows 95), run the
              SETUPNT.EXE program from the \WIN32 directory of the
              CEC-488 software disk.  This program will install
              the Windows NT driver.

         For C or C++ programming:
              Write your code as described in the manual.
              However, use this include file instead of ieee-c.h:

                        #include "ieee_32.h"

              This include file may be found in the \WIN32 directory
              of the CEC-488 disk.

              Link with one of these libraries (depending on your
              compiler), instead of with the DOS library (IEEE488.LIB):

                        IEEE_32M.LIB            for Microsoft Visual C++
              or
                        IEEE_32B.LIB            for Borland C++

              These libraries are found in the \WIN32 directory of
              the CEC-488 disk.

         For Visual BASIC programming:
              See the instructions above.
              No changes are needed for 32-bit programming.