NuWa

Technical Manual

(Version 1.0)

# Warranty

All products manufactured by ICPDAS Inc. are warranted against defective materials for a period of one year from the date of delivery to the original purchaser.

# Warning

ICPDAS Inc. assumes no liability for damages consequent to the use of this product. ICPDAS Inc. reserves the right to change this manual at any time without notice. The information furnished by ICPDAS Inc. is believed to be accurate and reliable. However, no responsibility is assumed by ICPDAS Inc. for its use, or for any infringements of patents or other rights of third parties resulting from its use.

# Copyright

Copyright by ICPDAS Inc., LTD. All rights reserved worldwide.

# Trademark

The names used for identification only maybe registered trademarks of their respective companies.

# License

The user can use, modify and backup this software on a single machine. The user may not reproduce, transfer or distribute this software, or any copy, in whole or in part.

Contents

- Introduction …………………………………………… 5

  - Overview …………………………………………………. 5

  - NuWa Features …..……………………………………… 6

  - Placement ……………...………………………………... 9

- Quick Start ………………………………………………… 10

- Hardware Description ……………………………… 10

  - Block Diagram ………………………………………..… 10

  - Hardware Description …………………………………. 11

    - PXA255 Microprocessor ………………………….. 11

    - Real Time Clock …………………………………… 11

    - Watch Dog Timer ………………………………….. 11

    - Unique Serial ID …………………………………… 11

    - PCMCIA ……………………………………………. 12

    - Compact Flash …………………………………….. 12

    - Multi Media/ Secure Digital Memory Card ……… 12

    - Network …………………………………………….. 12

    - Display ……………………………………………… 12

    - USB Host …………………………………………. 13

    - USB Client ……………………………………….. 13

    - Audio ……………………………………………… 13

    - Touch Screen Controller ………………………… 13

    - Controller Area Network (CAN) ………………… 13

    - Blue Tooth ………………………………………… 14

    - IrDA ………………………………………….……. 14

    - Expansion I/O Bus ………………………………. 14

  - Connector and Jumper Description ………………... 15

    - J1 - Peripheral I/O ………………………………….. 16

      - J1: Reset ……………………………………… 16

      - J1: Indicator LED …………………………….. 16

      - J1: PXA255 Full Function UART …………… 16

      - J1: PXA255 JTAG ……………………………. 17

      - J1: USB Client ……………………………….. 18

      - J1: USB Host …………………………………. 19

      - J1: PXA255 IrDA ……………………………... 20

      - J1: PXA255 Blue Tooth ……………………… 21

      - J1: MMC / SD Memory Card ……………….. 22

      - J1: Audio Interface ………………………. 23

    - J2: RS485 …………………………………………… 24

    - J3, J4: USB Host ……………………………………. 24

    - J3, J4: Ethernet …………………………………….. 24

    - J5: Power Connector ………………………………. 24

    - J6: RS-232 (COM6) ………………………………… 24

    - J7: VGA Interface …………………………………… 25

    - J16: CPLD JTAG ……………………………………. 26

    - J17: RS-232 (COM7 ~ COM9) ……………………. 26

    - J23: Touch Screen ……………………………… 27

    - J25: Expansion I/O Bus Connector …………… 28

    - J27: Compact Flash Socket …………………… 28

    - J31: PCMCIA Socket ………………………....... 29

    - J35: Controller Area Network (CAN) …………. 30

    - J36: Operation Mode Selection ………………. 31

  - GPIO Define …………………………………………….. 32

  - Memory Mapping ………………………………………. 33

  - CPLD Define …………………………………………….. 34

Appendix A Accessories ……………………………………… 40

Appendix B Environmental characteristics ………………. 45

1.  Introduction

  - Overview

The NuWa is an All-In-One RISC base CPU Board using the Intel PXA255 XScale® RISC microprocessor. The NuWa is designed for high performance, low power and Fan-Less.因為此特性, 他的應用非常的廣泛. 例如: PDA, Set-Top Box, Gateway, PLC, Window Base Terminal, Hand Held Device. Mobile or IP Phone, Thin Client…

NuWa Serial Boards Selection Guide

| Model | NuWa-430 | NuWa-450 | NuWa-470 |
| --- | --- | --- | --- |
| Processor | Intel PXA255 400 MHz |
| SDRAM | 64 MB |
| Flash | 32 MB Flash for Image / 8 MB Flash for Registry |
| SRAM | N/A | N/A | 512 KB |
| EEPROM | N/A | N/A | 128 KB |
| Unique Serial Number | 64 Bits Factory-Lasered Serial Number |
| Watch Dog Timer | 271 ns to 1165 seconds |
| JTAG and Debug | Pin Header for debug and update firmware |
| PCMCIA | N/A | Type I/II |
| Compact Flash | Type I/II |
| MMC/SD | Pin Header |
| VGA Port | N/A | 1024x768 @ 16bpp |
| LCD Interface | TFT / STN, 640x480 @ 16bpp |
| Touch Interface | Built in 4-wired touch controller |
| Serial Ports | RS-232 x1, RS485 x 1 |
| Additional Serial Ports | N/A | 4-wired RS-232 x3 2-wired TTL RS-232 x1 2 |
| IrDA Capability | Pin Header for IR Module |
| Blue Tooth | Pin Header for Blue Tooth Module |
| Network | 10/100 x1 | 10/100 x1 | 10/100 x2 |
| CAN Bus | N/A | N/A | 1 |
| USB Host | 2 | 2 | 4 |
| USB Client | 1 |
| Audio | Line In / Line Out / MIC |
| Expansion Interface | ICP DAS I/O Slot |

  - NuWa Features

Microprocessor

- Intel® XScale® PXA255 32 Bits Processor

- Clock rates up to 400 MHz

Cache

- 32KB Data Cache and 32KB Instruction Cache

- 2KB Mini Data Cache and 2KB Mini Instruction Cache

System Memory

- Up to 64 MB 3.3V SDRAM

- Up to 32MB Flash for Boot Loader and OS Image

- Up to 8MB Flash for Registry

Compact Flash

- Type I/II Compact Flash socket @ 3.3V

- Support Memory and I/O device

PCMCIA

- Type II PCMCIA Flash socket @ 3.3V

- Support Memory and I/O device

Network Support

- DAVICOM DM9000 10/100 MB Fast Ethernet Controller

- RJ45 Connector.

Display

MQ-200: CRT

- MQ-200 2D Graphics Controller

- Display Resolution up to 1024x768

- Built in 2MB video memory

XScale: LCD

- Single- or Dual- Panel Display

- Recommended Display Resolution of 640x480

- Up to 65535 colors in Active Color Mode

USB Host

- Phillip ISP1160 USB Host Controller

- USB Specification Rev. 1.1

USB Client

- PXA255 Processor USB Device Controller

Audio

- AC’97 CODEC (16Bits)

- Support Line-In, Line-Out and MIC-In

- 250mW per Channel amplified out

Touch Screen

- DMC9000 Touch Screen Controller

- Support 4-Wired, Resistive Type Touch Screen

CAN Bus

- SJA1000 CAN Bus Controller

Serial Ports

- Provide RS232/485 serial ports

- Full function , 2-Wired , 4-Wired and TTL Level support

Blue Tooth Support

- Baud rate is programmable up to 921 Kbps

IrDA Support

- Baud rate is programmable up to 239Kbps

Real Time Clock

- Dallas DS1302 Real Time Clock

Watch Dog Timer

- PXA255 Internal Watch Dog Timer

- Programmable timeout periods from 271 ns to 1165 seconds

Unique Serial ID

- Provides 64 bits factory-lasered unique Serial ID

Expansion Interface

- ICPDAS I8000 Serial I/O Modules Support

- 8 Bits Data Width

- 256 bytes memory space

- Interrupt Mode Support

- TX/RX Support

Power Supply

- 5V main power

- 12V used for Inverter of LCD

  - Placement

- Quick Start

The following steps guide user how to install NuWa quickly.

Step 1: Connecting Power Source

The NuWa main power source is +5V. +12 used for LCD inverter only.

| J5 | Signal |
| --- | --- |
| Pin 1 | VCC +5V |
| Pin 2 | GND |
| Pin 3 | Frame GND |
| Pin 4 | VCC +12V |

Step 2: Connecting Display

NuWa provide a standard female 15 Pins D-SUB type connector (J7) to connect analog CRT display.

| J7 | Signal | J7 | Signal |
| --- | --- | --- | --- |
| Pin 1 | RED | Pin 9 | VCC 5V |
| Pin 2 | GREEN | Pin 10 | GND |
| Pin 3 | BLUE | Pin 11 | N.C |
| Pin 4 | N.C | Pin 12 | N.C |
| Pin 5 | GND | Pin 13 | H. Sync |
| Pin 6 | GND | Pin 14 | V. Sync |
| Pin 7 | GND | Pin 15 | N.C |
| Pin 8 | GND |  |  |

Step 3: Connecting Ethernet

NuWa provides RJ-45 8 Pins type 10/100 Base Fast Ethernet port to connect or control world wide I/O device or Database on J3 and J4 upper side. There are 2 LEDs to indicate Ethernet status.

| J3/J4 LAN | Signal |
| --- | --- |
| Pin 1 | TPT+ |
| Pin 2 | TPT- |
| Pin 3 | TPR+ |
| Pin 4 | LAN_GND |
| Pin 5 | LAN_GND |
| Pin 6 | TPR- |
| Pin 7 | LAN_GND |
| Pin 8 | LAN_GND |

Step 4: Connecting USB HID Device

The Human Interface Device is a kind of USB class device such as Keyboard and Mouse. User can use these USB devices to control NuWa.

Step 5: Inserting Compact Flash Memory Card

Install your own Application programs or data to Compact Flash if needed.

Step 6: Plugging I8000 Serial I/O Device

NuWa provide 1 slot of expansion bus to plug I8000 serial I/O device on J25. The I8000 serial I/O devices provide variety functions including Digital I/O、Analog I/O、Motion control、Counter、RS-232/422/485 …

Step 7: Overall Review

Please overall review to mask sure all steps are correct before turn the system on.

- Hardware Description

The following section provides a detail description of the feature provided by NuWa. These sections include the jumper setting, connectors and pin outs.

  - Block Diagram

  - Hardware Description

    - Microprocessor

NuWa is an All-In-One RISC (ARM 5TE) base CPU board using Intel PXA255 RISC microprocessor. The PXA255 is a low power and high integrated system on a chip design based on the Intel® XScale™ micro architecture. The PXA255 built in 32KByte instruction cache, 32KByte Data cache, 2KByte Mini data cache and 2KByte Mini instruction cache. The PXA255 default run mode frequency is 400 MHz and the system memory frequency is 100 MHz.

    - Real Time Clock

NuWa built in a Dallas DS1302 RTC. It has 31 bytes SRAM to save seconds, minutes, hours, day, data, months and year information. Operation System loads RTC information to setup system clock when system power on. NuWa has an external Battery to keep DS1302 information when system power off.

    - Watch Dog Timer

The PXA255 contains a watch dog timer, OSMR3, which can be used to protect against erroneous software or hardware fail. Timeout periods can be adjusted from 271 ns to 1165 seconds.

    - Unique Serial ID

NuWa provides 64 bits factory-lasered, read-only Unique ID. The Unique Serial ID like a software key. Programmer can use it to identify your system.

    - PCMCIA

PCMCIA is managed by PXA255 and CPLD core logic. The NuWa is fitted with a Type I /II PCMCIA socket mounted on the board. It supports 3.3 V Type I and II Memory and IO device. The NuWa support hot swap changeover of the cards and notification of card insert

    - Compact Flash

Compact Flash (CF) controlled by PXA255 and CPLD core logic. The NuWa is fitted with a Type I /II Compact Flash socket mounted on the board. It supports 3.3 V Type I and II Compact Flash Memory and IO device. The CF card provides removable storage in a wide variety of capacities. Normally, CF card store user application programs. The NuWa support hot swap changeover of the cards and notification of card insert.

    - Multi Media / Secure Digital Memory Card

This interface allow user to use a Multi Media Card (MMC) or Secure Digital (SD) Memory Card.

    - Network

NuWa built in DAVICOM DM9000 10/100 BT Fast Ethernet controller. The controller provides an embedded PHY and MAC, complies with IEEE 802.3x flow control for full duplex specification. Configuration data and MAC information are stored in an external EEPROM. It provides 2 LED to indicate Ethernet status. Yellow LED indicates link status, Green LED indicates of transceiver status.

    - Display

NuWa provides two display interfaces, CRT and LCD.

PXA255 microprocessor built in a LCD controller. It supports both passive (SNT) and active (TFT) flat panel display with maximum supported resolution of 640x480x16-bit/piexl. PXA255 have 2 dedicated DMA channels allow the LCD controller to support single and dual panel display.

Standard NuWa platform built in a MediqQ MQ-200 2D embedded graphics controller. NuWa provide a standard 15 pins, D-SUB type VGA connector. MQ-200 built in 2MB video memory. Display resolutions up to 1024x768, pixel depths up to 32 bits per pixel.

    - USB Host

NuWa built in a Philips ISP1160 USB Host controller. It has been designed to support the Open Host Controller Interface (OHCI). The USB Host controller complies with USB Specification Rev. 1.1. Support data transfer at full speed (12 MBit/s) and low speed (1.5 MBit/s). The HID (Human Interface Device), ext. keyboard and mouse, Mass Storage device are supported. The Each USB Host port provided 100 mA to 500 mA depend on client device. NuWa has power protection function. If the USB voltage is short circuited or more the 500 mA is drawn from either port, NuWa turns off the power of USB Port and automatically protects the devices and system.

    - USB Client

This function allows the NuWa to appear as a client device to USB host such as desktop. This port support full USB connection speed (12MBit/sec). Insert and removal of host computer or hub will cause an interrupt.

    - Audio

NuWa built in an AC’97 Audio codec. There are three audio interfaces supported on NuWa: stereo microphone input, line in and amp line out. The amplified line out is suitable for driving an 8Ω load with a maximum power output of 250mW per channel.

    - Touch Screen Controller

NuWa built in an embedded touch screen controller, DMC9000. It supports analog 4 wired resistive touch screens. The Pin 5 (GND) is not necessary to connect if your touch screen do not used.

    - Controller Area Network (CAN)

Controller Area Network (CAN) is a protocol developed for the automotives industry that is increasingly being used in industrial and automation applications. The maximum transfer speed is 1Mbps. The CAN bus is managed by SJA1000 on NuWa platform.

    - Blue Tooth

The PXA255 microprocessor built in a Blue Tooth communication port. This port allow user to connect a Blue Tooth module. Or set this port as a 4-wired RS-232. These signals are TTL level.

    - IrDA

The PXA255 built in an IrDA communication port. This port allow user to connect an IrDA transceiver for IrDA communication. Or set this port as a 2-wired RS-232. These signals are TTL level.

    - Expansion I/O Bus

The NuWa provide an expansion I/O Bus to Add-On ICPDAS 8K serial I/O modules, such as Digital In/Out, Analog In/Out, Motion Control, and Communication Modules. It support interrupt mode.

  - Connector and Jumper Description

This section describes the pin outs of connectors and jumpers.

Connectors and Jumpers Summary Table

| Name | Function |
| --- | --- |
| J1 | Peripheral I/O Connector |
| J2 | RS-485 |
| J3 | LAN2, USB Host Port 3, 4 |
| J4 | LAN1, USB Host Port 1, 2 |
| J5 | Power Connector |
| J6 | TTL Level RS-232 |
| J7 | VGA Interface (From MQ200) |
| J16 | CPLD JTAG Port |
| J17 | RS-232 |
| J23 | Touch Screen Connector |
| J25 | Extension Bus |
| J27 | Compact Flash Socket |
| J31 | PCMAIA Socket |
| J35 | CAN Bus Connector |
| J36 | Operating Mode. |

3.3.1 J1 – Peripheral I/O

The connector J1 is a multi-functions I/O connector. The illustration shows these functions as blow.

3.3.1.1 J1: Reset

This signal will issue a hardware reset to CPU and system peripherals. Boot-loader cleans the contents of SDRAM after reset, and re-loads the operating system to SDRAM. Then jump to SDRAM running operating system.

| J1 | Signal |
| --- | --- |
| Pin 1 | Reset In |
| Pin 3 | GND |

3.3.1.2 J1: Indicator LED

The indicator LED is controlled by software. The GPIO_27 set to low (LED off) during boot loader running stage. The GPIO_27 is set to high (LED on) during the normal operating mode. When the system going to suspend mode, GPIO_27 則以 1Hz 的頻率閃爍. 當系統回復到 normal operating mode 時, GPIO_27 is set to high (LED On).

| J1 | Signal |
| --- | --- |
| Pin 2 | GPIO_27 |
| Pin 4 | GND |

3.3.1.3 J1: PXA255 Full Function UART

The Full function UART baud rate is programmable up to 230 Kbps. This port is used for debug function in default. It will send message out after power on. The debug port baud rate is 38400 bps.

| J1 | Signal |
| --- | --- |
| Pin 5 | RTS |
| Pin 6 | CTS |
| Pin 7 | DTR |
| Pin 8 | DCD |
| Pin 9 | RI |
| Pin 10 | DSR |
| Pin 12 | TXD |
| Pin 14 | RXD |
| Pin 16 | GND |

3.3.1.4 J1: CPU JTAG

The JTAG port is used during manufacturing to program boot loader to flash. User can use the JTAG port to access and control PXA255 CPU.

| J1 | Signal |
| --- | --- |
| Pin 11 | TCK |
| Pin 13 | TDI |
| Pin 15 | TMS |
| Pin 17 | TDO |
| Pin 18 | GND |

3.3.1.5 J1: USB Client

The USBC VCC In is power supplied form host computer.

| J1 | Signal |
| --- | --- |
| Pin 19 | USBC VCC In |
| Pin 21 | USBC_D- |
| Pin 23 | USBC_D+ |
| Pin 25 | GND |

3.3.1.6 J1: USB Host

| J1 | Signal |
| --- | --- |
| Pin 20 | VCC 5V |
| Pin 22 | D- |
| Pin 24 | D+ |
| Pin 26 | GND |

3.3.1.7 J1: PXA255 IrDA

| J1 | Signal |
| --- | --- |
| Pin 28 | IR_RXD |
| Pin 30 | ID_TXD |
| Pin 32 | GND |

3.3.1.8 J1: PXA255 Blue Tooth

| J1 | Signal |
| --- | --- |
| Pin 36 | BT_RTS |
| Pin 38 | BT_CTS |
| Pin 40 | BT_TXD |
| Pin 42 | BT_RXD |
| Pin 44 | GND |

3.3.1.9 J1: MMC/SD Card

| J1 | Signal |
| --- | --- |
| Pin 27 | VCC 3.3V |
| Pin 29 | GND |
| Pin 31 | Write Protect |
| Pin 33 | Card Detect |
| Pin 35 | CMD |
| Pin 37 | DAT |
| Pin 39 | CK |
| Pin 41 | CS |

3.3.1.10 J1: Audio Interface

| J1 | Signal |
| --- | --- |
| Pin 43 | Audio GND |
| Pin 45 | MIC In Left |
| Pin 46 | MIC In Right |
| Pin 47 | Line In Right |
| Pin 49 | Line In Left |
| Pin 51 | Audio GND |
| Pin 48 | Line Out Right |
| Pin 50 | Line Out Left |
| Pin 52 | Audio GND |

3.3.2 J2: RS485

The NuWa support 1 channel of 2-wired RS485 with 16 bytes FIFO. This RS485 is a half-duplex interface that provides combined TXD and RXD signals. RS485 supports up to 32 transmitters and receivers on a single network. The maximum cable length is 4000 ft.

| J2 | Signal |
| --- | --- |
| Pin 1 | RS485_D+ |
| Pin 2 | RS485_D- |

3.3.3 J3, J4: USB Host

| J3/J4 USB | Signal |
| --- | --- |
| Pin 1 | VCC 5V |
| Pin 2 | D- |
| Pin 3 | D+ |
| Pin 4 | GND |

3.3.4 J3, J4: Ethernet

| J3/J4 LAN | Signal |
| --- | --- |
| Pin 1 | TPT+ |
| Pin 2 | TPT- |
| Pin 3 | TPR+ |
| Pin 4 | LAN_GND |
| Pin 5 | LAN_GND |
| Pin 6 | TPR- |
| Pin 7 | LAN_GND |
| Pin 8 | LAN_GND |

3.3.5 J5: Power Connector

The NuWa main power source is 5V. It means NuWa can work just only single 5V input. The voltage input 12V is reserved for LCD back light used.

| J5 | Signal |
| --- | --- |
| Pin 1 | VCC 12V |
| Pin 2 | VCC 5V |
| Pin 3 | GND |
| Pin 4 | Frame GND |

3.3.6 J6: RS232 (COM6)

This function is provided by U57 (Ti 16C754) channel 1. The baud rate is programmable up to 230 Kbps. These signals are TTL Level.

| J6 | Signal |
| --- | --- |
| Pin 1 | TXD |
| Pin 2 | RXT |
| Pin 3 | GND |

3.3.7 J7: VGA Interface

| J7 | Signal | J7 | Signal |
| --- | --- | --- | --- |
| Pin 1 | RED | Pin 9 | VCC 5V |
| Pin 2 | GREEN | Pin 10 | GND |
| Pin 3 | BLUE | Pin 11 | N.C |
| Pin 4 | N.C | Pin 12 | N.C |
| Pin 5 | GND | Pin 13 | H. Sync |
| Pin 6 | GND | Pin 14 | V. Sync |
| Pin 7 | GND | Pin 15 | N.C |
| Pin 8 | GND |  |  |

3.3.8 J16: CPLD JTAG

The NuWa has is a complex programmable logic device (CPLD) that contain control logic for the platform. This JTAG port is used during manufacturing to program control logic to CPLD.

| J16 | Signal |
| --- | --- |
| Pin 1 | VCC 3.3V |
| Pin 2 | M4_TDO |
| Pin 3 | M4_TDI |
| Pin 4 | M4_EN |
| Pin 5 | M4_RST |
| Pin 6 | M4_TMS |
| Pin 7 | GND |
| Pin 8 | M4_TCK |

3.3.9 J17: RS232

This function is provided by U57 (Ti 16C754) channel 2 to 4. The baud rate is programmable up to 230 Kbps.

| J17 | Signal | J17 | Signal |
| --- | --- | --- | --- |
| Pin 1 | TXD_7 | Pin 2 | RXD_7 |
| Pin 3 | RTS_7 | Pin 4 | CTS_7 |
| Pin 5 | DTR_7 | Pin 6 | DSR_7 |
| Pin 7 | CD_7 | Pin 8 | RI_7 |
| Pin 9 | GND | Pin 10 | GND |
| Pin 11 | TXD_8 | Pin 12 | TXD_9 |
| Pin 13 | RXD_8 | Pin 14 | RXD_9 |
| Pin 15 | RTS_8 | Pin 16 | RTS_9 |
| Pin 17 | CTS_8 | Pin 18 | CTS_9 |

3.3.10 J23: Touch Screen

| J23 | Signal |
| --- | --- |
| Pin 1 | IY+ |
| Pin 2 | IX- |
| Pin 3 | IY- |
| Pin 4 | IX+ |
| Pin 5 | GND |

3.3.11 J25: Expansion I/O Bus Connector

| J25 | Signal | J25 | Signal | J25 | Signal |
| --- | --- | --- | --- | --- | --- |
| Pin 1A | GND | Pin 1B | GND | Pin 1C | GND |
| Pin 2A | VCC 5V | Pin 2B | VCC 5V | Pin 2C | VCC 5V |
| Pin 3A | RST- | Pin 3B | N.C | Pin 3C | READY |
| Pin 4A | RTS+ | Pin 4B | N.C | Pin 4C | N.C |
| Pin 5A | N.C | Pin 5B | SPI_CS | Pin 5C | INTR |
| Pin 6A | BP_INS | Pin 6B | SPI_CK | Pin 6C | BP_WE |
| Pin 7A | BP_TXD | Pin 7B | SPI_DI | Pin 7C | BP_OE |
| Pin 8A | BP_RTD | Pin 8B | SPI_DO | Pin 8C | BP_CS |
| Pin 9A | BP_A8 | Pin 9B | SCL | Pin 9C | BP_D7 |
| Pin 10A | BP_A7 | Pin 10B | SDA | Pin 10C | BP_D6 |
| Pin 11A | BP_A6 | Pin 11B | TMR | Pin 11C | BP_D5 |
| Pin 12A | BP_A5 | Pin 12B | INITS5 | Pin 12C | BP_D4 |
| Pin 13A | BP_A4 | Pin 13B | INITS4 | Pin 13C | BP_D3 |
| Pin 14A | BP_A3 | Pin 14B | INITS3 | Pin 14C | BP_D2 |
| Pin 15A | BP_A2 | Pin 15B | INITS2 | Pin 15C | BP_D1 |
| Pin 16A | BP_A1 | Pin 16A | INITS1 | Pin 16C | BP_D0 |

3.3.12 J27: Compact Flash Socket

| J27 | Signal | J27 | Signal |
| --- | --- | --- | --- |
| Pin 1 | GND | Pin 26 | Card Detect 1 |
| Pin 2 | Data 3 | Pin 27 | Data 11 |
| Pin 3 | Data 4 | Pin 28 | Data 12 |
| Pin 4 | Data 5 | Pin 29 | Data 13 |
| Pin 5 | Data 6 | Pin 30 | Data 14 |
| Pin 6 | Data 7 | Pin 31 | Data 15 |
| Pin 7 | CE1- | Pin 32 | CE2- |
| Pin 8 | Address 10 | Pin 33 | VS1- |
| Pin 9 | OE- | Pin 34 | IOR- |
| Pin 10 | Address 9 | Pin 35 | IOW- |
| Pin 11 | Address 8 | Pin 36 | WE- |
| Pin 12 | Address 7 | Pin 37 | INTR |
| Pin 13 | CF VCC 3.3V | Pin 38 | CF VCC 3.3V |
| Pin 14 | Address 6 | Pin 39 | N.C |
| Pin 15 | Address 5 | Pin 40 | VS2- |
| Pin 16 | Address 4 | Pin 41 | Reset |
| Pin 17 | Address 3 | Pin 42 | WAIT- |
| Pin 18 | Address 2 | Pin 43 | N.C |
| Pin 19 | Address 1 | Pin 44 | REG- |
| Pin 20 | Address 0 | Pin 45 | BVD2- |
| Pin 21 | Data 0 | Pin 46 | BVD1- |
| Pin 22 | Data 1 | Pin 47 | Data 8 |
| Pin 23 | Data 2 | Pin 48 | Data 9 |
| Pin 24 | IOCS16 | Pin 49 | Data 10 |
| Pin 25 | Card Detect 2 | Pin 50 | GND |

3.3.13 J31: PCMCIA Socket

| J31 | Signal | J31 | Signal |
| --- | --- | --- | --- |
| Pin 1 | GND | Pin 35 | GND |
| Pin 2 | Data 3 | Pin 36 | Card Detect 1 |
| Pin 3 | Data 4 | Pin 37 | Data 11 |
| Pin 4 | Data 5 | Pin 38 | Data 12 |
| Pin 5 | Data 6 | Pin 39 | Data 13 |
| Pin 6 | Data 7 | Pin 40 | Data 14 |
| Pin 7 | CE1- | Pin 41 | Data 15 |
| Pin 8 | Address 10 | Pin 42 | CE2- |
| Pin 9 | OE- | Pin 43 | N.C |
| Pin 10 | Address 11 | Pin 44 | IOR- |
| Pin 11 | Address 9 | Pin 45 | IOW- |
| Pin 12 | Address 8 | Pin 46 | Address 17 |
| Pin 13 | Address 13 | Pin 47 | Address 18 |
| Pin 14 | Address 14 | Pin 48 | Address 19 |
| Pin 15 | WE- | Pin 49 | Address 20 |
| Pin 16 | INTR | Pin 50 | Address 21 |
| Pin 17 | VCC 3.3V | Pin 51 | VCC 3.3V |
| Pin 18 | VCC 3.3V | Pin 52 | VCC 3.3V |
| Pin 19 | Address 16 | Pin 53 | Address 22 |
| Pin 20 | Address 15 | Pin 54 | Address 23 |
| Pin 21 | Address 12 | Pin 55 | Address 24 |
| Pin 22 | Address 7 | Pin 56 | Address 25 |
| Pin 23 | Address 6 | Pin 57 | N.C |
| Pin 24 | Address 5 | Pin 58 | Reset |
| Pin 25 | Address 4 | Pin 59 | WAIT- |
| Pin 26 | Address 3 | Pin 60 | N.C |
| Pin 27 | Address 2 | Pin 61 | REG- |
| Pin 28 | Address 1 | Pin 62 | BVD1- |
| Pin 29 | Address 0 | Pin 63 | BVD2- |
| Pin 30 | Data 0 | Pin 64 | Data 8 |
| Pin 31 | Data 1 | Pin 65 | Data 9 |
| Pin 32 | Data 2 | Pin 66 | Data 10 |
| Pin 33 | IOCS16- | Pin 67 | Card Detect 2 |
| Pin 34 | GND | Pin 68 | GND |

3.3.14 J35: Controller Area Network (CAN)

| J35 | Signal |
| --- | --- |
| Pin 1 | CAN- |
| Pin 2 | CAN+ |
| Pin 3 | CAN+ |
| Pin 4 | CAN GND |
| Pin 5 | Frame GND |

3.3.15 J36: Operating Mode Selection

During boot loader running stage, it will check this jumper to determiner operating mode. This jumper is short pin 2 and 3 in normal operating mode. When user short pin 1 and 2, boot loader will ask host computer to download OS image to NuWa.

| J36 | Signal |
| --- | --- |
| Short 1-2 | Download Mode |
| Short 2-3 | Normal Mode |
| Open | Normal Mode |

  - GPIO Define

The following table summarizes the use of PXA255 GPIO pins, their direction, active level, alternate function and reset state.

PXA255 GPIO Define

| GPIO No. | Function Description | Alternate Setting | Direction Setting | Active Level | Pull H/L |
| --- | --- | --- | --- | --- | --- |
| 0 | N/A | -- | -- | -- | High |
| 1 | N/A | -- | -- | -- | High |
| 2 | Interrupt Group from CPLD | 00 | Input | High | Low |
| 3 | EEPROM IO | 00 | Bi-Direction | -- | High |
| 4 | EEPROM / DS1302 CLK | 00 | Output | -- | High |
| 5 | MMC Write Protection | 00 | Output | Low | High |
| 6 | MMC Clock | 01 | Output | -- | -- |
| 7 | 48 MHz Clock | 01 | Output | -- | -- |
| 8 | MMC CS | 01 | Output | High | -- |
| 9 | MMC Card Detect | 00 | Input | Low | High |
| 10 | EEPROM CS | 00 | Output | Low | High |
| 11 | USB Wakeup Event | 00 | Output | High | Low |
| 12 | 32 KHz Clock | 01 | Output | -- | -- |
| 13 | LCD On | 00 | Output | High | High |
| 14 | N/A | -- | -- | -- | Low |
| 15 | nCS1 for Flash | 10 | Output | Low | High |
| 16 | PWM0 | 10 | Output | -- | High |
| 17 | N/A | -- | -- | -- | High |
| 18 | RDY | 01 | Input | Low | High |
| 19 | DACK for ISP1160 | 00 | Output | Low | High |
| 20 | DREQ for ISP1160 | 01 | Input | High | -- |
| 21 | PCMAIC RDY | 00 | Input | High | High |
| 22 | Compact Flash RDY | 00 | Input | High | Low |
| 23 | SPI CLK | 00 | Output | -- | Low |
| 24 | SPI CS | 00 | Output | Low | High |
| 25 | SPI Data Out | 00 | Output | -- | High |
| 26 | SPI Data In | 00 | Input | -- | High |
| 27 | Indicator LED | 00 | Output | -- | Low |
| 28 | AC97 Bit Clock | 01 | Output | -- | High |
| 29 | AC97 SDATA In | 01 | Input | -- | -- |
| 30 | AC97 SDATA Out | 10 | Output | -- | High |
| 31 | AC97 Sync | 10 | Output | Low | High |
| 32 | N/A | -- | -- | -- | -- |
| 33 | nCS5 for I/O | 10 | Output | Low | High |
| 34 | FF_RXD | 01 | Input | -- | -- |
| 35 | FF_CTS | 01 | Input | -- | -- |
| 36 | FF_DCD | 01 | Input | -- | -- |
| 37 | FF_DSR | 01 | Input | -- | -- |
| 38 | FF_RI | 01 | Input | -- | -- |
| 39 | FF_TXD | 10 | Output | -- | -- |
| 40 | FF_DTR | 10 | Output | -- | -- |
| 41 | FF_RTS | 10 | Output | -- | -- |
| 42 | BT_RXD | 01 | Input | -- | -- |
| 43 | BT_TXD | 10 | Output | -- | -- |
| 44 | BT_CTS | 01 | Input | -- | -- |
| 45 | BT_RTS | 10 | Output | -- | -- |
| 46 | IR_RXD | 01 | Input | -- | -- |
| 47 | IX_TXD | 10 | Output | -- | -- |
| 48 | PCMCIA nPOE | 10 | Output | Low | -- |
| 49 | PCMCIA nPWE | 10 | Output | Low | -- |
| 50 | PCMCIA nPIOR | 10 | Output | Low | -- |
| 51 | PCMCIA nPIOW | 10 | Output | Low | -- |
| 52 | PCMCIA nPCE[1] | 10 | Output | Low | -- |
| 53 | PCMCIA nPCE[2] | 10 | Output | Low | -- |
| 54 | PCMCIA PSKTSEL | 10 | Output | -- | -- |
| 55 | PCMCIA nPREG | 10 | Output | Low | -- |
| 56 | PCMCIA nPWAIT | 01 | Input | Low | High |
| 57 | PCMCIA nPIOIS16 | 01 | Input | Low | High |
| 58 | LCD D0 | 10 | Output | -- | -- |
| 59 | LCD D1 | 10 | Output | -- | -- |
| 60 | LCD D2 | 10 | Output | -- | -- |
| 61 | LCD D3 | 10 | Output | -- | -- |
| 62 | LCD D4 | 10 | Output | -- | -- |
| 63 | LCD D5 | 10 | Output | -- | -- |
| 64 | LCD D6 | 10 | Output | -- | -- |
| 65 | LCD D7 | 10 | Output | -- | -- |
| 66 | LCD D8 | 10 | Output | -- | -- |
| 67 | LCD D9 | 10 | Output | -- | -- |
| 68 | LCD D10 | 10 | Output | -- | -- |
| 69 | LCD D11 | 10 | Output | -- | -- |
| 70 | LCD D12 | 10 | Output | -- | -- |
| 71 | LCD D13 | 10 | Output | -- | -- |
| 72 | LCD D14 | 10 | Output | -- | -- |
| 73 | LCD D15 | 01 | Output | -- | -- |
| 74 | LCD Frame Clock | 10 | Output | -- | -- |
| 75 | LCD Line Clock | 10 | Output | -- | -- |
| 76 | LCD Pixel Clock | 10 | Output | -- | -- |
| 77 | LCD AC Bias | 10 | Output | High | -- |
| 78 | nCS2 | 10 | Output | Low | High |
| 79 | nCS3 | 10 | Output | Low | High |
| 80 | nCS4 | 10 | Output | Low | High |
| 81 | PCMCIA Reset | 00 | Output | High | Low |
| 82 | Compact Flash Reset | 00 | Output | High | Low |
| 83 | Unique ID SDIO | 00 | Bi-Direction | -- | High |
| 84 | RTC CS | 00 | Output | Low | High |

  - Memory Mapping

| Address | CS# | Bus Width | Function |
| --- | --- | --- | --- |
| 0000,0000 – 01FF,FFFF | CS0 | 32-bit | Flash memory 32 Mbytes |
| 0400,0000 – 040F,FFFF | CS1 | 16-bit | Data Flash memory 8 Mbytes |
| 0800,0000 – 080F,FFFF | CS2 | 32-bit | SRAM 1 Mbytes |
| 0C00,0000 – 0C00,0100 | CS3 | 32-bit | DM9000 LAN1 |
| 0C20,0000 – 0C20,0100 | CS3 | 32-bit | DM9000 LAN2 |
| 0C40,0000 – 0DFF,FFFF | CS3 | 32-bit | CPLD |
| 1000,0000 – 101F,FFFF | CS4 | 32-bit | MQ200 |
| 1400,0000 – 1400,01FF | CS5 | 8-bit | 87K IO Slot |
| 1420,0000 – 1420,0010 | CS5 | 16-bit | ISP1160 |
| 1440,0000 – 1440,000F | CS5 | 8-bit | UART 1 RS-232 |
| 1460,0000 – 1460,000F | CS5 | 8-bit | UART 2 RS-485 |
| 1480,0000 – 1480,000F | CS5 | 8-bit | UART 3 RS-232 |
| 14A0,0000 – 14A0,000F | CS5 | 8-bit | UART 4 RS-232 |
| 14C0,0000 – 14C0,000F | CS5 | 8-bit | UART 5 RS-232 |
| 14E0,0000 – 14E0,000F | CS5 | 8-bit | UART 6 RS-232 |
| 1500,0000 – 1500,000F | CS5 | 8-bit | UART 7 RS-232 |
| 1520,0000 – 1520,000F | CS5 | 8-bit | UART 8 RS-232 |
| 1560,0000 – 1560,0000 | CS5 | 8-bit | CAN Bus controller |
| 2000,0000 – 2FFF,FFFF | Slot 0 | 8,16 bit | PCMCIA |
| 3000,0000 – 3FFF,FFFF | Slot 1 | 8,16 bit | CF card |
| 4000,0000 – 43FF,FFFF | -- | 32-bit | Peripherals Registers |
| 4400,0000 – 47FF,FFFF | -- | 32-bit | LCD Registers |
| 4800,0000 – 4BFF,FFFF | -- | 32-bit | Memory Control Registers |
| A000,0000 – A3FF,FFF | SDCS0 | 32-bit | SDRAM 64Mbytes |

  - CPLD Define

The NuWa has a complex programmable logic device (CPLD) that contains control logic for the platform. The description as below:

| Address (Hex) | Access | Function | Detail |
| --- | --- | --- | --- |
| 0C400000 | Read | INTR Group 1 Status | Bit 0: USB Host Bit 1: DOC Bit 2: CAN Bit 3: LAN1 Bit 4: LAN2 Bit 5: USB Host Suspend |
|  | Write | INTR Group 1 Setting | Bit[x] = 1= Enable INTR |
| 0C800000 | Read | INTR Group 2 Status | Bit 0: UART_1 Bit 1: UART_2 Bit 2: UART_3 Bit 3: UART_4 Bit 4: UART_5 Bit 5: UART_6 Bit 6: UART_7 Bit 7: UART_8 |
|  | Write | INTR Group 2 Setting | Bit[x] = 1= Enable INTR |
| 0CC00000 | Read | INTR Group 3 Status | Bit 0: PCMCIA over current Bit 1: CF over current Bit 2: Expansion Bus Bit 3: N/A Bit 4: PCMCIA Insert Bit 5: PCMCIA Remove Bit 6: Compact Insert Bit 7: Compact Remove |
|  | Write | INTR Group 3 Setting | Bit[x] = 1= Enable INTR |

| 0D000000 | Read | Version ID | Bit 0: Version ID Data 0 Bit 1: Version ID Data 1 Bit 2: Version ID Data 2 Bit 3: Version ID Data 3 Bit 4: User Define Data 0 Bit 5: User Define Data 1 Bit 6: User Define Data 2 Bit 7: User Define Data 3 |
| --- | --- | --- | --- |
|  | Write | User Define | User Define |

Appendix A – Accessories

A.1 Cables

NuWa provides 4 cables for user to connect I/O device. There are:

- Peripheral I/O Cable (Connected to J1)

- TTL Level RS-232 Cable (Connected to J6)

- RS-232 Cable (Connected to J17)

- CAN Bus Cable (Connected to J35)

A.1.1 Peripheral I/O Cable (Connected to J1)

| Item | Function | Pin Out Mapping | Connector Type |
| --- | --- | --- | --- |
| A | Reset | J1/1 (GND) J1/3 (RST) | Push Button |
| B | Debug Port | J1/12 → B/2 (TXD) J1/14 → B/3 (RXD) J1/16 → B/5 (GND) | Female D-SUB 9 Pins |
| C | JTAG Port | J1/11→C/2 (TCK) J1/13→C/3 (TDI) J1/15→C/4 (TMS) J1/17→C/11 (TDO) J1/18→C/14 (GND) | Female D-SUB 25 Pins |
| D | USB Client | J1/19→D/1 (VIN) J1/21→D/2 (D-) J1/23→D/3 (D+) J1/25→D/4 (GND) | USB B Type |
| E | USB Host | J1/20→E/1 (VCC) J1/22→E/2 (D-) J1/24→E/3 (D+) J1/26→E/4 (GND) | USB A Type |
| F | MIC IN | J1/43 (AGND) J1/45 (Left Channel) J1/46 (Right Channel) | Audio Jack |
| G | Line Out | J1/48 (Right Channel) J1/50 (Left Channel) J1/52 (AGND) | Audio Jack |
| H | Power LED | J1/32 (VCC) J1/34 (GND) | Red LED |

A.1.2 TTL Level RS-232 Cable (Connected to J6)

| Item | Function | Pin Out Mapping | Connector Type |
| --- | --- | --- | --- |
| A | TTL RS-232 | J6/1→A/3 (TXD) J6/2→A/2 (RXD) J6/3→A/5 (GND) | Male D-SUB 9 Pins |

A.1.3 RS-232 Cable (Connected to J17)

| Item | Function | Pin Out Mapping | Connector Type |
| --- | --- | --- | --- |
| A | Full Function RS-232 | J17/1→ A/3 (TXD) J17/2→A/2 (RXD) J17/3→A/7 (RTS) J17/4→A/6 (DSR) J17/5→A/4 (DTR) J17/6→A/8 (CTS) J17/7→A/1 (DCD) J17/8→A/9 (RI) J17/9→A/5 (GND) | Male D-SUB 9 Pins |
| B | 4 Wired RS-232 | J17/10→B/5 (GND) J17/12→B/3 (TXD) J17/14→B/2 (RXD) J17/16→B/7 (RTS) J17/18→B/8 (CTS) | Male D-SUB 9 Pins |
| C | 4 Wired RS-232 | J17/9→C/5 (GND) J17/11→C/3 (TXD) J17/13→C/2 (RXD) J17/15→C/7 (RTS) J17/17→C/8 (CTS) | Male D-SUB 9 Pins |

A.1.4 CAN Bus Cable (Connected to J35)

| Item | Function | Pin Out Mapping | Connector Type |
| --- | --- | --- | --- |
| A | CAN Bus | J35/1→A/1 (CANL) J35/2→A/2 (CANH) J35/3→A/3 (CANH with 100 Ω) J35/4→A/4 (CAN GND) J35/4→A/5 (Frame GND) | Male D-SUB 9 Pins |

A.2 Shipping CD

All NuWa related Documentations such as Technical Manual、Windows CE.NET SDK、User’s Manual、Windows CE.NET BSP and NUWA_Utility are included on shipping CD.

The contents of CD list as below:

Technical Manual\NuWa_Tech.DOC

Windows CE.NET\BSP\NUWA35E_20050309.MSI

Windows CE.NET\BSP\BSP_INSTALLATION.DOC

Windows CE.NET\NUWA UTILITY\NUWASDK.DLL

Windows CE.NET\NUWA UTILITY\NUWAUTILITY.EXE

Windows CE.NET\NUWA UTILITY\NUWAUTILITY_USERS_GUIDE.DOC

Windows CE.NET\SDK\NUWASDK.MSI

Windows CE.NET\SDK\\NUWASDK.DOC

Appendix B – Environmental characteristics

| Parameter | MIN | TYP | MAX | Units | Condition |
| --- | --- | --- | --- | --- | --- |
| Operating Temperature | 0 | 25 | 65 | ˚C |  |
| Storage Temperature | -20 | 25 | 75 | ˚C |  |
| Normal Mode Current | 1000 | 1500 | 2000 | mA | 5V |
| Suspend Mode Current | 500 | 750 | 1000 | mA | 5V |